## Slide 1: DPWiFi revA
Date: 2024-10-28
Authors:

## Slide 2: Abstract
First, answer a fundamental question: “Why DPWiFi?”
Next, DPWiFi originally proposed as a TGbn PHY in Nov ‘23, an improved RF polarization processing model incorporated in June ‘24 unearthed a serious, latent flaw in the original Dynamic Polarization Propagation Medium formulation. Remedied, an updated “DPWiFi revA” Tx-Rx mathematical model plus corresponding “DPWiFiTRXv4” MATLAB computational model functional validation and performance characterization data, analyses and conclusions are presented herein.
November 2024

## Slide 3
Excerpted from the P802.11bn PAR: …
5.2.b Scope of the project: This amendment defines modifications to both the IEEE Std 802.11 physical layer (PHY) and the IEEE Std 802.11 Medium Access Control (MAC). The amendment adds an Ultra High Reliability capability to a Wireless Local Area Network (WLAN). The Ultra High Reliability capability is defined for both an isolated Basic Service Set (BSS) and overlapping BSSs as:
• at least one mode of operation capable of increasing throughput by 25%, as measured at the MAC data service Access Point, in at least one Signal to Interference and Noise Ratio (SINR) level (Rate vs Range), compared to the Extremely High Throughput MAC/PHY operation, and
• at least one mode of operation capable of reducing latency by 25% for the 95th percentile of the latency distribution compared to the Extremely High Throughput MAC/PHY operation, and
…
November 2024
Q: Why DPWiFi? A: PAR Compliance!

## Slide 4
November 2024
DPWiFi vs EHT Throughput/ Latency
STA1
STA2
SMX-4 MCS13 320MHz
4 Spatial Streams T = 13.6uS R = 2.88 Gbps
Throughput = 4R
Latency (to P33) = 8T
PMX-32 MCS13 320MHz
32 Spatial Streams
T = 13.6uS R = 2.88 Gbps
EHT
DPWiFi
Throughput = 32R = 800% EHT
Latency (to P33) = T = 12.5% EHT
    DPWiFi Increases Throughput 800% and Decreases Latency by 87.5% over EHT

## Slide 5
Legacy WiFi (Static) Polarization Processing
Static Polarization Impact, WiFi Stream S(t) traversing a Propagation Medium ψ: PTRX (S,ψ) = cosψ S(t)
A WiFi Tx antenna “polarizes” by launching RF waveforms S in a precise spatial orientation IAW an “Orthogonal Polarization Baseline (OPB)”
Linearly Polarized PTX radiates along a fixed angle between 0o (H) or 90o (V)
PTX(S) = H or V, per the OPB
Normal terrestrial propagation may further polarize S, rotating PTX by a “polarization angle” ψ
  LP waveforms propagate fixed-rotated by ψo from PTX(S)
  PTX (S, ψ) = ψ or ψ + 90o
A WiFi Rx antenna “depolarizes” a detected ψ-polarized waveform into its OPB-aligned V-H component
PRX (S, ψ) = PTX(S) = H or V
PTRX (S,ψ) = cosψ S(t)
Propagation Medium Polarization

## Slide 6
Proposed DPWiFi Dynamic Polarization Operation
Dynamic Polarization Impact, WiFi Stream S(t) traversing a Propagation Medium ψ : DPTRX (S,ψ) = cosψ if TxDPC = RxDPC, else f(cosψ, sinψ)
November 2024
The Propagation Medium further rotates DPTX(S) by ψ
DPTX (S, ψ) = TxDPC(ψ)
A DPWiFi Rx Antenna depolarizes DPTX into its OPB-aligned component
DPRX(S) = RxDPC
DPTRX(S, ψ) = TxDPC(ψ) · RxDPC S(t) = cosψ if TxDPC=RxDPC, else = f(cosψ, sinψ)
A DPWiFi Tx Antenna modulates RF Stream Polarization by switching its orthogonal elements H, V in accordance with a binary sequence DPC
DPTX(S) = TxDPC
Propagation Medium Polarization

## Slide 7
DPWiFi revA
  Given n WiFi-7 RF stream n-vectors [S], [S*] and [S’], and
  The ψ-polarized Propagation Medium nxn matrix [HDP], and
  Walsh n-vectors [TxDPC] and [RxDPC] such that
[TxDPC] = [DPC1 DPC2 … DPCn] = [RxDPC], where
DPCi · DPCj = cosψ if i = j
DPCi · DPCj = (cosψ + sinψ)/2 if i ≠ j
    If [HDP] is Non-Singular there exists an [HDP-1]such that [S’] = [S] x [HDP] x [HDP-1] = [S]

## Slide 8
DPWiFi revA Propagation Medium [HDP]
  Walsh-modulated DPWiFi Polarization establishes that
  S*(t) = cosψ S(t) if Tx DPC = Rx DPC, or S*(t) = (cosψ + sinψ)/2 S(t) if Tx DPC ≠ Rx DPC
  Extending to the case of n Si and corresponding DPCi we obtain [S*] = [S] x [HDP], where
  Noting that for 0o < ψ < 45o
  0.50 ≤ (cosψ + sinψ)/2 ≤ 0.71 and 0.70 ≤ cosψ ≤ 1.00, we can therefore conclude
    The DPWiFi revA Propagation Medium/ MIMO Multiplexer [HDP] is Indeed Non-Singular

## Slide 9
DPWiFi revA Rx MIMO Demultiplexer [HDP-1]
Then:
Equivalently:
Given:
Then:
Equivalently:
    The DPWiFi revA MIMO Demultiplexer [HDP-1] is a Trivial Construct

## Slide 10
DPWiFi rev- vs DPWiFi revA
    DPWiFi rev- is just a Degenerate Manifestation of DPWiFi revA
    Note: DPWiFi rev- and DPWiFi revA are equivalent for ψ < 7.5o

## Slide 11
DPWiFi Mathematical Model

## Slide 12
DPWiFi Computational (MATLAB) Model

## Slide 13
DPWiFi MATLAB Validation Plan
DPWiFiTRXv4 32x 4kQAM5/6-320MHz DPWiFi Streams BER vs Propagation Polarization, Rx Adaptation |  | 
Case | Polarization Angle ψ (o) | Rx Adaptation
VP-1 | 0.0 | N
- |  | Y
VP-2 | 1.0 | N
- |  | Y
VP-3 | 1.1 | N
VP-4 |  | Y
VP-5 | 5.0 | N
VP-6 |  | Y
VP-7 | 10.0 | N
VP-8 |  | Y
VP-9 | 25.0 | N
VP-10 |  | Y
VP-11 | 40.0 | N
VP-12 |  | Y

## Slide 14
DPWiFi revA MATLAB Validation
BER = 0.0%
BER = 0.0%

## Slide 15
DPWiFi revA MATLAB Validation
BER = 0.3%
BER = 0.0%

## Slide 16
DPWiFi revA MATLAB Validation
BER = 19.6%
BER = 0.0%

## Slide 17
DPWiFi revA MATLAB Validation
BER = 27.5%
BER = 0.0%

## Slide 18
DPWiFi revA MATLAB Validation
BER = 38.4%
BER = 0.0%

## Slide 19
DPWiFi revA MATLAB Validation
BER = 45.0%
BER = 0.0%

## Slide 20
DPWiFi revA MATLAB Validation Results
Observations
Assessments
  DPWiFi indeed transports 92 Gbps within a 320 MHz channel
  DPWiFi is extraordinarily sensitive to propagation medium impairments Absent receiver adaptation, even a slight morning mist would irremediably crash a DPWiFi link
  Rx Adaptation, however, comprehensively mitigates any amount of Propagation Polarization
Conclusions DPWiFi revA (henceforth simply “DPWiFi”) will be the fastest (Rate), farthest (Range) and toughest (Impairment-impervious) WLAN PHY ever devised
DPWiFi revA BER Performance Subject to Impaired Propagation DPWiFi-32 MCS13 320 MHz vs Propagation Polarization, Rx Adaptation |  |  |  |  |  |  | 
Propagation Impairment Polarization Angle | None 0.2o | Mist 1.0o | Fog 1.1o | Rain 5.0o | Foliage 10.0o | Grzng Reflection 25.0o | Nr Orthgnl Reflection 40.0o
Polarization Index | 0.5016 | 0.5087 | 0.5095 | 0.5417 | 0.5792 | 0.6645 | 0.7044
BER, No Adaptation | 0.000 | 0.000 | 0.003 | 0.196 | 0.275 | 0.384 | 0.450
BER, Adaptation | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000

## Slide 21
So, What Next? Hardware Validation!
Quick-turn DPWiFi Prototype
8x 11.5 Gbps SMX-4 WiFi-7s 1x 92.2 Gbps PMX-32 DPWiFi

## Slide 22
Summary and Conclusions
TGbn PHY candidate DPWiFi comprises breakthrough MIMO Polarization Multiplexing delivering 92 Gbps P2P data transport within 320 MHz at 6 GHz, regardless of propagation medium impairments.
A MATLAB model has fully simulation-validated the above-claimed DPWiFi theoretical functionality and performance.
A WiFi-7 based prototype will attempt to correspondingly hardware-validate DPWiFi by this year’s end.
DPWiFi remains without peer as a candidate TGbn PHY and, incidentally, fully and I believe uniquely complies with the P802.11bn PAR

## Slide 23: References
1. 23/1606r1-UHRSG Dynamic Polarization Multiplexing and Beamforming WLANs Carlos A Rios (Terabit Wireless Internet), 13-Sep-2023
23/1756r3-TGbn MIMO Dynamic Polarization and Beamforming: Proposed IEEE802.11bn PHY Carlos A Rios (Terabit Wireless Internet), 16-Nov-2023
24/0041r12-TGbn DPWiFi MATLAB Validation Carlos A Rios (Terabit Wireless Internet), 02-Feb-2024
24/0440r6-TGbn DPWiFi for IEEE802.11bn WMANs Carlos A Rios (Terabit Wireless Internet), 22-Apr-2024