## Slide 1: Indication for co-exist event
Date: 2024-9-2
Authors:

## Slide 2: Introduction
11bn defines a mechanism for a non-AP STA to report unavailability at TXOP level and define or reuse/update existing mechanism for a non-AP STA to report long term (periodic) unavailability.
  [Motion #30, [1] and [66-82]]
In this contribution, we analyze co-existence events and provide solutions for aperiodic events.

## Slide 3: Different kinds of co-existence events
Periodic and predictable
  Co-ex event characters like periodicity and event duration can be signaled to the peer in advance.
  It is feasible for the peer to not transmit to it in the event duration.
For aperiodic events, available solutions:
  Informing the peer in advance.
    not always success because of stringent time to contend channel
  Querying before transmission.
    Leads to much overhead.

## Slide 4: Proposal 1 for aperiodic co-ex events
Inform the peer the statistic parameters of the events
  Such as average periodicity, average duration, largest duration, etc.
  The peer can take use of these parameters and make better transmission, such as
    Transmitting at time of a lower possibility to encounter co-ex events.
    Not downgrading MCS right after a transmission failure
    Deciding the time to retransmit
AP
STA
OpenBT, …
Co-ex Events On (parameters)
…
Close BT, ….
Co-ex Events
Off

## Slide 5: Proposal 2 for aperiodic co-ex events
Signal the peer the information of the event just happened and not informed ahead.
  Such as the start time and the duration of the event.
  To trigger a retransmission without MCS downgrade for a transmission failure caused by the coex event.
  The peer can use the information in deciding MCS adjustment.
  This scheme can work together with the proposal 1.
    After the peer is informed that there would be co-ex events, it assumes that a transmission failure are caused by co-ex event at first.
    In case no indication of happened co-ex event, it takes a transmission failure as it is caused by channel fading or collision in the air.
AP
STA
Co-ex Event happened
Co-ex Event happened
Data
Data
BA

## Slide 6: Summary
In this contribution, we discuss the aperiodic co-ex events and provide 2 solutions.
  Inform the peer the statistic parameters of the events
  Signal the peer the information of the event just happened and not informed ahead.

## Slide 7: SP 1:
Do you agree to inform the peer the following statistic parameters of aperiodic co-ex events?
  Average periodicity
  Average duration of the events
  Largest duration of the events

## Slide 8: SP 2:
Do you agree to optionally signal the peer the coex event just happened and not informed ahead with following information for aperiodic coex events?
  The starting time of the event
  The duration of the event

## Slide 9: References
[1] 11-23-1934-00-00bn-in-device-interference-mitigation-follow-up Liwen Chu
[2] 11-23-1964-01-00bn-coexistence-protocols-for-uhr Alfred Asterjadhi
[3] 11-23-2002-02-00bn-in-device-coexistence-and-interference-follow-up Laurent Cariou
[4] 11-23-2026-00-00bn-balanced-wireless-in-device Brian Hart
[5] 11-23-2078-05-00bn-coex-enhancement-for-xr-use-cases Guoqing Li
[6] 11-24-0094-00-00bn-probe-before-talk-and-unsolicited-unavailability-announcement-for-co-ex-management Qi Wang
[7] 11-24-0420-00-00bn-enabling-flexible-coexistence-operation Guogang Huang
[8] 11-24-0436-00-00bn-sp-based-in-device-coexistence Jason Guo
[9] 11-24-0494-02-00bn-in-device-coexistence-follow-up Liwen Chu