## Slide 1: Concurrent Messaging
Date: 2024-08-28
Authors:
Name | Affiliations | Address | Phone | Email
Yue Xu | Huawei | Huawei Nanjing R&D Institute, Nanjing, Jiangsu, China, 210012 |  | xuyue57@Huawei.com
Chenhe Ji |  |  |  | 
Shuaishuai Zhang |  |  |  | 
Chun Pan |  |  |  | 

## Slide 2: Introduction
Reliability and Low Latency is one of the most important and practical requirement in TGbn.
In the real industrial, enterprise, agricultural scenarios, with the increasing demand for intelligent control and precise adjustment, the number of various distributed sensors is increasing. When the sensors report abnormal information simultaneously, it raises the issue of concurrent messaging within a dense network.
In this contribution, we discuss the issue of concurrent messages and provide some considerations regarding reliability and latency.

## Slide 3: Recap: Reliability and Low Latency in TGbn
The approved TGbn PAR intends to consider, compared to EHT MAC/PHY operation, at least one mode of operation that is capable of [1] :
- Reducing latency
- Increased reliability of WLAN connectivity
Task

## Slide 4: Recap: Scenarios in TGbn
The approved TGbn PAR intends to the scenarios and the demands:
- Increased manageability and mobility support
- Increased performance in congested environments
Implementation

## Slide 5: Demands in real
The use cases of industrial scenarios [2] [3]
Sensors | Periodical-based & Event-based report of information to the control system. High-density deployment environment.
Robot/drone motion control | Remotely operating group devices
Assembly line | Combination of AGV/AMR, sensors, robot/drone motion control, and video transfer.
The use cases of agricultural scenarios: Anomaly Detection and Precise Control
Smart greenhouse
Temperatures
Humidity
CO2 concentration
Soil PH
…
Smart farming
Temperatures
Ventilation
Foodstuffs
Density
…
Smart irrigation
Temperatures
Lighting
Soil ph
insect pest
…
In these scenarios, a common feature is that sufficient sensors are required to monitor specific environment features and report specific information periodically or in event-triggered mode.
In addition, to ensure the accuracy of reported information, the feedback mechanism of multiple sensors is reasonable.
Concurrency issue

## Slide 6: Concurrent messages issue (1/3)
8
Sensor
Sensor
Sensor
Sensor
Sensor
Sensor
Exception
Example: Smart greenhouse for CO2 concentration
(Event-Triggered)
backoff
BA
Exception
Exception
8
Exception
BA
backoff
BA
Exception
BA
backoff
In existing WLANs, to obtain more accurate exception information, sensors (STAs) need to perform EDCA for multiple rounds to report sufficient data of an exception.
Performance of Latency and reliability may not be guaranteed.
The AP obtains ‘abnormal’ information through 4 sensors, which is at least 4 times of EDCA process (The four sensors need to report data in sequence.)
#1
#3
#2
#4
#1
#2
#3
#4
Difficulty

## Slide 7: Concurrent messages issue (2/3)
Both exception detection and periodic detection have several features in common:
- A specific quantity of sensors (or STAs)
- Report data of the same feature.
- The data size may be limited
- In a (short) time period.
Grouping?
AP
Reduced multiple rounds of EDCA process
Grouped by certain characteristics within the WLAN
Grouping interaction
Event-triggered and/or periodically
STA
STA
Group1
STA
STA
Group3
STA
STA
Group2

## Slide 8: Concurrent messages issue (3/3)
BA
8
PPDU
Notice
Group1
Group2
Group3
Trigger
PPDU
PPDU
PPDU
BA
backoff
backoff
All devices are equal.
- No ‘leader’, No ‘sub’
‘Notice’ information needs to be carried.
- AP should know the timing
The AP performs scheduling
Both Event-triggered and periodically.
Grouping in AP sides, and STA does not need to know other members.
UL-OFDMA

## Slide 9: Summary
With the increasing demand for intelligent control and precise regulation, based on the analysis of real industrial, enterprise, and agricultural scenarios, the issue of concurrent messages is presented together with considerations (high level) that may be helpful.

## Slide 10: SP
Do you agree that the ‘grouping’ in scenarios with concurrent messages (as described in the submission) is an issue that needs further research and discussion.
-Yes
-No
-Abstain