## Slide 1: Enhanced Long Range (ELR) PPDU Design
Date: 2024-09-xx
Authors:
Name | Affiliations | Address | Phone | Email
Lin Yang | Qualcomm |  |  | 
Henry Chou |  |  |  | 
Bin Tian |  |  |  | 
Youhan Kim |  |  |  | 
Notes: September 2012

## Slide 2: Introduction
Enhanced Long Range (ELR) PPDU was recently proposed in 802.11bn [1-3]
  To improve link budget by 6 dB
    DL and UL in 2.4GHz and UL only in 5/6 GHz bands
  Motion on introducing ELR PPDU was passed
In this presentation we will talk about our thoughts on the ELR PPDU design to reach this goal
  ELR preamble format
  ELR packet detection
  ELR mode classification
  ELR-STF and ELR-LTF
  High level thoughts on ELR signaling

## Slide 3: Legacy Compliant ELR Preamble Structure
Propose to keep legacy preamble up to U-SIG in ELR PPDU
  Unified format with other PPDUs
  ELR mode classification takes place after all other legacy 11n/ac/ax/be detections, no need to carry multiple PPDU format hypothesis
Propose to have two ELR-Mark symbols after U-SIG for ELR mode classification
  ELR-Mark symbols carry a known sequence to the receiver to facilitate detection
  Two signature symbols are needed for 6dB+ improvement
Propose to have ELR-SIG right after ELR-LTF
  ELR-SIG carries required information for receiver data demod and deferral
  To get required channel estimation quality and SNR boosting, ELR-SIG follows ELR-LTF
  ELR-SIG and ELR-Data have same tone plan and duplication method to reduce implementation complexity
L-SIG
RL-SIG
ELR-Data
L-LTF
L-STF
ELR-mark2
ELR-mark1
ELR-STF
ELR-LTF
ELR-SIG
U-SIG1
U-SIG2

## Slide 4: ELR Packet Detection – Design Philosophy
ELR packet detection should be done @ L-STF
  Otherwise AP/STA needs to wait for at least 32us till ELR-STF to get the ELR packet detection result
    During this waiting time
      There could be more cases where other STA (including AP) transmits on top of the ELR PPDU (collision)
      If AP/STA choose not to transmit but wait, even it gets channel earlier than other in-BSS STAs or OBSS STAs, this AP/STA will have significant disadvantage @ contention
Same L-STF length as legacy to keep compatible with legacy Rx processing
L-SIG
RL-SIG
ELR-Data
L-LTF
3dB
L-STF
3dB
ELR-mark2
ELR-mark1
ELR-STF
ELR-LTF
ELR-SIG
U-SIG1
U-SIG2

## Slide 5: ELR-Mark Based Mode Classification
Two symbols for ELR-Mark are needed to ensure reliable mode detection performance at ELR operating SNR
  Prefer two symbols without boosting, as too many boosting is not good
  Low PAPR on known ELR-mark symbols may be desired
Propose QBPSK modulation on both ELR-Mark symbols to reduce false alarm
  No existing PPDU transmits signal with QBPSK modulation at this location, most of them are BPSK modulated, like SIG field, LTF, …

## Slide 6: ELR and Legacy Preamble Formats
L-SIG
Data
11a
LEN%3 = 0
L-LTF
L-STF
HT-STF
HT-SIG1
HT-SIG2
Data
HT-LTF1
HT-STF
L-SIG
HT-STF
HT-SIG1
Data
L-LTF
L-STF
HT-SIG2
HT-LTFs
L-SIG
VHT-STF
VHT-SIG-A1
L-LTF
L-STF
VHT-SIG-A2
L-SIG
HE-STF
RL-SIG
HE-SIG-A1
HE-SIG-A2
Data
L-LTF
L-STF
LEN%3 = 0
LEN%3 = 1
HE-LTFs
L-SIG
HE-STF
RL-SIG
HE-SIG-A1
HE-SIG-A2
Data
L-LTF
L-STF
LEN%3 = 2
HE-LTFs
HE-SIG-Bs
L-SIG
HE-STF
RL-SIG
HE-SIG-A1
HE-SIG-A2
Data
L-LTF
L-STF
LEN%3 = 2
HE-LTFs
HE-SIG-A3
HE-SIG-A4
L-SIG
Mark1
Mark2
OOK
L-LTF
L-STF
LEN%3 = 0
-1*L-SIG
-1*L-SIG
L-SIG
EHT-SIGs
RL-SIG
U-SIG1
U-SIG2
Data
L-LTF
L-STF
LEN%3 = 0
EHT-LTFs
EHT-STF
PHY version = X1 EHT PPDU Type = Y1
11n - HT GF
11n - HT MF
11ac - VHT
11ax - HE SU/TB
11ax - HE MU
11ax - HE ER SU
11ba - WUR
11be - EHT MU
L-SIG
RL-SIG
U-SIG1
U-SIG2
Data
L-LTF
L-STF
LEN%3 = 0
EHT-LTFs
EHT-STF
PHY version = X1 EHT PPDU Type = Y2
11be - EHT TB
Data
L-SIG
RL-SIG
U-SIG1
U-SIG2
L-LTF
L-STF
LEN%3 = 0
PHY version = TBD2
Post-11be
BPSK modulated
QBPSK modulated
Variable modulation
PE
PE
PE
PE
PE
VHT-LTFs
HT-LTFs
L-SIG
RL-SIG
U-SIG1
L-LTF
L-STF
LEN%3 = 0
PHY version = TBD1
ER SU
U-SIG2
U-SIG3
U
L-SIG
RL-SIG
L-LTF 3~6dB+
L-STF 3~6dB+
ELR-Mark2
ELR-Mark1
ELR PPDU
U-SIG1
U-SIG2
PHY version = 1
ELR-SIG
ELR-LTFs
ELR-STF
Data
PE

## Slide 7: ELR-Mark Tone Plan
Prefer to have regular pilots in ELR-Mark symbols as in other frame formats
  Keep consistent format and more compatible with legacy processing
  4 regular pilots as EHT-SIG
Prefer to use legacy 48 data tones x 2 symbols to carry ELR-Mark sequences
  Note that ELR-Mark symbols maintain the same total TX power as the U-SIG symbols

## Slide 8: Carrying BSS Color in ELR-Mark Sequence
ELR capable devices is more prone to packet detection FA from OBSS STAs
  It may have enhanced packet detection sensitivity
  It takes more time to determine whether the packet is intended to it
Having BSS color info in the ELR-Mark sequence, ELR capable receiver can decide early the following to enable early drop if needed
  If the received packet is an ELR packer or not
  If this packet is from in-BSS or not
Mapping BSS color to ELR-Mark sequence
  6-bit BSS color can be mapped to 64 orthogonal sequences and transmitted over two ELR-Mark symbols
    One such example is using Hadamard sequence of order 96
  Each device having its own BSS color would know what its ELR-mark sequence is, and uses it for the sequence match in the ELR detection

## Slide 9: ELR Mode Classification Performance
Example detection metric: ( is soft output of equalizer)
Simulation setup
  3dB boosting on two L-LTF symbols in ELR PPDU
  Two (un-boosted) ELR-Mark symbols both with BPSK/QBPSK modulation on data tones
  FA signal from other PPDU formats:
    Two symbols both random BPSK
    No boosting on two L-LTF symbols
Observation
  With two Mark symbols, both FA and MD rates close to 10^-3 at target ELR operating SNR
  QBPSK modulated ELR-Mark provides better FA performance
  FA from other BSS color is comparable with FA from other PPDU formats

## Slide 10: ELR-STF
Prefer to keep ELR-STF for implementation consistency with other PPDU formats and processing time margin
ELR-STF duration and sequence are the same as that of UHR DL SU/MU PPDU
  4us using EHT-STF sequence
ELR-STF has same boosting as ELR-LTF
Note that ELR-STF is the short name of UHR-STF for ELR PPDU

## Slide 11: ELR-LTF (1)
Mainly to decide ELR-LTF duration and boosting, GI length
Data demod simulation setup
  2x4x1 DNLOS, 4x-LTF with GI = 0.8us or 3.2us
  Practical timing/frequency/channel estimation
Observations:
  One 4x-LTF with 3 dB boosting is enough
    Equivalently, two 2x ELR-LTF+3 dB boosting or four 2x ELR-LTF without boosting
    Loss is within 0.5dB to ideal channel estimation
  GI = 0.8us works well

## Slide 12: ELR-LTF (2)
ELR PPDU may need a fixed/single mode of LTF+GI
  There is no good way to indicate the LTF+GI type upfront
    ELR-SIG is after ELR-LTF
Candidate LTF+GI modes for ELR PPDU
  Option 1: 2x LTF + 0.8/1.6us GI
    Existing modes
    Comparing to 0.8us GI, 1.6us GI has more margin for timing offset error at very low SNR
  Option 2: 4x LTF + 0.8/3.2us GI
    Existing modes
    3.2us GI is overkill
  Option 3: 4x LTF + 1.6us GI
    Not an existing mode
Recommendation:
  Two 2x-LTF symbols with 1.6us GI + 3 dB boosting
Note that ELR-LTF is the short name of UHR-LTF for ELR PPDU

## Slide 13: ELR Signaling
ELR Signaling
  U-SIG design
  ELR-SIG design
L-SIG
RL-SIG
ELR-Data
L-LTF
+3dB
L-STF
+3dB
ELR-mark2
ELR-mark1
ELR-STF
+3dB
ELR-LTF
+3dB
ELR-SIG
U-SIG1
U-SIG2
Rotation pattern in ELR mode:

## Slide 14: U-SIG Design for ELR PPDU Format
For EHT/UHR but non-ELR capable devices, they rely on U-SIG content to defer or terminate decoding from ELR packet
  Relevant fields (existing): PHY version ID, UL/DL bit, BSS color, TXOP
  Relevant fields (new for ELR mode): ELR indication
    Assume ELR shares same version ID with 11bn
For a new ELR capable device, if it can detect USIG, then may perform early drop based on STA-ID and BSS color or prepare to receive ELR packet targeting to it
Propose to carry ELR indication and STA-ID in U-SIG for ELR PPDU

## Slide 15: ELR-SIG Design Consideration
ELR-SIG carries required info for receiver data demod and deferral
  E.g. MCS, LDPC/BCC coding, length, STA-ID, …..
Given the low data rate and duplication, one ELR-SIG symbol may not be enough, let us assume two symbols for ELR-SIG
Need to keep the decoding delay for ELR-SIG manageable, to meet receiver timelines
  Unlike most other WiFi PPDU formats, no symbol between ELR-SIG and ELR-Data
  More tones as ELR-SIG sent at 4x symbol
Propose separately encoded two symbols for ELR-SIG
  To buy some time for configuring the Data Rx processing
  Carry MCS, LDPC/BCC coding bits as well as length field in the symbol 1, so Rx has more time to prepare the switch in MCS and coding, and calculate LDPC parameters

## Slide 16: Summary
Proposed legacy compatible ELR PPDU format to support 6dB+ link budget improvement
  Keep legacy preamble up to U-SIG
  Two known ELR-Mark symbols with QBPSK modulation for ELR mode detection
    Also carrying BSS color info to enable early drop
  ELR packet detection @ L-STF with 3dB boosting
  3 dB boosted ELR-STF and ELR-LTF for reliable ELR data reception
  Carrying ELR indication and STA-ID in U-SIG in ELR PPDU to allow early drop at bystander devices
  Separately encoded two symbol design for ELR-SIG to buy some time to configure the Data Rx processing

## Slide 17: References
[1] 24/0873, design-targets-and-considerations-for-enhanced-long-range
[2] 24/0875, enhanced-long-range-support
[3] 24/0921, an-enhanced-long-range-ppdu

## Slide 18: SP 1
Do you agree to include the following into the 11bn SFD?
  ELR PPDU includes legacy preamble up to U-SIG

## Slide 19: SP 2
Do you agree to include the following into the 11bn SFD?
  ELR packet detection is done at L-STF, which has same length as legacy with 3dB power boosting
    L-LTF also has same length as legacy with same power boosting as L-STF

## Slide 20: SP 3
Do you agree to include the following into the 11bn SFD?
  U-SIG carries ELR indication in ELR PPDU

## Slide 21: SP 4
Do you agree to include the following into the 11bn SFD?
  U-SIG carries STA-ID in ELR PPDU

## Slide 22: SP 5
Do you agree to include the following into the 11bn SFD?
  Define two ELR-Mark symbols for ELR mode classification
    ELR-Mark symbols carry a known sequence to receiver

## Slide 23: SP 6
Do you agree to include the following into the 11bn SFD?
  No power boosting on ELR-Mark symbols

## Slide 24: SP 7
Do you agree to include the following into the 11bn SFD?
  Two ELR-Mark symbols are both QBPSK modulated on data subcarriers

## Slide 25: SP 8
Do you agree to include the following into the 11bn SFD?
  ELR-Mark symbols use the following tone plan
    4 regular pilots as EHT-SIG + 48 data tones

## Slide 26: SP 9
Do you agree to include the following into the 11bn SFD?
  ELR-Mark symbols carry BSS color info in ELR-Mark sequence

## Slide 27: SP 10
Do you agree to include the following into the 11bn SFD?
  11bn defines the following PPDU frame format for ELR
    PE TBD
L-SIG
RL-SIG
ELR-Data
L-LTF
L-STF
ELR-mark2
ELR-mark1
ELR-STF
ELR-LTF
ELR-SIG
U-SIG1
U-SIG2
Note that ELR-STF/ELR-LTF are the short names of UHR-STF/UHR-LTF for ELR PPDU

## Slide 28: SP 11
Do you agree to include the following into the 11bn SFD?
  ELR PPDU has ELR-STF duration and sequence same as that of UHR DL SU/MU PPDU
    4us using EHT-STF sequence
Note that ELR-STF is the short name of UHR-STF for ELR PPDU

## Slide 29: SP 12
Do you agree to include the following into the 11bn SFD?
  ELR PPDU has 3dB boosting applied on both ELR-STF and ELR-LTF
Note that ELR-STF/ELR-LTF are the short names of UHR-STF/UHR-LTF for ELR PPDU

## Slide 30: SP 13
Do you agree to include the following into the 11bn SFD?
  ELR PPDU defines a fixed/single mode of LTF+GI
    11bn supports 2x LTF+1.6us GI only for ELR PPDU

## Slide 31: SP 14
Do you agree to include the following into the 11bn SFD?
  11bn uses two UHR-LTF symbols for ELR PPDU

## Slide 32: SP 15
Do you agree to include the following into the 11bn SFD?
  ELR PPDU defines two symbols for ELR-SIG

## Slide 33: SP 16 (passed)
Do you agree to include the following into the 11bn SFD?
  ELR-SIG is located right after ELR-LTF in ELR PPDU
Note that ELR-LTF is the short name of UHR-LTF for ELR PPDU

## Slide 34: SP 17
Do you agree to include the following into the 11bn SFD?
  ELR PPDU defines separately encoded two symbols for ELR-SIG
    Each symbol has separate CRC and tail bits (6 bits)

## Slide 35: SP 18
Do you agree to include the following into the 11bn SFD?
  ELR-SIG has same tone plan and duplication scheme as ELR-data and BCC encoded with MCS0

## Slide 36
Appendix