## Slide 1: Coordinated BF: Figures of Merit
Date: September 1, 2024
Authors:

## Slide 2: Introduction
Coordinated BF has been discussed in multiple contributions – for example in [1-6]
A motion supporting the inclusion of Co-BF into the TGbn spec passed in the July meeting [7]
There may be various approaches for supporting Co-BF in TGbn, each accompanied by a corresponding sounding feedback scheme and transmit precoder calculation
In this contribution we lay out several important figures of merit and other considerations (pertaining to evaluation methodology) that should, in our opinion, be taken into account when developing Co-BF in TGbn

## Slide 3: Scenarios to be Evaluated
Coordinated BF is a scheme where two or more APs collaborate, such that each AP transmits data to its own STAs while nulling their transmitted signals in the direction of OBSS STAs (see exemplary figure below)
  Unlike joint Tx, here each AP transmits only to its own STAs and is not aware of the payload transmitted to the OBSS STAs
In order to make a fair comparison between various approaches, we should consider practical scenarios for Co-BF evaluation
These include:
  Two cooperating APs (at least initially, more than 2 APs – TBD)
  Single and multiple STAs per AP
  STAs receiving single or multiple streams
  STAs with more Rx antennas than allocated streams
Do we need to consider changes to the channel model?
STA1a
STA1b
STA2a
STA2b
AP1
AP2

## Slide 4: What needs to be Standardized?
Some aspects (e.g. precoder computation) are better left for implementation, but other parts need to be standardized
  Sounding protocol:
    Is joint sounding NDP (multiple cooperating APs transmitting the sounding NDP simultaneously) or sequential sounding NDP (each AP transmits the sounding NDP separately) to be supported?
    Here MAC aspects also need to be taken into consideration
  Sounding feedback:
    What type of sounding feedback do the STAs generate to support Co-BF?
    Does transmission of fewer streams imply smaller feedback (similar to MU-MIMO)?
  Communication between AP and OBSS STA
    Is a STA expected to communicate directly with an OBSS AP (w.r.t. feedback report)? Does that have an impact on Items #1 and #2 above?
In the next slides we discuss figures of merit that should be considered when evaluating different Co-BF design proposals

## Slide 5: Figures of Merit
Performance
  What is the expected (link-level) performance as well as goodput? It is best if multiple scenarios, as depicted on Slide #3, are used for evaluation
Sounding feedback size
  Excessive feedback will reduce the system gain expected from the Co-BF transmission
Feedback computation complexity
  We should keep STA’s feedback computation complexity to the minimum required
  Complexity here may refer to both matrix manipulations (e.g. SVD) as well as compression
Sounding flexibility
  Some designs may require a specific sounding protocol (e.g. joint sounding NDP) whereas others may be agnostic
  Here MAC/system aspects will have to be considered as well

## Slide 6: Figures of Merit – cont.
Precoder computation complexity
  If a specific precoder computation flow is suggested for achieving a certain performance, its complexity should be evaluated
Joint precoder (across APs) communication + computation complexity
  Do APs need to cooperate when computing the precoder – e.g. one AP computing the joint precoder for all cooperating APs? If so, then this should definitely be taken into consideration (in terms of complexity and AP-to-AP communication)
  Alternatively, is channel data shared and the same precoding algorithm is carried out in all APs, or will each AP have the freedom to carry out – independently - any precoding algorithm it wishes?
LTFs and Channel Estimation
  Does the number of LTFs depend on the specific AP’s total number of streams? Or do the APs need to cooperate – in terms of the LTFs - to allow STAs to estimate the full interference covariance?

## Slide 7: Summary
Now that Co-BF has been formally accepted as a TGbn feature, detailed design discussions are expected to begin
We presented several comparison metrics that should be used to evaluate potential designs
We also highlighted that different practical scenarios should be considered in simulation evaluations (one vs. multiple STAs per AP, single vs. multiple streams per STA, more Rx antennas than streams)

## Slide 8: References
[1] 11-23-776r1: Performance of C-BF and C-SR, Ron Porat (Broadcom)
[2] 11-23-1998r0: Zero MUI Coordinated BF, Shimi Shilo (Huawei)
[3] 11-24-11r0: Coordinated Spatial Nulling Concept, Rainer Strobel (Maxlinear)
[4] 11-24-12r0: Coordinated Spatial Nulling Simulations, Rainer Strobel (Maxlinear)
[5] 11-24-1204r0: Coordinated Beamforming for 11bn, Insik Jung (LGE)
[6] 11-24-142r1: Residual Interference in CBF, Dana Ciochina (Sony)
[7] 11-24-171r13: TGbn Motions list part 1, Alfred Asterjadhi (Qualcomm)
Notes: at least one mode of operation capable of improved support, compared to 802.11be, for applications with stringentworst-case latency and jitter requirementscompared to 802.11be // i.e., avoid “worst-case”