## Slide 1: Considerations for ELR PPDU format
Date: 2024-09-xx
Authors:
Name | Affiliation | Address | Phone | Email
Dongguk Lim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | dongguk.lim@lge.com
Eunsung Park |  |  |  | Ensung.park@lge.com
Insik Jung |  |  |  | insik0618.jung@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Sanggook Kim |  | 10680 Treena St San Diego, CA 92131 |  | sanggook.kim@lge.com
September, 2024

## Slide 2: Introduction
The ELR transmission was discussed in the previous F2F meeting to resolve the problem of TX power imbalance.
And, the following ELR PPDU format has been suggested in [1].
In this contribution, we investigated more considerations of the Legacy preamble and ELR preamble portions for configuring the ELR PPDU format.
Legacy Preamble
ELR Preamble
ELR Data

## Slide 3: Legacy preamble portion (1/4)
To coexist with legacy STA and 3rd party devices, ELR PPDU should contain the legacy preamble consisting of L-STF, L-LTF, L-SIG, and RL-SIG like conventional PPDU formats.
  Herein, the L-SIG and RL-SIG are set to equal with the L-SIG and RL-SIG in the EHT PPDU.
  Similar to HE-ER PPDU, the power boosting may be adopted in L-STF and L-LTF.
In addition, to avoid the ambiguity of ELR PPDU packet classification and ensure ELR transmission, we can consider including the U-SIG field in the ELR PPDU.
  Based on the decision of the previous F2F meeting, the PHY identifier field of the U-SIG field in the ELR PPDU is set to 1.

## Slide 4: Legacy preamble portion (2/4)
Packet classification perspective
  ELR PPDU includes two BPSK symbols after L-SIG by including the RL-SIG and U-SIG fields.
    Therefore, the STAs before 11ax that receiving ELR PPDU will recognize it as a non-HT PPDU.
  Meanwhile, 11ax or 11be STA can recognize whether it is its own version’s PPDU or not with the following when receiving the ELR PPDU.
    Through the repetition check of the L-SIG field and calculating MOD( LENGTH,3), it can be done.
      The LENGTH field of the L-SIG field is set equal to that of 11be. Thus, 11ax STA can know that the received PPDU is not HE PPDU.
      Also, 11be STA can recognize that received PPDU is the PPDU of the next version protocol by using the value of the PHY identifier field in the U-SIG field.

## Slide 5: Legacy preamble portion (3/4)
Protection perspective
  The ELR transmission may be protected by using the LENGTH field of L-SIG field but it is not reliable because only 1 parity bit is used to check whether it is correct.
  Thus, to ensure the reliable protection of the ELR transmission, we can use the TXOP field by including the U-SIG in the ELR PPDU.
  Therefore, 11be STA or 11bn STA which is not a intended STA can perform the TXOP protection for the ELR transmission.
Legacy preamble portion of the ELR PPDU
∙∙∙

## Slide 6: Legacy preamble portion (4/4)
The U-SIG field of ELR PPDU
  The U-SIG field of ELR PPDU consists of 2 OFDM symbols and includes the 5 version independent fields, i.e., PHY Version Identifier, Bandwidth, UL/DL, BSS Color, and TXOP as defined in 11be.
    Herein, the Bandwidth field is set to 20MHz in the ELR transmission.
  It may also need to include the version dependent field such as PPDU Type and Compression Mode that may be used to indicate the ELR PPDU to unintended 11bn STA.
    Considering consistency with 11be, for example, this field is set to 3.
      If ELR transmission is only considered in UL, this value is set to 2 when the UL/DL field is set to 1.
  Regarding other version-dependent fields, we need to do more study.

## Slide 7: ELR preamble portion (1/3 )
ELR preamble portion can be configured with ELR-STF, ELR-LTF, and ELR-SIG fields.
As ELR-STF, we may consider reusing of 1x/2x EHT-STF sequence for 20MHz defined in 11be.
  Herein, the ELR-STF can be configured with some modification of the short STF sequence in the time domain and for example, it can be used to identify the ELR PPDU by using the auto-correlation method.
    In terms of RX processing, the 11bn STA supporting the ELR transmission continues processing until the ELR-STF for identifying the ELR PPDU even though it has some errors in the processing of the L-preamble portion due to coverage shortage.
Similar to ELR-STF, the EHT-LTF sequence for 20MHz may be reused for the ELR-LTF.
  For the exact channel estimation and robust transmission, for example, ELR-LTF can consist of the 4x EHT-LTF sequence for 20MHz.
For the reliable transmission of ELR PPDU, the power boosting may be applied to ELR-STF and ELR-LTF as well as L-STF and L-LTF.
∙∙∙
∙∙∙

## Slide 8: ELR preamble portion (2/3)
Even though we applied more symbol repetition to the U-SIG field, it was hard to reach sufficient performance compared with a data field as shown in the Appendix.
  It means that an intended 11bn STA may not decode the U-SIG field successfully when it receives the ELR PPDU.
  So, to indicate some version-independent information of the U-SIG field and transmission information related to data fields, ELR-SIG exists in ELR PPDU following the ELR-LTF field.
  For example, the ELR-SIG may contain part of fields. Exact fields and size are open for further discussion.
    PHY Version Identifier : for forward compatibility
    BSS color : for identifying own BSS
    Bandwidth : if only 20MHz is used, it may omitted.

## Slide 9: ELR preamble portion (3/3)
    UL/DL : if ELR PPDU is only applied to UL, it may be omitted.
    MCS : if MCS0 is only applied, it may be omitted.
    Coding : indication of BCC or LDPC
  For achieving equal link margin gain with a data field at this field, this field may be transmitted by applying the same transmission method with the data field such as 52-tone RU repetition.
    The MCS0 is applied to the ELR-SIG field.
  By considering the above information and MCS of the ELR-SIG, the ELR-SIG field may consist of one OFDMA symbol.

## Slide 10: Summary
In this contribution, we looked into the configuration of ELR PPDU.
  To avoid the spoofing error of ELR PPDU and ensure transmission protection, the ELR PPDU contains the legacy preamble portion, i.e., L-STF, L-LTF, L-SIG, RL-SIG, U-SIG.
  ELR preamble portion may be consist of ELR-STF, ELR-LTF, ELT-SIG fields.
    The ELR-STF may be used for the identification of ELR PPDU.
    The ELR-SIG may contain the version-independent information of U-SIG and the information related to the transmission of data fields.

## Slide 11: Straw poll 1
Do you agree to include the following text in the 11bn SFD?
  The ELR PPDU consists of the legacy preamble portion, the ELR preamble potion, and data field.
    The details of legacy preamble portion and ELR preamble portion are TBD.

## Slide 12: Straw poll 2
Do you agree to include the following text in the 11bn SFD?
  The Legacy preamble portion included in ELR PPDU is configured with L-STF, L-LTF, L-SIG, RL-SIG, and, U-SIG.
∙∙∙

## Slide 13: Straw poll 3
Do you agree to include the following text to the 11bn SFD?
  The U-SIG field in ELR PPDU consists of 2 OFDM symbols and includes the same version independent fields defined in the U-SIG field of EHT PPDU
    The details for the version dependent fields are TBD.

## Slide 14: Straw poll 4
Do you agree to include the following text to the 11bn SFD?
  The ELR preamble portion included in ELR-PPDU is configured with ELR-STF, ELR-LTF, and, ELR-SIG.
    The configuration of each field is TBD.
∙∙∙
∙∙∙

## Slide 15: Straw poll 5
Do you agree to include the following text to the 11bn SFD?
  In the ELR transmission, the power boosting is applied on L-STF, L-LTF, ELR-STF, and ELR-LTF.
    The value of power boosting is 3.

## Slide 16: Straw poll 6
Do you agree to include the following text to the 11bn SFD?
  ELR-SIG in ELR-PPDU includes the following fields
    PHY Version Identifier
    BSS color
    MCS
    Coding
  The other fields of ELR-SIG field is TBD.

## Slide 17: Reference
[1] 11-24-0873-02-00bn-design-targets-and-considerations-for-enhanced-long-range
[2]11-24-1184-00-00bn-Considerations on ELR transmission

## Slide 18: Appendix – U-SIG performance

## Slide 19: Appendix – Packet classification
  HT-MM : LENGTH%3 == 0 + HT-SIG1 QBPSK + HT-SIG2 QBPSK
  VHT : LENGTH%3 == 0 + VHT-SIG1 BPSK + VHT-SIG2 QBPSK
  HE SU/MU : LENGTH%3 ~= 0 +RL-SIG + HE-SIGA1 BPSK + HE-SIGA2 BPSK
  HE ER SU : LENGTH%3 ~= 0 +RL-SIG + HE-SIGA1 BPSK + HE-SIGA2 QBPSK
  EHT MU PPDU : LENGTH%3 = 0 + RL-SIG + U-SIG1 BPSK+ U-SIG2 BPSK + PHY identifier field = 0