## Slide 1: A transmission scheme for UHR
Date: 2024-9-4
Authors:

## Slide 2: Introduction
11bn will provide:
  at least one mode of operation capable of reducing latency by 25% for the 95th percentile of the latency distribution compared to the Extremely High Throughput MAC/PHY operation and
  at least one mode of operation capable of reducing MAC Protocol Data Unit (MPDU) loss by 25% compared to the Extremely High Throughput MAC/PHY operation for a given scenario, especially for transitions between BSSs.
In this contribution, we discuss a transmission scheme for low latency and high reliability traffic.

## Slide 3: A Transmission Scheme for Low Latency and High Reliability Traffic
PPDU 1
PPDU 2
SIFS
The transmission scheme consists of 2 consecutive PPDUs separated by SIFS. PPDU 2 has data field that is replication of PPDU 1’s data field.
  U-SIG of PPDU 1 indicates there is PPDU 2 SIFS later.
  U-SIG of PPDU 2 indicates there is PPDU 1 SIFS earlier.
  The BA is after PPDU 2.
The transmission scheme does not have much impact to the transmit and receive processing.
BA
SIFS
t

## Slide 4: A Transmission Scheme for Low Latency and High Reliability Traffic (cont’d)
PPDU 1
PPDU 2
SIFS
If PPDU 1 is collided, the receiver has PPDU 2.
The BSS can set a threshold Lth to make PPDU 2 success transmission with higher probability.
  The PPDUs for low latency and high reliability traffic is longer than Lth and others are shorter than Lth.
If the channel is poor, the receiver can better treat the signal via soft combining data fields of PPDU 1 and PPDU 2.
BA
Colliding PPDU
SIFS
Lth
t

## Slide 5: Summary
In this contribution, we discuss a transmission scheme for low latency and high reliability traffic.
  The transmission scheme consists of 2 consecutive PPDUs separated by SIFS, in which PPDU 2 has data field that is replication of PPDU 1’s data field.
  The transmission scheme is indicated by U-SIG.
PPDU 1
PPDU 2
SIFS
BA
SIFS
t

## Slide 6: SP:
Do you agree to define a transmission scheme in UHR for low latency and high reliability traffic as following?
  The transmission scheme consists of 2 consecutive PPDUs separated by SIFS, in which PPDU 2 has data field that is replication of PPDU 1’s data field, as shown in the figure.
  The transmission scheme is indicated by U-SIG.
PPDU 1
PPDU 2
SIFS
BA
SIFS
t

## Slide 7: References
[1] https://development.standards.ieee.org/myproject-web/app#viewpar/14476/10639
[2] 11-24-0740-00-00bn-time-domain-a-ppdu-for-collision-reduction-and-priority-access Ning Gao