## Slide 1: TXOP bandwidth expansion - Follow up
Date: 2024-09-09
Authors:

## Slide 2: Introduction
TXOP bandwidth expansion [1][2] has been proposed to improve the utilization of secondary channels for 11bn
In this contribution, we provide simulation results of TXOP bandwidth expansion with varying channel loads on secondary channels

## Slide 3: Recap: Wide bandwidth channel access (baseline)
For wide bandwidth channel access, baseline provides two options when a STA encounters insufficient available bandwidth due to busy secondary channels
  Option 1 (Dynamic bandwidth operation): Initiate Tx using available subchannels
    Limitations: Underutilization of secondary channels
  Option 2 (Static bandwidth operation): Invoke the backoff procedure again (choose not to Tx)
    Limitations: Channel access delay and potential failure to obtain a TXOP

## Slide 4: Recap: TXOP BW expansion procedure [1]
A STA that intends to expand BW of its TXOP (multiple protection is applied)
  (1) Performs xIFS CCA on secondary subchannels during its TXOP
  (2) Transmits an ICF on the idle subchannels following TBD channel access procedure
    TXNAV of the STA is not extended after the channel access procedure
    The other STAs do not contend the channel during the TXOP due to non-zero NAV timer
  (3) Performs frame exchanges on the subchannels after ICR have received
(40MHz)
Tx short PPDU1
Rx resp frame
(40MHz)
Tx short PPDU2
Rx resp frame
S40 CH
BUSY
S40 CH
IDLE
3
2
1
0
AIFS
XIFS
(for CCA)
SIFS
XIFS
(for CCA)
SIFS
3
2
1
0
B
U
S
Y
I
D
L
E
SIFS
Tx
ICF
Tx
ICF
Tx
ICF
Tx
ICF
Rx
ICR
Rx
ICR
Rx
ICR
Rx
ICR
SIFS
Tx
80 MHz PPDU
(1)
(2)
(3)
(1)

## Slide 5: Channel access mechanisms under simulated
Channel bonding (Dynamic bandwidth operation)
-Initiate Tx on the contiguous BW
- 20/40/80 MHz PPDU
Dynamic puncturing (Dynamic bandwidth operation)
Initiate Tx on the available subchannels
  20/40/60(20+40 or 40+20)/80 MHz PPDU
PIFS-based BW expansion (Proposal 1)
- Initiate Tx using available subchannels
- Expand BW to the IDLE subchannels after PIFS
* IDLE subchannel is determined by PIFS CCA
EDCA-based BW expansion (Proposal 2)
-Initiate Tx using available subchannels
-Expand BW to the IDLE subchannels after new backoff
- New BO counter is generated [0, CW_min]
* IDLE subchannel is determined by PIFS CCA
3
2
1
0
IDLE
Frame exchange (40+20 MHz)
TXOP
OBSS TXOP
BUSY
IDLE
P20
S20
S40
Frame exchange (40+20 MHz)
3
2
1
0
IDLE
Frame exchange (40 MHz)
TXOP
OBSS TXOP
BUSY
IDLE
P20
S20
S40
*Simulation results of the Static BW operation are in APPENDIX

## Slide 6: Simulation Setup
BW expansion rules:
  MyBSS attempts BW expansion once when its TXOP BW is 20/40 MHz, and one or more secondary channel(s) is idle
    20/40 MHz expanded to 40/60/80 MHz
MyBSS:
  1 BSS, operating BW = 80 MHz, 1AP-1STA, DL only
  MCS 11, 8 SS (Data rate = 968 Mbps/20 MHz)
  RTS enabled, A-MPDU enabled (64 MPDUs), 1 MPDU=1500 Bytes
  MyBSS load
    LL traffic : 100 Mbps (fixed)
    Non-LL traffic : [500(Low) 1000(Medium) 1500(High)] Mbps
  Scheduling (at the beginning of a TXOP)
    Transmits non-LL traffic when it has no LL traffic in its queue
OBSS:
  Four 20 MHz OBSS and two 40 MHz OBSS
    Primary channel of each OBSS is randomly selected among Ch_2 to Ch_4
  Each OBSS has 1AP-1STA, DL only
  Data rate = 143.4 Mbps/20 MHz (MCS 7)
  RTS enabled, A-MPDU (max 64 MPDUs) enabled, 1 MPDU=1500 Bytes
  Traffic load
    Non-LL traffic : [5 10 20 30] % of maximum data rate
Common EDCA parameters: CW_min = 15, CW_max= 1023, TXOP limit = 6 ms
P20
MyBSS
(80 MHz)
OBSS 1
(40 MHz)
OBSS 3
(20 MHz)
Ch_1
Ch_2
Ch_3
Ch_4
OBSS 2
(40 MHz)
OBSS 4
(20 MHz)
OBSS 5
(20 MHz)
OBSS 6
(20 MHz)

## Slide 7: Simulation Results (Throughput) -Average of 100 trials
MyBSS load (Low)
  All channel access schemes can handle all traffic regardless of OBSS load
MyBSS load (Medium)
  Neither Channel Bonding nor Dynamic Puncturing can handle their traffic even with an OBSS load of 10%
  At OBSS loads of 20% and 30%, TPUT performance of the BW expansion schemes also decrease, but they still achieve about 7-15% higher throughput compared to Channel Bonding
MyBSS load (High)
  When OBSS load is 10%, TPUT difference between Channel Bonding and the BW expansion schemes is around 28%
    Under the same conditions, Dynamic puncturing shows 11.7% better performance than Channel Bonding
*Observation: The performance gain of the proposed schemes is highest when the OBSS load is moderate(10 %), rather than when it is very low(5 %) or very high (20/30%)
Chart: MyBSS load (Low)
| Channel bonding | Dynamic puncturing | PIFS expansion | EDCA expansion
L5 load | 599.7639 | 599.8935 | 599.928 | 599.9028
L10 load | 599.8941 | 600.1377 | 600.0041 | 599.9773
L20 load | 599.7777 | 600.1255 | 599.7516 | 599.6278
L30 load | 596.9952 | 598.1641 | 597.9243 | 597.4904
Chart: MyBSS load (Medium)
| Channel bonding | Dynamic puncturing | PIFS expansion | EDCA expansion
L5 load | 1075 | 1099 | 1098.5 | 1099
L10 load | 937.4282 | 1034.3 | 1098.6 | 1098
L20 load | 860.0716 | 894.3166 | 996.1276 | 977.3595
L30 load | 829.5223 | 848.3013 | 911.2826 | 894.3234
100 %
100 %
100 %
110.2 %
103.4 %
101.8 %
115.6 %
114.2 %
109.3%
115.6 %
112.6 %
107.3%
100 %
102.2 %
102.2 %
102.2 %
Chart: MyBSS load (High)
| Channel bonding | Dynamic puncturing | PIFS expansion | EDCA expansion
L5 load | 1162.7 | 1309.3 | 1429.3 | 1426.4
L10 load | 979.3174 | 1091.1 | 1262.8 | 1252.3
L20 load | 897.8524 | 937.3622 | 1052 | 1019.4
L30 load | 831.9918 | 847.9366 | 909.9211 | 890.0853
100 %
111.7 %
128.1 %
126.4 %
100 %
104.6 %
118.5 %
115.3 %
100 %
102 %
107.9 %
105.7%
100 %
112.6 %
122.9 %
122.7 %

## Slide 8: Simulation Results (Channel occupancy ratio) -Average of 100 trials
The BW expansion schemes access secondary channels more frequently than Channel bonding and Dynamic puncturing schemes
  It seems that throughput gain of the proposed schemes are from the increased secondary channel utilization ratio
Chart: 
| Ch_1 | Ch_2 | Ch_3 | Ch_4
Channel bonding (MyBSS) | 0.9371 | 0.2877 | 0.0018 | 0.0018
Channel bonding (All BSS) | 0.04904 | 0.63069 | 0.82403 | 0.83155
Chart: 
| Ch_1 | Ch_2 | Ch_3 | Ch_4
Dynamic puncturing (MyBSS) | 0.9363 | 0.282 | 0.059 | 0.0447
Dynamic puncturing (All BSS) | 0.04906 | 0.63553 | 0.7913 | 0.80744
Chart: 
| Ch_1 | Ch_2 | Ch_3 | Ch_4
PIFS expansion (My BSS) | 0.9003 | 0.3924 | 0.1477 | 0.14
PIFS expansion (All BSS) | 0.06338 | 0.55471 | 0.72778 | 0.73771
Chart: 
| Ch_1 | Ch_2 | Ch_3 | Ch_4
EDCA expansion (MyBSS) | 0.888 | 0.3745 | 0.1336 | 0.126
EDCA expansion (All BSS) | 0.06604 | 0.56115 | 0.73913 | 0.74923
Chart: MyBSS load (High) (OBSS load 20 %)
| Ch_1 | Ch_2 | Ch_3 | Ch_4
Channel bonding | 0.98614 | 0.91839 | 0.82583 | 0.83335
Dynamic puncturing | 0.98536 | 0.91753 | 0.8503 | 0.85214
PIFS expansion | 0.96368 | 0.94711 | 0.87548 | 0.87771
EDCA expansion | 0.95404 | 0.93565 | 0.87273 | 0.87523
MyBSS channel occupancy ratio

## Slide 9: Enabling the proposed BW expansion mechanism
TXOP BW expansion procedure can be done by using the functions already supported in the baseline with minimal spec changes
(40MHz)
Tx short PPDU1
Rx resp frame
(40MHz)
Tx short PPDU2
Rx resp frame
S40 CH
BUSY
S40 CH
IDLE
3
2
1
0
AIFS
PIFS
(for CCA)
SIFS
PIFS
(for CCA)
SIFS
3
2
1
0
B
U
S
Y
I
D
L
E
SIFS
Tx
ICF
Tx
ICF
Tx
ICF
Tx
ICF
Rx
ICR
Rx
ICR
Rx
ICR
Rx
ICR
SIFS
Tx
80 MHz PPDU
(1)
Performing PIFS CCA during the TXOP is already supported in the baseline
(3)
TXOP holder cannot transmit wider BW PPDU during its TXOP
Needs to relax PPDU BW rules in (10.23.2.8 Multiple frame exchange sequence in an EDCA TXOP)
(2)
Both the PIFS access and the invoking a new backoff procedure are already supported in the baseline

## Slide 10: Conclusions
We have proposed to define an enhanced channel access mechanism letting a STA expanding bandwidth of its obtained TXOP
Simulation results show that the proposed mechanisms achieve higher TPUT than the baseline channel access mechanisms by leveraging the available secondary channels
    PIFS-based expansion (vs. Channel bonding) : ~ 28.1 % gain
    EDCA-based expansion (vs. Channel bonding) : ~ 26.4 % gain
The proposed channel access mechanism does not require any hardware changes, and cause no OBSS issues (APPENDIX)

## Slide 11: Straw Poll 1
Do you agree to define a mechanism for expanding bandwidth of the obtained TXOP to increase secondary channel utilization in TGbn?
  NOTE: Details of the mechanism are TBD.

## Slide 12: References
[1] 11-23/2211 TXOP bandwidth expansion Sanghyun Kim (WILUS)
[2] 11-24/0850 TXOP Bandwidth Expansion Related to Secondary Channel Access Jerome Gu (Clourney Semiconductor)

## Slide 13: APPENDIX Simulation results (+ Static bandwidth operation) -Average of 100 trials
As OBSS load increases, Static BW operation can hardly perform channel access
Therefore, Static BW operation has low expected TPUT in the presence of OBSS and appears to be an unsuitable scheme for handling low latency traffic
Chart: MyBSS load (Low)
| Static BW operation | Channel bonding | Dynamic puncturing | PIFS expansion | EDCA expansion
L5 load | 599.5073 | 599.7639 | 599.8935 | 599.928 | 599.9028
L10 load | 582.4169 | 599.8941 | 600.1377 | 600.0041 | 599.9773
L20 load | 104.9816 | 599.7777 | 600.1255 | 599.7516 | 599.6278
L30 load | 21.92 | 596.9952 | 598.1641 | 597.9243 | 597.4904
Chart: MyBSS load (Low)
| Static BW operation | Channel bonding | Dynamic puncturing | PIFS expansion | EDCA expansion
OBSS load 5 % | 2441.5 | 950.4668 | 806.1509 | 825.5791 | 822.9165
OBSS load 10 % | 17993 | 1069.3 | 1177 | 1095.1 | 1089.5
OBSS load 20 % | 424280 | 1521.9 | 1584.1 | 1553 | 1561.3
OBSS load 30 % | 1027700 | 2360.6 | 2176.2 | 2217.1 | 2399
424,280
1,027,700
17,993

## Slide 14: APPENDIX Simulation Results (OBSS impact) -Average of 100 trials
No OBSS impact is observed depending on the channel access scheme used
  40 MHz OBSS
    OBSS 1 and OBSS 2
  20 MHz OBSS
    OBSS 3-6
Chart: MyBSS load (Low)
| OBSS 1 | OBSS 2 | OBSS 3 | OBSS 4 | OBSS 5 | OBSS 6
Channel bonding | 0.97005 | 0.96051 | 0.98684 | 0.98762 | 0.9921 | 0.98793
Dynamic puncturing | 0.97027 | 0.96109 | 0.98518 | 0.97384 | 0.99119 | 0.99286
PIFS expansion | 0.96215 | 0.96618 | 0.99046 | 0.98738 | 0.98742 | 0.9817
EDCA expansion | 0.96383 | 0.95857 | 0.97849 | 0.99113 | 0.99115 | 0.99204
Chart: MyBSS load (Medium)
| OBSS 1 | OBSS 2 | OBSS 3 | OBSS 4 | OBSS 5 | OBSS 6
Channel bonding | 0.95006 | 0.93989 | 0.98759 | 0.99185 | 0.99141 | 0.99712
Dynamic puncturing | 0.94504 | 0.94175 | 0.99295 | 0.98392 | 0.98956 | 0.98866
PIFS expansion | 0.9327 | 0.9367 | 0.98272 | 0.9877 | 0.98799 | 0.98846
EDCA expansion | 0.94233 | 0.93185 | 0.98498 | 0.98338 | 0.99001 | 0.98143
Chart: MyBSS load (High)
| OBSS 1 | OBSS 2 | OBSS 3 | OBSS 4 | OBSS 5 | OBSS 6
Channel bonding | 0.95624 | 0.94156 | 0.99354 | 0.98926 | 0.98742 | 0.97535
Dynamic puncturing | 0.94243 | 0.94373 | 0.98488 | 0.9844 | 0.98536 | 0.98726
PIFS expansion | 0.92972 | 0.93099 | 0.9854 | 0.98561 | 0.98016 | 0.98241
EDCA expansion | 0.92605 | 0.94038 | 0.98379 | 0.97729 | 0.98007 | 0.98508
Chart: MyBSS load (Low)
| OBSS 1 | OBSS 2 | OBSS 3 | OBSS 4 | OBSS 5 | OBSS 6
Channel bonding | 0.77083 | 0.76977 | 0.93868 | 0.9189 | 0.92966 | 0.93639
Dynamic puncturing | 0.77473 | 0.77447 | 0.93709 | 0.91919 | 0.92331 | 0.93083
PIFS expansion | 0.77305 | 0.76351 | 0.93751 | 0.92371 | 0.92483 | 0.93172
EDCA expansion | 0.77036 | 0.77288 | 0.93709 | 0.93037 | 0.91682 | 0.92676
Chart: MyBSS load (Medium)
| OBSS 1 | OBSS 2 | OBSS 3 | OBSS 4 | OBSS 5 | OBSS 6
Channel bonding | 0.6976 | 0.68203 | 0.93304 | 0.9382 | 0.92835 | 0.93807
Dynamic puncturing | 0.69445 | 0.70196 | 0.91372 | 0.9203 | 0.92974 | 0.93283
PIFS expansion | 0.68806 | 0.67483 | 0.91751 | 0.9349 | 0.92022 | 0.92218
EDCA expansion | 0.68784 | 0.68504 | 0.92407 | 0.93509 | 0.92547 | 0.90961
Chart: MyBSS load (High)
| OBSS 1 | OBSS 2 | OBSS 3 | OBSS 4 | OBSS 5 | OBSS 6
Channel bonding | 0.72632 | 0.73652 | 0.94087 | 0.93604 | 0.92362 | 0.94331
Dynamic puncturing | 0.72562 | 0.72785 | 0.94389 | 0.93528 | 0.93054 | 0.93572
PIFS expansion | 0.71662 | 0.72279 | 0.92958 | 0.92173 | 0.91211 | 0.92926
EDCA expansion | 0.71855 | 0.72546 | 0.9322 | 0.92393 | 0.91264 | 0.93132

## Slide 15: APPENDIX Simulation Results (Latency) -Average of 100 trials
No meaningful difference in LL Tx latency is observed depending on the channel access scheme used
MyBSS load (High)
OBSS load 10 %
Chart: MyBSS load (High)
| Channel bonding | Dynamic puncturing | PIFS expansion | EDCA expansion
OBSS load 5 % | 3917.1 | 3629.6 | 3333.6 | 3402.1
OBSS load 10 % | 4111.6 | 4023.6 | 4041.6 | 4060.7
OBSS load 20 % | 4308.4 | 4241.9 | 4287.6 | 4288.4
OBSS load 30 % | 4420.8 | 4525.3 | 4588.5 | 4570