## Slide 1: High-Capability Protection in DPS
Date: 2024-08-30
Authors:

## Slide 2: Introduction
Low power listen mode was proposed by [1]. References[2-6] continue to develop the low power listen mode to dynamic power save (DPS) and provide more details.
References[4, 5, 7] propose to add a new Intermediate FCS field before the padding so that the STA can use the padding time to change bandwidth.
STA/AP in DPS mode will switch from the high-capability mode to the low-capability mode at the end of the TXOP.
When capability switching involves bandwidth changing, the round-trip switch delay is relatively large [9].

## Slide 3: Motivation
The round-trip switch delay accounts for a high proportion of the time-limited TXOP.
If the data transmission has not been completed and capability switches are performed each TXOP, there will be a large unnecessary padding cost and time waste.
For some data transmission tasks, the transmission duration can be roughly estimated in advance based on the amount of data and PHY capabilities.
Slide 3
High-capability mode
ICF
Low-capability mode
Switch delay
Switch delay
Duration
Low-capability mode
padding

## Slide 4: Proposal 1: High-capability protection time
Taking STA DPS as an example.
ICF from AP can indicate time or duration information based on data volume and capabilities in high-capability mode.
STA replies ICR, which also contains time information based on ICF.
STA starts switching back on or after the indicated end time.
If the time span exceeds the TXOP, AP does not need to resend the ICF to switch the STA to high-capability mode on next TXOP, it can directly communicate with the STA in high-capability.
If AP need to increase or decrease the time, it can send ICF w/o padding but w/ time information to update the end time. STA replies ICR containing the updated time information.
High-capability mode
ICF
Low-capability mode
Switch delay
Switch delay
Duration
Low-capability mode
padding
TXOP
TXOP
TXOP

## Slide 5: Proposal 1: High-capability protection time
For AP DPS, the proposed methods are also applicable.
ICF from STA can indicate time or duration information based on data volume and capabilities in high-capability mode.
AP broadcasts ICR, which also contains time information based on ICF or Buffer Report.
AP starts switching back on or after the indicated end time.
If the time span exceeds the TXOP, the STA or other associated STAs do not need to resend the ICF to switch the AP to high-capability mode on current and next TXOP, they can directly communicate with the AP in high-capability.
If the STA or other associated STAs need to increase or decrease the time, they can send ICF w/o padding but w/ time information to update the end time. AP broadcasts ICR containing the updated time information.
High-capability mode
ICF
Switch delay
Duration
padding
TXOP
TXOP
TXOP
Switch delay
Low-capability mode
Low-capability mode

## Slide 6: Proposal 2: Other switch-back conditions
Option 1: Time without frame exchange reaches a time threshold. (The time threshold can be pre-defined or indicated during DPS capability negotiation. It can be larger than EMLSR’s timeout interval because DPS does not need to switch as sensitively as EMLSR. The larger time threshold offers robustness for DPS. Robustness is another way to protect high-capability.)
Option 2: Time without high-capability frame exchange reaches a time threshold. (Option 1 is a subset of Option 2)
DPS STA
Switch delay
STA starts switching back
Time threshold
DPS STA
Switch delay
STA starts switching back
Data
Time threshold
Data
Small amounts of buffered data left or small amounts of data generated in real time.
AP
AP
ACK
Data
ACK
ACK
Data is transmitted via low-capability frames (soft switch)
When STAs return to the low-power state at the same time, Option 2 can transmit more data in case of picture.

## Slide 7: Proposal 2: Other switch-back conditions
Option 1: Time without frame exchange reaches a time threshold. (The time threshold can be pre-defined or indicated during DPS capability negotiation. It can be larger than EMLSR’s timeout interval because DPS does not need to switch as sensitively as EMLSR. The larger time threshold offers robustness for DPS. Robustness is another way to protect high-capability.)
Option 2: Time without high-capability frame exchange reaches a time threshold. (Option 1 is a subset of Option 2)
DPS STA
STA starts switching back
Time threshold
DPS STA
STA starts switching back
Data
Time threshold
Data
Time threshold can be utilized to transfer small amounts of data via low capability.
AP
AP
ACK
Data
ACK
ACK
Data is transmitted via low-capability frames (soft switch)
When the same amount of data is transmitted, Option 2
can return to the low-power state earlier in case of picture.
Switch delay
Switch delay

## Slide 8: Summary
In this contribution, we propose high-capability protection methods in DPS to avoid frequent capability states switching and unnecessary time and padding overhead before data transmission is completed.
Due to the introduction of high-capability protection, it is possible to achieve DPS across TXOPs.
Switch-back conditions with high-capability protection can cope with various practical scenarios in DPS.

## Slide 9: References
[1] 11-22-1414-00-0uhr-low-power-listening-mode
[2] 11-23-0010-00-0uhr-considerations-for-enabling-ap-power-save
[3] 11-23-1875-01-00bn-power-save-proposal-for-non-ap-mobile-ap
[4] 11-23-2003-00-00bn-client-power-save
[5] 11-23-1965-00-00bn-dynamic-power-save-follow-up
[6] 11-24-0485-00-00bn-low-power-listening-mode-for-clients
[7] 11-23-1873-00-00bn-post-fcs-mac-padding
[8] 11-23-1942-00-00bn-inter-ppdu-low-power-listening-scheme
[9] 11-24-0844-00-00bn-padding-time-in-dynamic-power-save