## Slide 1: Charging and Discharging Intervals in Passive AMP STAs
Date: 2024-09-05
Authors:

## Slide 2: Abstract
An AMP STA that harvests ambient RF may be able to charge and store energy on a capacitor to a voltage that enables RX+TX operation of the STA before the voltage drops and the STA goes into idle mode to re-charge the capacitor. The parameters involved in maximum RX+TX operation duration, STA re-charging and initial charging are investigated.

## Slide 3: Background: Passive Tag Analog Front-End
https://ieeexplore.ieee.org/stamp/stamp.jsp?tp=&arnumber=6376990
Vdd
Signals:
POR – “Power On Reset”. Reset the logic of the tag
BS – Back Scattering enable
Srx – Detected RX signal
Stx – TX modulation signal
fosc – On-chip oscillator generated frequency
https://ieeexplore.ieee.org/stamp/stamp.jsp?tp=&arnumber=6740091

## Slide 4: Energizer to STA WPT Losses
AP
Friis simplified WPT energizing loss: WPTloss = 20log10(λ) – 20log10(4πd)
WPT Loss Factors:
Distance
Frequency
Antennas Gain
Tag orientation
Shadowing
Object Absorption
Distance | 2.4 GHz Loss | 0.9 GHz Loss | PT 2.4/0.9 GHz dBm | Pr 2.4/0.9 GHz dBm
1 m | 40 dB | 31.5 dB | 20 | -20/-11.5
2 m | 46 dB | 37.5 dB | 20 | -26/-17.5
4 m | 52 dB | 43.5 dB | 20 | -32/-23.5
5 m | 54 dB | 45.5 dB | 20 | -34/-25.5
10 m | 60 dB | 51.5 dB | 20 | -40/-31.5
Energizer
PT
Pr1
Pr2
Pr3
Accurate energizing power received Pr at each STA antenna depends on multiple parameters. Antenna gain is a trade-off.
Higher than 20 dBm PT energizer EIRP transmitted levels such as 27, 30 or 36 dBm are potentially available
Can the energizer deliver enough power to all STAs?
PT - Power transmitted
Pr - Power received
Antenna Gain trade-off:
Reduced loss vs. reduced spatial coverage.
WPT Energizing Loss @ 900 MHz is lower.

## Slide 5: STA Power Charging / Discharging Timing Profile
STA harvests energy from 0 volts to Vmin. Then the voltage is sufficient to power-on reset some digital circuits, bias a reference voltage for level measurements and control impedance matching to optimize harvesting and charging.
Once the STA Vdd approaches VH it turns to “RX standby mode” and waits for a command.
Absorbing in-band PPDU signal energy, the STA turns on “RX mode” and may be able to follow up with “TX mode” afterwards with sufficient stored energy.
Once the stored voltage Vdd drops below VL the STA turns into “idle” mode.
Voltage measured on chip
Vdd

## Slide 6: Storage Capacitor Discharging Interval During RX&TX
Power
VH
VL
Re-Charge
Power
Voltage
Time
Vdd
Energy stored on a capacitor:
Example: C=10 nF, VH=1.1v, VL=0.9v,
PD – STA dissipated power averaged over RX & TX duration=10uW
Energy discharged from 1.1v to 0.9v: EDisch =0.5 10^-8 (1.21-0.81) = 2 10^-9 Joule (W Sec)
Discharge interval: T = EDisch /PD = 2 10^-4 Sec = 200 uSec.
This result is independent of the STA harvester performance, or the ambient power at the antenna
T – Maximum RX & TX duration. STA power consumption and capacitor value need to support this duration
TX
RX
“Idle”
“Standby”
VN
“Standby”
T - Discharge Interval
VH- Capacitor high voltage level
VL- Capacitor low voltage level
Maximum energy discharge from the capacitor:

## Slide 7: Storage Capacitor Re-Charge Interval Parameters
VH
VL
Re-Charge
Re-Charge
PRch
PRch
Power
Voltage
Example: C=10 nF, VH=1.1v, VL=0.9v,
PAnt- power at the antenna = -23 dBm = 5uW
DCEff =0.4 (40%), PRch – Average power consumed by STA during re-charge=1uW
PHrv =5 0.4= 2 uW, ERch =2 10^-3 uW Sec
Recharge interval: TRch = 2 10^-3/( 2-1) = 2 mSec
This result is dependent on the ambient power at the antenna and the STA performance
For “Re-Charge” we demand
and hence if is lower than -26dBm, the capacitor will not re-charge in this example
Energy accumulated during “Re-charge” interval:
Where:
- recharge interval
- antenna, harvested and re-charge dissipated power levels respectively
– RF to DC conversion efficiency
PAnt
DCEff
VN
“Standby”
“Standby”
“Idle”
“Idle”
Discharge
Discharge
Discharge
Vdd
On the other hand:

## Slide 8: Capacitor Initial Charging Interval Parameters
Time
Voltage
VH
VL
Controlled
Optimal Charging
Initial
Charging
Vmin- POR Voltage
Power
“Power-On”
Example: C=10 nF, VH=1.1v, DCEff0 =0.1 (10%), PAnt = -23 dBm = 5uW
PHrv =5 0.1= 0.5 uW
ES =5∙1.2110^-9 ≈ 610^-9 W Sec
Capacitor initial charging Interval: TStore= 12 mSec @ -23 dBm, 10nF, 1.1v and 10% efficiency
This result is dependent on the ambient power at the antenna and the STA performance
Not all harvesters are sensitive enough to charge from -23 dBm.
In fact, for charging all STAs in 10 m range, we may need harvesters that are sensitive enough @ < -32 dBm / 900 MHz
Energy charged from zero voltage:
Where:
- Capacitor charging interval from zero voltage
- Harvested power
– Average RF to DC conversion efficiency from 0 voltage to VH
PAnt
DCEff0
VN
“Standby”
Vdd

## Slide 9: Summary of Results
Maximum RX & TX Duration is dependent on the respective discharge interval and is a function of:
  Storage capacitor -
  Maximum and minimum voltage levels -VH , VL (which depend on the CMOS process and circuit design)
  Power dissipated during TX & RX - PD (depends also on process and circuit design)
Re-charging the storage capacitor during interval is a function of:
  Storage capacitor -
  Maximum and minimum voltage levels -VH , VL
  Power consumed during “Re-charge” interval -
  Power harvested - = (Conversion efficiency of the RF at the antenna to DC on the capacitor)
  is function of the power at the antenna and power consumption levels

## Slide 10: Straw Poll #1
  Do you agree that the AMP STA design shall meet a minimal harvester sensitivity of TBD energizing power at the antenna?
  Note: Sensitivity is frequency dependent
Yes
No
Abstain

## Slide 11: References
11-24-0047-00-0 AMP Station operation states; Solomon Trainin (Wiliot)
11-24-0826-00-0 Energy balance of the state-based AMP station; Solomon Trainin (Wiliot)