## Slide 1: Details on data forwarding for seamless roaming
Date: 2024-9-15
Authors:

## Slide 2: Introduction
TGbn agreed that the current AP MLD may forward DL data to the target AP MLD [1].
As we showed in a previous contribution[2], DL data forwarding is important to minimize the UL suspension duration during roaming.
In this contribution, we see some factors need to consider in DL data forwarding.

## Slide 3: Recap : Roaming procedure with single link
In single link case, STA should not transmit UL to the target AP while receiving DL from the current AP.
  STA can transmit UL to the target AP and may switch back to receive DL from the current AP. However, this may cause DL data loss if the current AP transmits DL while STA is transmitting UL.
  In dual link case, STA can transmit UL to the target AP while receiving DL from the current AP.
After the current AP completes buffered DL transmission, STA can start transmitting UL to the target AP.
This causes longer UL suspension.
  Dropping buffered DL at the current AP could reduce this, but this causes DL data loss.
Current AP
Target AP
STA
Roaming request
Context transfer
DS mapping change
may ack to Roaming request
Roaming response
Current
AP
DL
Target
AP
z
Current
AP
UL
suspension
Target
AP
Complete buffered DL transmission
Delete link
Additional
UL suspension
Add link with the target AP

## Slide 4: Recap : Roaming procedure with single link with DL data forwarding
With buffered DL data forwarding from the current AP to the target AP, STA does not need to wait for DL from the current AP and can start transmitting UL after a link with the target AP becomes enabled.
  In some cases, the current AP cannot forward all buffered data due to amount of buffered data, backhaul condition, etc. In such cases, selective DL data forwarding may be needed.
The current AP can delete link with STA immediately after completing context transfer and DS mapping change.
Current AP
Target AP
STA
Roaming request
Context transfer
DS mapping change
may ack to Roaming request
Roaming response
Buffered data forwarding
Add link with the target AP
Delete link
Current
AP
DL
Target
AP
z
Current
AP
UL
Target
AP
suspension

## Slide 5: Discussion point for data forwarding
Data forwarding availability depends on the following factors, and these factors can be static or dynamic.
Backhaul condition(delay) which depends on
  backhaul congestion(dynamic)
  network architecture(static)
    type of backhaul(wired, wireless)
    If data may send via central controller, this may have additional backhaul delay and processing delay[5].
AP MLD may have a huge amount of data in its buffer(dynamic)[3]
AP MLD Capability/implementation(static/dynamic)
  AP MLD may buffer DL data deep in the hardware.[4, 5]
Therefore, we need to check these factors and decide whether to forward and how to forward.

## Slide 6: DL data forwarding preparation phase
Before initiating roaming, APs check the data forwarding availability which depends on static factors.
APs exchange some frames to measure backhaul condition(delay).
  For example, Measurement Request/Response frame can be used.
APs exchange their capability information about network architecture, buffer implementation, etc.
  For example, these information can be included in FT Capability and Policy field of the MDE, new Link Reconfiguration element, etc.
Based on measurement results and capability information, the current AP decides whether to perform data forwarding.
Current AP
Target AP
STA
Roaming request
Backhaul measurement and capability exchange
may ack to Roaming request
Roaming response
Buffered data forwarding
Add link with the target AP
Delete link
Context transfer
DS mapping change

## Slide 7: DL data forwarding execution phase
Since the status of the buffer and backhaul congestion change dynamically, it is advisable to check the status after the STA or the current AP initiates roaming.
The current AP and the target AP measure backhaul condition at this phase by exchange of roaming request and response.
They can also add their buffer status information in roaming request and response.
Based on measurement results and buffer information obtained by roaming request and response, the current AP decides whether to forward and how to forward.
Current AP
Target AP
STA
Roaming request
may ack to Roaming request
Roaming response
Buffered data forwarding
Add link with the target AP
Delete link
Roaming request
Roaming response

## Slide 8: Target AP selection based on information related to data forwarding
These information related to availability of data forwarding can be used to select target AP.
If the STA or the current AP does not decide AP to roam, they can decide target AP based on data forwarding availability.
The current AP measures backhaul condition between other APs and exchanges their information related to network architecture, buffer implementation, etc.
Based on measurement results and obtained information, the current AP can decide candidate target AP(s) to roam for the STA.
Current AP
other APs
STA
Roaming request
Backhaul
measurement
may ack to Roaming request
Roaming response
Buffered data forwarding
Add link with the target AP
Delete link
Context transfer
DS mapping change
Target AP selection

## Slide 9: Forwarding data selection
These information can also be used to select data to forward.
For example, if the backhaul delay is low, low-latency traffic may be sent by the target AP. Conversely, if backhaul delay is high, the current AP should handle it.
If the STA lost its connection with the current AP (for example, due to sudden RSSI drop[6], current AP sleep, etc.), the STA cannot retrieve buffered DL data frames from the current AP. Therefore, the current AP needs to forward its buffered data as much as it can.
Current AP
Target AP
STA
Roaming request
may ack to Roaming request
Roaming response
Buffered data forwarding with data selection
Add link with the target AP
Delete link
Roaming request
Roaming response

## Slide 10: Summary
Data forwarding between AP MLDs is important to mitigate UL suspension duration during roaming.
We see that some factors need to be considered for data forwarding.
We propose protocols to enable APs to check the availability of data forwarding.

## Slide 11: SP1
Do you agree to define a mechanism in 11bn that enables AP MLD to check the availability of forwarding data between AP MLDs?

## Slide 12: SP2
Do you agree to define a mechanism in 11bn that enables AP MLD to collect static information related to availability of forwarding data between AP MLDs before request/response exchange that initiates notification of the DS mapping change from the current AP MLD to the target AP MLD?
  Static information includes backhaul delay, buffer implementation, network architecture, etc.

## Slide 13: SP3
Do you agree to define a mechanism in 11bn that enables AP MLD to collect dynamic information related to availability of forwarding data between AP MLDs during roaming?
  Dynamic information includes backhaul congestion, buffer status of AP MLD, etc.

## Slide 14: SP4
Do you agree to define a mechanism in 11bn that enables AP MLD to decide candidate target AP MLD(s) to roam based on availability of forwarding data between AP MLDs?

## Slide 15: References
[1] 24/0209r4, “Specification Framework for TGbn”
[2] 24/1086r0, “Data forwarding for seamless roaming ,” Ryuichi Hirata (Sony Corporation)
[3] 24/0830r1, “Improve roaming between MLDs follow up,” Po-Kai Huang (Intel)
[4] 23/2157r2, “Seamless roaming within a mobility domain,” Binita Gupta (Cisco Systems)
[5] 24/0679r1, “Thoughts on Functionality and Security Architecture for UHR Seamless Roaming,” Thomas Derham (Broadcom)
[6] 24/0398r0, “Coordinated Roaming through Target AP MLD,” Binita Gupta (Cisco Systems)