## Slide 1: Trigger based AMP communications
Date: 2024-09-08
Authors:
Name | Affiliation | Address | Phone | Email
Chuanfeng He | OPPO |  |  | hechuanfeng@oppo.com
Weijie Xu |  |  |  | 
Yinan Qi |  |  |  | 
Doc.: IEEE 802.11-24/1534r0
Sep 2024

## Slide 2: Abstract
In this contribution, we discuss trigger based communications for AMP.
Doc.: IEEE 802.11-24/1534r0

## Slide 3
Potential transmission from AMP STA
  AMP STA transmission during scanning
    Probe request for active scanning
  AMP STA transmission during authentication and association
    Authentication/Association request
  AMP STA transmission during data transaction
    Data transmission from AMP STA. For inventory case, AMP STAs transmit ID information for AP collection.
Chuanfeng He (OPPO)
Slide 3
Doc.: IEEE 802.11-24/1534r0
Sep 2024

## Slide 4
Restriction of AMP STA autonomous transmission
  AMP STA can not perform legacy channel access through either virtual carrier sense or physical carrier sense mechanism.
    AMP STA can not demodulate legacy signal, since it can only support simple modulation scheme, like OOK.
  AMP STA can not send legacy preamble or NAV setting frame.
    For compatible STA to perform channel access.
    For AMP STA to protect its TXOP
Chuanfeng He (OPPO)
Slide 4
Doc.: IEEE 802.11-24/1534r0
Sep 2024

## Slide 5
Trigger based AMP communications
  For AMP STA with backscatter, transmission is not autonomous and can only be excited by carrier wave from AP or energizer.
  For AMP STA with active transmitter, autonomous transmission is not supported. The transmission of AMP STA can only be initialized by trigger from AP.
    AP performs channel access and shares its TXOP to AMP STA.
    One trigger can initialize transmission from one or multiple AMP STAs, which can be TDMed, FDMed or CDMed.
Chuanfeng He (OPPO)
Slide 5
Doc.: IEEE 802.11-24/1534r0
Sep 2024
An example of trigger based TDM transmission from multiple AMP STA
    AMP STA1-3 wake up and monitor trigger from AP when powered on.
    Trigger schedules resources for transmission from potential AMP STAs.
    AMP STAs obtain resources, timing information, and perform data transmission using corresponding resource.

## Slide 6
Role of trigger for AMP STA transmission
  Trigger can initialize transmission from AMP STA with backscatter and active transmitter.
    Known transmission request from AMP STA
    Predicted potential transmission request from AMP STA
  Trigger can convey information for transmission from AMP STA
    TXOP sharing information
    Resource grant for AMP data transmission, e.g. time/frequency resource
    Recommended MCS
    Timing information for synchronization and duty cycle operation
    Other necessary BSS parameters, e.g. trigger interval, security related information, …
Chuanfeng He (OPPO)
Slide 6
Doc.: IEEE 802.11-24/1534r0
Sep 2024

## Slide 7
Proposal
  Transmission from AMP STA can only be initialized by trigger.
  Trigger conveys information for AMP STA transmission. The trigger at least includes following necessary information:
    TXOP sharing and resource grant
    Timing
    Trigger interval
Chuanfeng He (OPPO)
Slide 7
Doc.: IEEE 802.11-24/1534r0
Sep 2024

## Slide 8: Reference
https://development.standards.ieee.org/myproject-web/app#viewpar/11414
Doc.: IEEE 802.11-24/1534r0
Sep 2024