## Slide 1: PPDU Design for AMP
Date: 2024-09-12
Authors:
Doc.: IEEE 802.11-24/1535r2
September 2024
Name | Affiliation | Address | Phone | Email
Yinan Qi | OPPO |  |  | v-qiyinan@oppo.com
Weijie Xu |  |  |  | xuweijie@oppo.com
Wang Ke |  |  |  | 
Shengjiang Cui |  |  |  | 
Chuanfeng He |  |  |  | 
Jinyu Zhang |  |  |  | 
Zhisong Zuo |  |  |  | 

## Slide 2: Abstract
In this contribution, we discuss the PPDU design issue and propose a harmonized PPDU design approach.
Doc.: IEEE 802.11-24/1535r2

## Slide 3
Recap of PPDU Design
  Issues such as legacy preamble design, AMP asymmetric UL/DL PPDU design, and coding are discussed in [1].
  In [2], a DL PPDU structure is proposed that includes a wake/energize section, a control signaling section, and a backscattering data read section.
  References [3]-[5] present an AMP DL PPDU structure featuring a wideband preamble followed by a narrowband AMP segment.
  Key proposals:
    For DL, a wideband legacy preamble combined with a narrowband AMP segment.
    Consider including synchronization and SIG fields in the AMP segment.
    The PPDU can also include a portion dedicated to backscattering.
Yinan Qi (OPPO)
Slide 3
Doc.: IEEE 802.11-24/1535r2
September 2023

## Slide 4
PPDU Design Issue 1: DL/UL differentiation
  Q: do we need to differentiate DL/UL PPDU format?
    At least for active Tx, DL and UL formats are expected to be different
      DL: legacy preamble + AMP
      UL: AMP only
    Power saving: AMP devices do not need to process UL PPDU
Yinan Qi (OPPO)
Slide 4
Doc.: IEEE 802.11-24/1535r2
September 2023
Legacy Preamble
Narrow band AMP
DL
UL
AMP

## Slide 5
PPDU Design Issue 1: DL/UL differentiation
  Definition of DL and UL
    Clear for active transmission but unclear for backscattering
    DL: AP wakes up/triggers/polls AMP STA
    UL: AMP STA sends its own ID to AP via either active transmission or backscattering
    For backscattering
      DL: AP/energizer/assistant node sends CW to AMP STA
      UL: AMP STA backscatters incoming CW, overlapping with CW part of DL
    Harmonized UL PPDU format can be designed
Yinan Qi (OPPO)
Slide 5
Doc.: IEEE 802.11-24/1535r2
September 2023
Legacy preamble
CW
DL
UL
AMP

## Slide 6
PPDU Design Issue 2: DL PPDU
  DL PPDU components
    Legacy preamble with 20 MHz
    AMP segment with narrow bandwidth
      Sync part for DL synchronization: length 8/16
      SIG part for PPDU configuration
      Payload
Yinan Qi (OPPO)
Slide 6
Doc.: IEEE 802.11-24/1535r2
September 2023
Legacy Preamble
SYNC
SIG
Payload

## Slide 7
PPDU Design Issue 2: UL PPDU
  UL PPDU components
    UL active transmission is based on AP polling without legacy preamble.
    Only AMP segment with narrow bandwidth
      BW depends on maximum clock offset, e.g., 2.4MHz offset for 1000ppm clock offset
      SIG field is optional if AP configures UL PPDU when polling
Yinan Qi (OPPO)
Slide 7
Doc.: IEEE 802.11-24/1535r2
September 2023
SYNC
SIG
Payload
AP polls AMP STA
AMP STA UL Tx
AP reserves channel

## Slide 8
Harmonized PPDU Design
  Instead of defining multiple PPDU formats, multiple PPDU components can be defined
    P1: Legacy preamble part
    P2: Energizing symbols
    P3: AMP sync part
    P4: AMP SIG filed
    P5: AMP payload
    P6: CW for backscattering
  Every PPDU component can be optionally contained or removed and one PPDU format can be a combination of multiple components to serve one or multiple use cases
Doc.: IEEE 802.11-24/1535r2
September 2023
AMP SYNC
AMP SIG
AMP Payload
CW
Legacy preamble
Energizing symbols

## Slide 9
Harmonized PPDU Design
  More flexible and easier to specify
  Some examples
    A: P3+P4+P5 for UL active transmission
    B: P1+P3+P4+P5 for DL
    C: P1+P2+P3+P4+ P5+P6 for backscattering
Doc.: IEEE 802.11-24/1535r2
September 2023
AMP SYNC
AMP SIG
AMP Payload
AMP SYNC
AMP SIG
AMP Payload
Legacy preamble
AMP SYNC
AMP SIG
AMP Payload
CW
Legacy preamble
Energizing symbols

## Slide 10
Other Remaining Issues
  Sync sequence design: length, structure, etc.
  SIG field: length, structure and configuration information contained;
  Rate: rate higher than 11ba is desired, e.g., 1Mbps, whether to support multiple rates;
  Overall PPDU length;
  Coding: convolutional or Manchester coding.
Yinan Qi (OPPO)
Slide 10
Doc.: IEEE 802.11-24/1535r2
September 2023

## Slide 11
Summary
  In this submission, we discuss the PPDU design issues for active transmission:
    DL and UL PPDU should be differentiated for active transmission;
    DL PPDU features with wide band legacy preamble followed by narrow band AMP segment;
    UL PPDU is polled by the AP and contains only AMP segment;
    Harmonized PPDU design is proposed;
    Remaining issues including sync sequence design, SIG field, transmission rates, overall PPDU length, coding, etc..
Yinan Qi (OPPO)
Slide 11
Doc.: IEEE 802.11-24/1535r2
September 2023

## Slide 12: Reference
IEEE 802.11-24/1199r1 PHY Design for AMP
IEEE 802.11-24/1236r0 Close-Range Backscattering Waveform and Modulation
IEEE 802.11-24/0861r0 AMP DL PPDU consideration
IEEE 802.11-24/1213r1 2.4 GHz Downlink AMP PPDU Follow up
IEEE 802.11-24/1214r2 Carrier PPDU Discussion for Long-range Backscatter Operataion
Doc.: IEEE 802.11-24/1535r2
September 2023

## Slide 13
SP1
Straw Poll #1
Do you agree to add following content to sub-clause 2.1 of FRD:
  11bp defines at least one mode of MAC/PHY that allows an AMP-only device with active uplink communication in 2.4GHz subject to the following requirements:
    clock accuracy requirement is relaxed compared to legacy WiFi devices;
    the active uplink communication can only be sent in response to be being polled by the AP.
Yes
No
Abstain
Yinan Qi (OPPO)
Slide 13
Doc.: IEEE 802.11-24/1535r2
September 2023

## Slide 14
SP2
  Do you agree that 11bp defines the following PPDU components?
    preamble
    energizing symbols
    AMP synch
    AMP SIG
    AMP payload
    CW for backscattering
Yinan Qi (OPPO)
Slide 14
Doc.: IEEE 802.11-24/1535r2
September 2023