## Slide 1: UHR-LTF Design for DRU – Further Results
Date: 2024-09-06
Authors:

## Slide 2: Abstract
In this contribution, we follow up on our proposal in [1] to reuse the EHT-LTF of RRU for DRU, specifically, we share:
  The PAPR performance results of two LTF selection methods applied to different tone plans.
  The PER performance results of the two LTF selection methods considering nonlinear power amplifier (PA) and power backoff of the transmitted signal.

## Slide 3: Recap of Reusing EHT-LTF for DRU
-1, –1, +1, –1, +1, –1, +1, +1, +1, –1, +1, +1, +1, –1, –1, +1, –1, –1, –1, –1, –1, +1, +1, –1, –1, –1, –1, +1, +1, –1, +1, –1, +1, +1, +1, +1, –1, +1, –1, –1, +1, +1, –1, +1, +1, +1, +1, –1, –1, +1, –1, –1, –1, +1, +1, +1, +1, –1, +1, +1, –1, –1, –1, –1, +1, –1, –1, +1, +1, –1, +1, –1, –1, –1, –1, +1, –1, +1, –1, –1, –1, –1, –1, –1, +1, +1, –1, –1, –1, –1, –1, +1, –1, –1, +1, +1, +1, –1, +1, +1, +1, –1, +1, –1, +1, –1, –1, –1, –1, –1, +1, +1, +1, –1, –1, –1, +1, –1, +1, +1, +1, 0, 0, 0, –1, +1, –1, +1, –1, +1, +1, –1, +1, +1, +1, –1, –1, +1, –1, –1, +1, –1, +1, –1, +1, +1, +1, –1, +1, +1, +1, –1, –1, +1, –1, –1, –1, –1, –1, +1, +1, –1, –1, –1, –1, –1, –1, +1, –1, +1, –1, –1, –1, –1, +1, –1, +1, +1, –1, –1, +1, –1, –1, –1, –1, +1, +1, –1, +1, +1, +1, +1, +1, +1, +1, –1, +1, +1, –1, –1, –1, –1, +1, –1, –1, +1, +1, –1, +1, –1, –1, –1, –1, +1, –1, +1, –1, –1, +1, +1, +1, +1, –1, –1, +1, +1, +1, +1, +1, –1, +1, +1, –1, –1, –1, +1, –1, –1, –1, +1, –1, +1, –1, +1, +1
Method 2
The UHR-LTF sequence of a DRU is the EHT-LTF sequence of a corresponding RRU. Specifically, the EHT-LTF sequence of the first RRU is used as the UHR-LTF sequence for the first DRU, the EHT-LTF sequence of the second RRU is used as the UHR-LTF sequence for the second DRU and so on and so forth
Method 1
The UHR-LTF sequence of a DRU is picked from the EHT-LTF sequence corresponding to the data/pilot subcarrier indices of the DRU
Note: The set of 7 elements of the selected LTF sequence in the blue boxes is a subset of the 26-elements LTF sequence corresponding to a 26-tone DRU
Example of a 4xLTF for 26DRU20

## Slide 4: Proposed Tone Plans for DRU (1/5)
Several DRU tone plans have been proposed
In [2], the authors proposed tone plans for DBW 20/40/80 MHz
Data and pilot subcarrier indices for Distributed Tone RUs (DRUs) in a 20 MHz UHR TB PPDU [2] |  |  |  |  | 
DRU Type | DRU index and subcarrier range |  |  |  | 
26DRU20 i = 1:9 | DRU1 [-120:9:-12, 6:9:114] | DRU2 [-116:9:-8, 10:9:118] | DRU3 [-118:9:-10, 8:9:116] | DRU4 [-114:9:-6, 12:9:120] | DRU5 [-112:9:-4, 5:9:113]
 | DRU6 [-119:9:-11, 7:9:115] | DRU7 [-115:9:-7, 11:9:119] | DRU8 [-117:9:-9, 9:9:117] | DRU9 [-113:9:-5, 4:9:112] | 
52DRU20 i = 1:4 | DRU1 26DRU20 [DRU1, DRU2] |  | DRU2 26DRU20 [DRU3, DRU4] |  | 
 | DRU3 26DRU20 [DRU6, DRU7] |  | DRU4 26DRU20 [DRU8, DRU9] |  | 
106DRU20 i = 1:2 | DRU1 26DRU20 [DRU1~4], [-3, 3] |  | DRU2 26DRU20 [DRU6~9], [-2, 2] |  | 

## Slide 5: Proposed Tone Plans for DRU (2/5)
Data and pilot subcarrier indices for Distributed Tone RUs (DRUs) in a 40 MHz UHR TB PPDU [2] |  |  |  |  |  | 
DRU Type | DRU index and subcarrier range |  |  |  |  | 
26DRU40 i = 1:18 | DRU1 [-242:18:-26, 10:18:226] | DRU2 [-233:18:-17, 19:18:235] | DRU3 [-238:18:-22, 14:18:230] | DRU4 [-229:18:-13, 23:18:239] | DRU5 [-225:18:-9, 27:18:243] | DRU6 [-240:18:-24, 12:18:228]
 | DRU7 [-231:18:-15, 21:18:237] | DRU8 [-236:18:-20, 16:18:232] | DRU9 [-227:18:-11, 25:18:241] | DRU10 [-241:18:-25, 11:18:227] | DRU11 [-232:18:-16, 20:18:236] | DRU12 [-237:18:-21, 15:18:231]
 | DRU13 [-228:18:-12, 24:18:240] | DRU14 [-234:18:-18, 18:18:234] | DRU15 [-239:18:-23, 13:18:229] | DRU16 [-230:18:-14, 22:18:238] | DRU17 [-235:18:-19, 17:18:233] | DRU18 [-226:18:-10, 26:18:242]
52DRU40 i = 1:8 | DRU1 [-242:9:-17, 10:9:235] |  | DRU2 [-238:9:-13, 14:9:239] |  | DRU3 [-240:9:-15, 12:9:237] | 
 | DRU4 [-236:9:-11, 16:9:241] |  | DRU5 [-241:9:-16, 11:9:236] |  | DRU6 [-237:9:-12, 15:9:240] | 
 | DRU7 [-239:9:-14, 13:9:238] |  | DRU8 [-235:9:-10, 17:9:242] |  |  | 
106DRU40 i = 1:4 | DRU1 26DRU40 [DRU1~4], [-8,5] |  | DRU2 26DRU40 [DRU6~9], [-6,7] |  | DRU3 26DRU40 [DRU10~13], [-7,6] | 
 | DRU4 26DRU40 [DRU15~18], [-5,8] |  |  |  |  | 
242DRU40 i = 1:2 | DRU1 106DRU40 [DRU1~2], 26DRU40 DRU5, [-244,-4,3,9] |  | DRU2 106DRU40 [DRU3~4], 26DRU40 DRU14, [-243,-3,4,244] |  |  | 

## Slide 6: Proposed Tone Plans for DRU (3/5)
Data and pilot subcarrier indices for Distributed Tone RUs (DRUs) in an 80 MHz UHR TB PPDU [2] |  |  |  | 
DRU Type | DRU index and subcarrier range |  |  | 
52DRU80 i = 1:16 | DRU1 [-483:36:-51, 17:36:449], [-467:36:-35, 33:36:465] | DRU2 [-475:36:-43, 25:36:457], [-459:36:-27, 41:36:473] | DRU3 [-479:36:-47, 21:36:453], [-463:36:-31, 37:36:469] | DRU4 [-471:36:-39, 29:36:461], [-455:36:-23, 45:36:477]
 | DRU5 [-477:36:-45, 23:36:455], [-461:36:-29, 39:36:471] | DRU6 [-469:36:-37, 31:36:463], [-453:36:-21, 47:36:479] | DRU7 [-481:36:-49, 19:36:451], [-465:36:-33, 35:36:467] | DRU8 [-473:36:-41, 27:36:459], [-457:36:-25, 43:36:475]
 | DRU9 [-482:36:-50, 18:36:450], [-466:36:-34, 34:36:466] | DRU10 [-474:36:-42, 26:36:458], [-458:36:-26, 42:36:474] | DRU11 [-478:36:-46, 22:36:454], [-462:36:-30, 38:36:470] | DRU12 [-470:36:-38, 30:36:462], [-454:36:-22, 46:36:478]
 | DRU13 [-476:36:-44, 24:36:456], [-460:36:-28, 40:36:472] | DRU14 [-468:36:-36, 32:36:464], [-452:36:-20,48:36:480] | DRU15 [-480:36:-48, 20:36:452], [-464:36:-32, 36:36:468] | DRU16 [-472:36:-40, 28:36:460], [-456:36:-24, 44:36:476]
106DRU80 i = 1:8 | DRU1 52DRU80 [DRU1~2], [-495, 485] | DRU2 52DRU80 [DRU3~4],[-491, 489] | DRU3 52DRU80 [DRU5~6],[-489, 491] | DRU4 52DRU80 [DRU7~8],[-493, 487]
 | DRU5 52DRU80 [DRU9~10],[-494, 486] | DRU6 52DRU80 [DRU11~12],[-490,490] | DRU7 52DRU80 [DRU13~14],[-488,492] | DRU8 52DRU80 [DRU15~16],[-492,488]
242DRU80 i = 1:4 | DRU1 [-499:4:-19, 17:4:497] |  | DRU2 [-497:4:-17, 19:4:499] | 
 | DRU3 [-498:4:-18, 18:4:498] |  | DRU4 [-496:4:-16, 20:4:500] | 
484DRU80 i = 1:2 | DRU1 [-499:2:-17, 17:2:499] |  | DRU2 [-498:2:-16, 18:2:500] | 

## Slide 7: Proposed Tone Plans for DRU (4/5)
In [3], the authors proposed a tone plan for DBW 80 MHz
Data and pilot subcarrier indices for Distributed Tone RUs (DRUs) in an 80 MHz UHR TB PPDU [3] |  |  |  | 
DRU Type | DRU index and subcarrier range |  |  | 
52DRU80 i = 1:16 | DRU1 [-471:16:-391, -367:16:-159, -135:16:-55, 41:16:121, 145:16:353, 377:16:457] | DRU2 [-463:16:-383, -359:16:-151, -127:16:-47, 49:16:129, 153:16:361, 385:16:465] | DRU3 [-467:16:-387, -363:16:-155, -131:16:-51, 45:16:125, 149:16:357, 381:16:461] | DRU4 [-459:16:-379, -355:16:-147, -123:16:-43, 53:16:133, 157:16:365, 389:16:469]
 | DRU5 [-465:16:-385, -361:16:-153, -129:16:-49, 47:16:127, 151:16:359, 383:16:463] | DRU6 [-457:16:-377, -353:16:-145, -121:16:-41, 55:16:135, 159:16:367, 391:16:471] | DRU7 [-469:16:-389, -365:16:-157, -133:16:-53, 43:16:123, 147:16:355, 379:16:459] | DRU8 [-461:16:-381, -357:16:-149, -125:16:-45, 51:16:131, 155:16:363, 387:16:467]
 | DRU9 [-470:16:-390, -366:16:-158, -134:16:-54, 42:16:122, 146:16:354, 378:16:458] | DRU10 [-462:16:-382, -358:16:-150, -126:16:-46, 50:16:130, 154:16:362, 386:16:466] | DRU11 [-466:16:-386, -362:16:-154, -130:16:-50, 46:16:126, 150:16:358, 382:16:462] | DRU12 [-458:16:-378, -354:16:-146, -122:16:-42, 54:16:134, 158:16:366, 390:16:470]
 | DRU13 [-464:16:-384, -360:16:-152, -128:16:-48, 48:16:128, 152:16:360, 384:16:464] | DRU14 [-456:16:-376, -352:16:-144, -120:16:-40, 56:16:136, 160:16:368, 392:16:472] | DRU15 [-468:16:-388, -364:16:-156, -132:16:-52, 44:16:124, 148:16:356, 380:16:460] | DRU16 [-460:16:-380, -356:16:-148, -124:16:-44, 52:16:132, 156:16:364, 388:16:468]
106DRU80 i = 1:8 | DRU1 [-471:8:-383, -367:8:-47, 41:8:361, 377:8:465] | DRU2 [-467:8:-379, -363:8:-43, 45:8:365, 381:8:469] | DRU3 [-465:8:-377, -361:8:-41, 47:8:367, 383:8:471] | DRU4 [-469:8:-381, -365:8:-45, 43:8:363, 379:8:467]
 | DRU5 [-470:8:-382, -366:8:-46, 42:8:362, 378:8:466] | DRU6 [-466:8:-378, -362:8:-42, 46:8:366, 382:8:470] | DRU7 [-464:8:-376, -360:8:-40, 48:8:368, 384:8:472] | DRU8 [-468:8:-380, -364:8:-44, 44:8:364, 380:8:468]
242DRU80 i = 1:4 | DRU1 [-499:4:-19, 17:4:497] |  | DRU2 [-497:4:-17, 19:4:499] | 
 | DRU3 [-498:4:-18, 18:4:498] |  | DRU4 [-496:4:-16, 20:4:500] | 
484DRU80 i = 1:2 | DRU1 [-499:2:-17, 17:2:499] |  | DRU2 [-498:2:-16, 18:2:500] | 

## Slide 8: Proposed Tone Plans for DRU (5/5)
In [4], the authors proposed a tone plan for DBW 20 MHz
Data and pilot subcarrier indices for Distributed Tone RUs (DRUs) in a 20 MHz UHR TB PPDU [4] |  |  |  |  | 
DRU Type | DRU index and subcarrier range |  |  |  | 
26DRU20 i = 1:9 | DRU1 [-120:9:-12, 6:9:114] | DRU2 [-115:9:-7, 11:9:119] | DRU3 [-118:9:-10, 8:9:116] | DRU4 [-113:9:-5, 4:9:112] | DRU5 [-117:9:-9, 9:9:117]
 | DRU6 [-112:9:-4, 5:9:113] | DRU7 [-116:9:-8, 10:9:118] | DRU8 [-119:9:-11, 7:9:115] | DRU9 [-114:9:-6, 12:9:120] | 
52DRU20 i = 1:4 | DRU1 26-tone [DRU1, DRU2] |  | DRU2 26-tone [DRU3, DRU4] |  | 
 | DRU3 26-tone [DRU6, DRU7] |  | DRU4 26-tone [DRU8, DRU9] |  | 
106DRU20 i = 1:2 | DRU1 26-tone [DRU1~4], [-3, 2] |  | DRU2 26-tone [DRU6~9], [-2, 3] |  | 

## Slide 9: Nonlinearity of the PA
To account for the nonlinearity of the PA, RAPP model is applied to the transmit signal [5][6].
  a smoothing factor is used.
A power backoff of 8 dB is then applied to the transmit signal before applying the channel.

## Slide 10: Simulation Parameters
Tone Plan: The tone plans proposed in [2], [3] and [4]
Distribution bandwidth (DBW) = 20 MHz, 40 MHz, and 80 MHz
Channel Model D
MCS 9
Oversampling factor (OSF) = 8
Nonlinear PA (RAPP model with p = 3)
Power Back off (BO = 8 dB)
All DRUs for the corresponding distribution bandwidth are considered
LTF Mode: 4xLTF
Simulation length: 1000 packets
APEP length: 100 Bytes

## Slide 11: PAPR Performance of DRU (DBW = 20 MHz)
Applying method 2 shows a significant improvement to the PAPR performance for all DRU sizes in DBW = 20 MHz
  Some DRUs perform better than others achieving PAPR values similar to RRUs
Some tone plans performs better than others
  Tone plan [4] shows a better PAPR performance for 26DRU20 and 52DRU20 while for 106DRU20 tone plan [2] performs better.

## Slide 12: PAPR Performance of DRU (DBW = 40 MHz)
In DBW = 40 MHz, method 2 shows a PAPR performance for 26DRU40 and 52DRU40 that is similar to the PAPR performance of the RRU.

## Slide 13: PAPR Performance of DRU (DBW = 80 MHz)
Similar behavior for DBW = 80 MHz
  Method 2 outperforms method 1
  Tone plan [2] shows a better PAPR performance for both 52DRU80 and 106DRU80 than [3].

## Slide 14: PER Performance of DRU (DBW = 20 MHz)
The PER results confirm the same conclusions drawn from the PAPR results where method 2 outperforms method 1 for all tone plans
Some tone plans (e.g., [2]) performs better than others considering method 1, but the performance gap between the tone plans converges by applying method 2

## Slide 15: PER Performance of DRU (DBW = 40 MHz)
For DBW = 40 MHz, method 2 shows impressive improvement over method 1 and still confirms the same conclusions for the PAPR performance.
The results are only presented for the 40 MHz tone plan that is publicly available

## Slide 16: PER Performance of DRU (DBW = 80 MHz)
For DBW = 80 MHz, method 2 shows a much better PER performance than method 1.
Further, tone plan [2] outperforms tone plan [3] for this DBW considering method 2.

## Slide 17: Discussion on PAPR and PER Performance
Method 2 shows a significantly better performance than method 1 in terms of both PAPR PER
  There is a positive correlation between PAPR performance and PER performance
  Smaller PAPR values of the LTF allows for more accurate channel estimation which in turn translates into better PER performance, hence the choice of LTF sequence that improves the PAPR will improve the PER.
  Reusing the EHT-LTF sequence for both RRU and DRU may simplify the implementation as the same sequence will be stored and used for both types of RU.
  The LTF sequence of the bandwidth containing the RRU may be used for the DRUs in the corresponding DBW
    The LTF sequence of the RRU in bandwidth 20 MHz may be used for the DRUs in DBW = 20 MHz. and so on and so forth.
New LTF sequences for DRU may need to get optimized separately for different DBW.
  It is not recommended to define new LTF sequences for DRU which may complicate the implementation.

## Slide 18: Conclusions and Way Forward
More results are generated for the selection methods of the LTF sequences for DRU considering different tone plans.
Method 2 shows a significant performance improvement over method 1 for both PAPR and PER.
Tone plan [2] shows the best PAPR and PER performance for method 2 considering different DBWs and DRU sizes
We recommend to reuse the 4x EHT-LTF of RRU for DRU.

## Slide 19: SP 1
Do you agree to add the following to 11bn SFD:
The LTF type 11bn supports for DRU in TB PPDU is 4xLTF, i.e., each tone of the DRU will have a nonzero value.
- 1xLTF and 2xLTF are TBD

## Slide 20: SP 2
Do you agree to add the following to 11bn SFD:
11bn supports to reuse the EHT-LTF sequences of RRU for DRU in TB PPDU, i.e., the elements of the LTF sequence for each DRU tone is selected from the EHT-LTF sequence of the corresponding DBW
- The LTF sequence selection method is TBD

## Slide 21: References
[1] 11/24-1114r0 UHR-LTF Design for DRU
[2] 11/24-0468r2 DRU Tone Plan for 11bn, Mediatek
[3] 11/24-0799r0 DRU Tone Plan from the perspective of PAPR, Huawei
[4] 11/24-1096r0 Mirror Symmetric 20 MHz DRU Tone Plan within 242 RRU Boundary, LGE
[5] 11/09-0451r16 TGac Functional Requirements and Evaluation Methodology
[6] 11/00-0294r0 Suggested PA Model for 802.11 HRb