## Slide 1: LTF Design for DRU
Date: 2024-09-08
Authors:
Name | Affiliations | Address | Phone | email
Ron Porat | Broadcom |  |  | ron.porat@broadcom.com
Leo Montreuil | Broadcom |  |  | leo.montreuil@broadcom.com

## Slide 2: Introduction
EHT-LTF sequences are PAPR optimized for RRU tones and pilots locations
Using or remapping the RRU LTF sequences to the DRU tones locations increase the PAPR to an unacceptable high level
For the lowest PAPR, we designed DRU LTF (denoted henceforth DLTF) sequences for 20, 40 and 80 MHz based on the designs in [1] and [2] (data tones and pilot locations)
  DLTF sequences are optimized for the DRU tone plan and pilots indices
Similar to the arguments in [3] we focus on 4x LTF. We don’t see a need to also have 2x LTF as it won’t work well with DRU
We also assume DRU is limited to Nss=2 (although the LTF design can be assumed to be optimal up to Nss=4) as higher Nss may not benefit from the DRU gain.

## Slide 3: 20 MHz DRU Tone Map [1] and Pilots [2]
Size | Tone/MHz | Boost (dB)
DRU26 | 2 | 8.1
DRU52 | 3 | 6.3
DRU106 | 6 | 3.3
Pilot indices for DRU transmission over 20MHz | 
DRU size | KdRxx_i
DRU26, i = 1:9 | { -111 15 }, { -89 37 }, { -100 26 }, { -78 48 }, { -67 59 }, { -56 70 }, { -34 92 }, { -45 81 }, { -23 103 }
DRU52, i = 1:4 | { -111 -89 15 37 }, { -100 -78 26 48 }, { -56 -34 70 92 }, { -45 -23 81 103 }
DRU106, i = 1:2 | { -111 -78 15 48 }, { -56 -23 70 103 }
Data and pilot subcarrier indices for Distributed Tone RUs (DRUs) in a 20 MHz UHR PPDU |  |  |  |  | 
DRU type | DRU index and subcarrier range |  |  |  | 
26-tone DRU i=1:9 | DRU1 [-120:9:-12, 6:9:114] | DRU2 [-116:9:-8, 10:9:118] | DRU3 [-118:9:-10, 8:9:116] | DRU4 [-114:9:-6, 12:9:120] | DRU5 [-112:9:-4, 5:9:113]
 | DRU6 [-119:9:-11, 7:9:115] | DRU7 [-115:9:-7, 11:9:119] | DRU8 [-117:9:-9, 9:9:117] | DRU9 [-113:9:-5, 4:9:112] | 
52-tone DRU i=1:4 | DRU1 26-tone [DRU1, DRU2] |  | DRU2 26-tone [DRU3, DRU4] |  | 
 | DRU3 26-tone [DRU6, DRU7] |  | DRU4 26-tone [DRU8, DRU9] |  | 
106-tone DRU i=1:2 | DRU1 26-tone [DRU1~4], [-3, 3] |  | DRU2 26-tone [DRU6~9], [-2, 2] |  | 

## Slide 4: 20 MHz DRU 4xLTF
DLTF-122:122 = [ ...
0 0 -1 +1 -1 +1 -1 +1 +1 +1 -1 +1 +1 -1 +1 -1 -1 -1 -1 +1 -1 -1 +1 -1 -1 +1 +1 -1 -1 -1 -1 -1 -1 -1 +1 ...
+1 -1 +1 -1 +1 +1 -1 +1 -1 +1 -1 -1 -1 -1 -1 +1 +1 +1 -1 +1 +1 -1 -1 +1 +1 -1 +1 -1 +1 -1 +1 -1 -1 +1 -1 ...
+1 +1 +1 +1 -1 +1 +1 -1 +1 -1 -1 -1 +1 +1 -1 +1 -1 -1 +1 -1 -1 -1 -1 -1 -1 +1 -1 +1 -1 -1 +1 +1 -1 +1 +1 ...
-1 +1 +1 -1 +1 +1 -1 +1 -1 +1 -1 +1 -1 -1 +1 -1 0 0 0 -1 +1 -1 +1 -1 -1 +1 -1 -1 -1 +1 -1 +1 -1 -1 -1 ...
+1 +1 +1 -1 +1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 +1 +1 -1 +1 -1 -1 -1 -1 +1 +1 +1 +1 +1 -1 -1 +1 -1 -1 +1 ...
+1 -1 -1 -1 -1 +1 -1 +1 +1 -1 -1 +1 +1 +1 -1 -1 +1 -1 -1 -1 -1 +1 -1 +1 +1 -1 -1 +1 -1 +1 +1 -1 +1 +1 -1 ...
+1 +1 -1 +1 +1 -1 +1 -1 +1 -1 -1 +1 +1 -1 -1 -1 -1 +1 +1 +1 -1 -1 -1 -1 +1 -1 -1 -1 +1 +1 +1 -1 +1 0 0 ];
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
DRU26 | 3.12, 3.79 | 3.29, 3.56 | 3.58, 3.67 | 3.80, 3.53 | 2.96, 2.97 | 2.99, 3.47 | 2.79, 3.70 | 3.77, 3.72 | 3.30, 3.42
DRU52 | 4.74, 4.75 |  | 4.71, 4.75 |  |  | 4.72, 4.72 |  | 4.74, 4.73 | 
DRU106 | 4.59, 4.77 |  |  |  |  | 4.77, 4.68 |  |  | 
PAPR (dB) for Nss=1&2

## Slide 5: 40 MHz DRU Tone Map [1]
Data and pilot subcarrier indices for Distributed Tone RUs (DRUs) in a 40 MHz UHR TB PPDU |  |  |  |  |  | 
DRU type | DRU index and subcarrier range |  |  |  |  | 
26-tone DRU i=1:18 | DRU1 [-242:18:-26, 10:18:226] | DRU2 [-233:18:-17, 19:18:235] | DRU3 [-238:18:-22, 14:18:230] | DRU4 [-229:18:-13, 23:18:239] | DRU5 [-225:18:-9, 27:18:243] | DRU6 [-240:18:-24, 12:18:228]
 | DRU7 [-231:18:-15, 21:18:237] | DRU8 [-236:18:-20, 16:18:232] | DRU9 [-227:18:-11, 25:18:241] | DRU10 [-241:18:-25, 11:18:227] | DRU11 [-232:18:-16, 20:18:236] | DRU12 [-237:18:-21, 15:18:231]
 | DRU13 [-228:18:-12, 24:18:240] | DRU14 [-234:18:-18, 18:18:234] | DRU15 [-239:18:-23, 13:18:229] | DRU16 [-230:18:-14, 22:18:238] | DRU17 [-235:18:-19, 17:18:233] | DRU18 [-226:18:-10, 26:18:242]
52-tone DRU i=1:8 | DRU1 [-242:9:-17, 10:9:235] |  | DRU2 [-238:9:-13, 14:9:239] |  | DRU3 [-240:9:-15, 12:9:237] | 
 | DRU4 [-236:9:-11, 16:9:241] |  | DRU5 [-241:9:-16, 11:9:236] |  | DRU6 [-237:9:-12, 15:9:240] | 
 | DRU7 [-239:9:-14, 13:9:238] |  | DRU8 [-235:9:-10, 17:9:242] |  |  | 
106-tone DRU i=1:4 | DRU1 26-tone [DRU1~4], [-8,5] |  | DRU2 26-tone [DRU6~9], [-6,7] |  | DRU3 26-tone [DRU10~13], [-7,6] | 
 | DRU4 26-tone [DRU15~18], [-5,8] |  |  |  |  | 
242-tone DRU i=1:2 | DRU1 106-tone [DRU1~2],26-tone DRU5, [-244,-4,3,9] |  | DRU2 106-tone [DRU3~4],26-tone DRU14, [-243,-3,4,244] |  |  | 

## Slide 6: 40 MHz DRU Pilots [2]
Pilot indices for DRU transmission over 40MHz | 
DRU size | KdRxx_i
DRU26, i = 1:18 | { -224 28 }, { -125 127 }, { -202 50 }, { -103 149 }, { -81 171 }, { -114 138 }, { -213 39 }, { -92 160 }, { -191 61 }, { -169 83 }, { -70 182 }, { -147 105 }, { -48 204 }, { -180 72 }, { -59 193 }, { -158 94 }, { -37 215 }, { -136 116 }
DRU52, i = 1:8 | { -224 -125 28 127 }, {-202 -103 50 149 }, { -213 -114 39 138 }, { -191 -92 61 160 }, { -169 -70 83 182 }, { -147 -48 105 204 }, { -158 -59 94 193 }, { -136 -37 116 215 }
DRU106, i = 1:4 | { -224 -103 28 149 }, { -213 -92 39 160 }, { -169 -48 83 204 }, { -158 -37 94 215 }
DRU242, i = 1:2 | { -224 -213 -103 -92 28 39 149 160 }, { -169 -158 -48 -37 83 94 204 215 }
Size | Tone/MHz | Boost (dB)
DRU26 | 1 | 11.1
DRU52 | 2 | 8.1
DRU106 | 3 | 6.3
DRU242 | 7 | 2.6

## Slide 7: 40 MHz DRU 4xLTF
DLTF-244:244 = [ ...
-1 -1 -1 -1 +1 +1 -1 +1 -1 -1 -1 +1 +1 +1 -1 -1 +1 -1 -1 -1 +1 -1 +1 +1 -1 +1 -1 +1 -1 -1 +1 +1 -1 -1 +1 ...
+1 +1 -1 +1 -1 +1 -1 +1 -1 -1 -1 -1 -1 -1 +1 -1 +1 +1 +1 -1 +1 +1 -1 -1 -1 +1 -1 -1 -1 -1 +1 -1 -1 +1 +1 ...
-1 +1 +1 +1 +1 -1 +1 -1 -1 -1 -1 -1 -1 -1 -1 +1 +1 +1 -1 +1 +1 +1 +1 -1 +1 +1 +1 -1 +1 +1 -1 +1 -1 +1 +1 ...
+1 -1 +1 +1 -1 +1 +1 +1 +1 +1 +1 -1 -1 -1 -1 +1 +1 +1 -1 -1 +1 -1 -1 -1 +1 -1 +1 -1 -1 +1 -1 -1 +1 +1 +1 ...
+1 +1 -1 +1 +1 +1 +1 -1 -1 +1 +1 +1 +1 -1 +1 -1 -1 -1 -1 +1 +1 +1 +1 +1 +1 -1 +1 +1 -1 +1 -1 +1 +1 +1 +1 ...
-1 -1 +1 +1 -1 -1 +1 +1 -1 -1 -1 +1 -1 +1 +1 +1 +1 +1 -1 -1 -1 -1 -1 -1 +1 -1 -1 +1 +1 -1 +1 -1 +1 -1 +1 ...
-1 -1 +1 +1 -1 +1 +1 -1 +1 +1 +1 +1 +1 +1 -1 -1 -1 +1 -1 -1 +1 +1 +1 -1 +1 +1 +1 -1 -1 -1 +1 +1 0 0 0 ...
0 0 -1 +1 +1 +1 -1 -1 -1 -1 +1 -1 -1 -1 +1 -1 +1 +1 +1 +1 +1 -1 +1 -1 +1 +1 -1 -1 +1 -1 -1 -1 +1 +1 +1 ...
-1 +1 +1 -1 +1 +1 +1 +1 -1 -1 -1 -1 -1 +1 -1 +1 -1 +1 +1 -1 -1 -1 +1 +1 +1 -1 -1 +1 +1 +1 +1 -1 -1 -1 +1 ...
+1 -1 -1 -1 -1 -1 +1 -1 +1 +1 +1 +1 -1 -1 +1 -1 +1 +1 -1 +1 -1 +1 +1 +1 -1 +1 -1 -1 +1 -1 +1 +1 -1 +1 +1 ...
+1 -1 +1 -1 -1 +1 +1 -1 +1 -1 +1 +1 +1 -1 +1 -1 +1 -1 -1 -1 -1 +1 +1 -1 -1 +1 +1 -1 -1 +1 -1 +1 +1 +1 -1 ...
-1 -1 -1 -1 +1 -1 -1 +1 -1 +1 +1 -1 +1 +1 -1 -1 -1 -1 -1 -1 +1 +1 +1 +1 +1 +1 -1 -1 +1 +1 -1 +1 -1 +1 -1 ...
-1 +1 +1 -1 -1 +1 -1 -1 -1 +1 +1 -1 +1 +1 -1 +1 -1 -1 +1 -1 +1 +1 -1 -1 +1 -1 +1 -1 -1 -1 +1 -1 -1 +1 -1 ...
+1 +1 +1 -1 +1 +1 -1 +1 +1 -1 +1 +1 -1 +1 +1 +1 -1 +1 -1 -1 -1 -1 -1 +1 +1 +1 -1 +1 -1 -1 +1 +1 -1 -1 ];
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18
DRU26 | 3.26, 3.87 | 3.60, 3.89 | 3.79, 3.60 | 3.74, 3.87 | 3.29, 3.87 | 3.90, 3.74 | 3.89, 3.13 | 3.78, 3.80 | 3.72, 3.84 | 3.08 3.52 | 3.21, 3.68 | 3.85, 3.80 | 3.61, 3.73 | 3.19, 3.45 | 3.85, 3.44 | 3.79, 3.79 | 2.95, 3.67 | 3.68, 3.89
DRU52 | 4.13, 4.04 |  | 3.85, 4.01 |  |  | 4.07, 4.06 |  | 4.05, 4.09 |  | 4.14, 4.10 |  | 3.88, 3.67 |  |  | 3.55, 3.89 |  | 3.89, 4.03 | 
DRU106 | 5.17, 4.92 |  |  |  |  | 5.19, 5.18 |  |  |  | 5.19, 5.08 |  |  |  |  | 5.26, 5.11 |  |  | 
DRU242 | 5.36, 5.35 |  |  |  |  |  |  |  |  | 5.26, 5.38 |  |  |  |  |  |  |  | 
LTF PAPR (dB) for Nss=1&2

## Slide 8: 80 MHz DRU Tone Map [1]
52-tone DRU i=1:16 | DRU1 [-483:36:-51, 17:36:449],[-467:36:-35, 33:36:465] | DRU2 [-475:36:-43, 25:36:457],[-459:36:-27, 41:36:473] | DRU3 [-479:36:-47, 21:36:453],[-463:36:-31, 37:36:469] | DRU4 [-471:36:-39, 29:36:461],[-455:36:-23, 45:36:477]
 | DRU5 [-477:36:-45, 23:36:455],[-461:36:-29, 39:36:471] | DRU6 [-469:36:-37, 31:36:463],[-453:36:-21, 47:36:479] | DRU7 [-481:36:-49, 19:36:451],[-465:36:-33, 35:36:467] | DRU8 [-473:36:-41, 27:36:459],[-457:36:-25, 43:36:475]
 | DRU9 [-482:36:-50, 18:36:450],[-466:36:-34, 34:36:466] | DRU10 [-474:36:-42, 26:36:458],[-458:36:-26, 42:36:474] | DRU11 [-478:36:-46, 22:36:454],[-462:36:-30, 38:36:470] | DRU12 [-470:36:-38, 30:36:462],[-454:36:-22, 46:36:478]
 | DRU13 [-476:36:-44, 24:36:456],[-460:36:-28, 40:36:472] | DRU14 [-468:36:-36, 32:36:464],[-452:36:-20,48:36:480] | DRU15 [-480:36:-48, 20:36:452],[-464:36:-32, 36:36:468] | DRU16 [-472:36:-40, 28:36:460],[-456:36:-24, 44:36:476]
106-tone DRU i=1:8 | DRU1 52-tone [DRU1~2], [-495, 485] | DRU2 52-tone [DRU3~4],[-491, 489] | DRU3 52-tone [DRU5~6],[-489, 491] | DRU4 52-tone [DRU7~8],[-493, 487]
 | DRU5 52-tone [DRU9~10],[-494, 486] | DRU6 52-tone [DRU11~12],[-490,490] | DRU7 52-tone [DRU13~14],[-488,492] | DRU8 52-tone [DRU15~16],[-492,488]
242-tone DRU i=1:4 | DRU1 [-499:4:-19, 17:4:497] |  | DRU2 [-497:4:-17, 19:4:499] | 
 | DRU3 [-498:4:-18, 18:4:498] |  | DRU4 [-496:4:-16, 20:4:500] | 
484-tone DRU i=1:2 | DRU1 [-499:2:-17, 17:2:499] |  | DRU2 [-498:2:-16, 18:2:500] | 
Data and pilot subcarrier indices for Distributed Tone RUs (DRUs) in a 80 MHz UHR TB PPDU | 
DRU type | DRU index and subcarrier range

## Slide 9: 80 MHz DRU Pilots [2]
Pilot indices for DRU transmission over 80MHz | 
DRU size | KdRxx_i
DRU52, i = 1:16 | { -447 -359 53 141 }, { -403 -315 97 185 }, { -227 -139 273 361 }, { -183 -95 317 405 }, { -425 -117 75 383 }, { -381 -73 119 427 }, { -337 -249 163 251 }, { -293 -205 207 295 }, { -194 -106 306 394 }, { -150 -62 350 438 }, { -370 -282 130 218 }, { -326 -238 174 262 }, { -260 -172 240 328 }, { -216 -128 284 372 }, { -392 -84 108 416 }, { -436 -348 64 152 }
DRU106, i = 1:8 | { -403 -315 97 185 }, { -227 -139 273 361 }, { -381 -117 119 383 }, { -293 -205 207 295 }, { -150 -62 350 438 }, { -326 -238 174 262 }, { -260 -172 240 328 }, { -348 -84 152 416 }
DRU242, i = 1:4 | { -403 -315 -227 -139 97 185 273 361 }, { -381 -293 -205 -117 119 207 295 383 }, { -326 -238 -150 -62 174 262 350 438 }, { -348 -260 -172 -84 152 240 328 416 }
DRU484, i = 1:2 | { -403 -381 -315 -293 -227 -205 -139 -117 97 119 185 207 273 295 361 383 }, { -348 -326 -260 -238 -172 -150 -84 -62 152 174 240 262 328 350 416 438 }
Size | Tone/MHz | Boost (dB)
DRU52 | 1 | 11.1
DRU106 | 2 | 8.1
DRU242 | 4 | 5.1
DRU484 | 7 | 2.6

## Slide 10: 80 MHz DRU 4xLTF
DLTF-500:500 = [ ...
0 -1 +1 -1 +1 +1 +1 +1 -1 +1 +1 -1 -1 -1 +1 +1 -1 -1 -1 +1 -1 +1 -1 +1 -1 +1 -1 +1 -1 +1 +1 -1 -1 +1 +1 +1 +1 +1 -1 +1 +1 -1 -1 ...
-1 +1 +1 +1 -1 +1 +1 +1 +1 -1 -1 +1 +1 -1 -1 +1 -1 -1 -1 -1 -1 +1 +1 +1 -1 +1 +1 -1 -1 +1 -1 -1 +1 -1 -1 -1 +1 -1 +1 +1 -1 -1 -1 ...
-1 -1 -1 -1 -1 -1 -1 +1 +1 +1 -1 -1 +1 +1 -1 +1 -1 -1 -1 +1 -1 +1 +1 +1 +1 -1 -1 -1 +1 -1 -1 +1 +1 -1 +1 -1 -1 -1 -1 -1 +1 +1 -1 ...
+1 -1 -1 -1 +1 +1 -1 -1 +1 -1 -1 +1 +1 +1 -1 +1 -1 -1 -1 -1 +1 +1 +1 -1 -1 +1 +1 -1 +1 +1 +1 +1 -1 -1 +1 +1 -1 -1 +1 -1 -1 +1 +1 ...
-1 +1 -1 -1 -1 +1 -1 +1 -1 -1 -1 +1 -1 +1 -1 -1 -1 -1 +1 +1 -1 -1 -1 +1 -1 +1 +1 -1 +1 -1 +1 -1 +1 -1 -1 -1 +1 +1 +1 +1 +1 -1 -1 ...
-1 +1 -1 +1 +1 -1 -1 -1 +1 -1 -1 +1 +1 +1 +1 -1 -1 -1 +1 -1 -1 -1 -1 +1 +1 -1 -1 -1 -1 -1 -1 +1 +1 +1 +1 +1 +1 +1 +1 +1 +1 -1 +1 ...
+1 -1 +1 -1 +1 -1 -1 +1 +1 +1 +1 -1 -1 +1 +1 +1 +1 +1 -1 +1 -1 +1 -1 -1 +1 -1 +1 +1 +1 +1 +1 -1 +1 -1 +1 -1 -1 -1 +1 -1 -1 -1 +1 ...
-1 -1 +1 -1 -1 -1 -1 +1 +1 +1 -1 +1 -1 +1 +1 -1 -1 +1 +1 -1 -1 +1 -1 +1 -1 -1 -1 -1 -1 -1 +1 -1 -1 +1 -1 -1 -1 -1 -1 -1 -1 +1 -1 ...
+1 +1 +1 +1 +1 +1 -1 -1 +1 +1 +1 +1 -1 -1 -1 -1 +1 +1 +1 +1 -1 -1 -1 -1 -1 +1 +1 -1 +1 +1 -1 -1 +1 -1 +1 -1 +1 +1 -1 -1 -1 -1 +1 ...
+1 +1 +1 +1 -1 -1 +1 -1 +1 -1 -1 +1 -1 +1 +1 -1 +1 -1 +1 -1 -1 +1 +1 -1 +1 -1 -1 -1 -1 -1 -1 -1 -1 +1 -1 +1 +1 +1 -1 -1 +1 -1 -1 ...
-1 -1 +1 -1 +1 +1 +1 -1 +1 +1 +1 -1 -1 -1 +1 +1 +1 +1 -1 +1 -1 +1 -1 +1 -1 +1 +1 -1 +1 -1 -1 -1 -1 +1 -1 -1 +1 -1 -1 -1 +1 -1 -1 ...
+1 -1 -1 +1 +1 +1 -1 -1 -1 +1 +1 +1 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 ...
0 +1 -1 -1 -1 -1 +1 -1 +1 -1 +1 -1 -1 +1 -1 +1 -1 -1 +1 +1 -1 +1 +1 -1 +1 -1 +1 +1 -1 +1 -1 +1 +1 +1 -1 +1 +1 -1 -1 -1 +1 +1 -1 ...
-1 -1 +1 +1 -1 +1 -1 +1 -1 -1 +1 +1 +1 -1 +1 +1 -1 +1 -1 +1 +1 +1 -1 +1 -1 +1 -1 +1 -1 +1 +1 -1 -1 -1 -1 -1 -1 +1 +1 -1 -1 +1 +1 ...
+1 +1 -1 -1 +1 +1 +1 -1 +1 +1 -1 -1 -1 +1 +1 +1 -1 -1 +1 -1 +1 +1 -1 -1 -1 -1 +1 -1 -1 -1 -1 -1 +1 -1 -1 -1 -1 -1 +1 +1 +1 +1 -1 ...
-1 -1 -1 +1 +1 -1 +1 -1 -1 +1 +1 +1 -1 +1 -1 -1 +1 +1 +1 -1 +1 -1 -1 +1 +1 +1 -1 +1 +1 -1 +1 +1 -1 +1 +1 +1 -1 -1 -1 -1 +1 -1 +1 ...
+1 +1 +1 -1 +1 -1 +1 -1 -1 +1 +1 +1 -1 +1 -1 -1 +1 +1 -1 -1 +1 -1 +1 +1 -1 -1 +1 +1 +1 +1 +1 +1 +1 -1 -1 +1 +1 +1 +1 +1 +1 -1 -1 ...
+1 +1 -1 -1 +1 +1 +1 +1 -1 -1 +1 +1 +1 -1 -1 -1 -1 -1 -1 +1 +1 +1 +1 -1 -1 -1 +1 +1 +1 -1 -1 +1 +1 +1 -1 +1 -1 +1 -1 +1 -1 -1 +1 ...
-1 +1 -1 +1 -1 +1 +1 +1 +1 -1 +1 +1 -1 -1 -1 -1 +1 -1 -1 +1 -1 -1 +1 -1 -1 -1 -1 +1 -1 +1 -1 +1 -1 -1 -1 +1 -1 +1 -1 -1 -1 -1 -1 ...
-1 -1 -1 -1 +1 -1 -1 -1 +1 +1 +1 +1 +1 +1 -1 -1 +1 -1 +1 -1 -1 +1 -1 +1 -1 -1 +1 -1 +1 +1 +1 +1 +1 -1 -1 -1 -1 +1 +1 +1 -1 -1 +1 ...
+1 +1 +1 +1 +1 +1 -1 -1 +1 +1 -1 -1 +1 +1 -1 -1 -1 +1 +1 -1 +1 +1 -1 -1 +1 -1 -1 -1 -1 +1 -1 +1 +1 -1 -1 +1 +1 -1 -1 +1 +1 -1 +1 ...
-1 -1 -1 +1 +1 +1 -1 +1 -1 +1 -1 -1 +1 -1 -1 +1 -1 +1 -1 +1 +1 -1 +1 -1 -1 -1 -1 +1 +1 -1 +1 +1 +1 -1 +1 +1 +1 +1 +1 +1 -1 -1 -1 ...
+1 -1 -1 -1 -1 -1 -1 +1 -1 -1 -1 -1 -1 +1 +1 -1 +1 -1 +1 +1 -1 -1 -1 -1 -1 +1 -1 -1 +1 +1 +1 -1 -1 +1 +1 -1 +1 -1 +1 -1 +1 +1 +1 ...
+1 -1 -1 -1 -1 -1 +1 -1 -1 -1 +1 -1 ];

## Slide 11: 80 MHz DRU 4xLTF PAPR
LTF PAPR (dB) for Nss=1&2
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
DRU52 | 4.96, 4.97 | 4.36, 4.43 | 5.01, 4.87 | 4.98, 4.89 | 4.88, 4.90 | 4.91, 4.94 | 4.68, 4.20 | 5.00, 4.92 | 4.60, 4.89 | 4.93, 5.01 | 4.84, 4.88 | 5.01, 4.93 | 5.08, 5.08 | 4.93, 5.06 | 4.96, 5.02 | 5.07, 4.60
DRU106 | 5.03, 5.12 |  | 5.12, 4.92 |  | 5.07, 5.20 |  | 5.03, 5.07 |  | 5.13, 5.06 |  | 4.86, 5.13 |  | 5.07, 5.15 |  | 5.18, 5.14 | 
DRU242 | 5.36, 5.11 |  |  |  | 5.26, 5.25 |  |  |  | 5.19, 5.38 |  |  |  | 5.35, 5.11 |  |  | 
DRU484 | 5.49, 5.41 |  |  |  |  |  |  |  | 5.50, 5.29 |  |  |  |  |  |  | 

## Slide 12: PAPR Summary
 | RRU PAPR (dB) |  | DRU PAPR (dB) |  |  |  | 
 | BPSK data, Median PAPR in 80MHz | 80MHz LTF | BPSK data, Median PAPR in 20MHz | BPSK data, Median PAPR in 80MHz | 20MHz DLTF, Max PAPR | 40MHz DLTF, Max PAPR | 80MHz DLTF, Max PAPR
RU26 | 5.89 | 4.25 | 5.95 | - | 3.80 | 3.90 | -
RU52 | 6.71 | 4.97 | 7.21 | 7.89 | 4.75 | 4.14 | 5.08
RU106 | 7.29 | 5.53 | 7.72 | 8.25 | 4.77 | 5.26 | 5.20
RU242 | 7.94 | 5.60 | - | 8.33 | - | 5.38 | 5.38
RU484 | 8.44 | 6.00 | - | 8.77 | - | - | 5.50
RU996 | 8.84 | 6.29 | - | - | - | - | -

## Slide 13: Conclusions
Proposed new low PAPR 4xLTF optimized for DRU which provides similar or lower PAPR than the EHT 4xLTF

## Slide 14: References
[1] 11-24-0468-02-00bn-dru-tone-plan-for-11bn
[2] 11-24-1230-01-00bn-pilot-tone-design-in-dru-transmission.pptx
[3] 11-24-1097-00-00bn-thoughts-on-UHR-LTF-for-DRU

## Slide 15: SP #1
Do you agree to add to the 11bn SFD the following design for 20MHz 4xLTF for DRU?
DLTF-122:122 = [ ...
0 0 -1 +1 -1 +1 -1 +1 +1 +1 -1 +1 +1 -1 +1 -1 -1 -1 -1 +1 -1 -1 +1 -1 -1 +1 +1 -1 -1 -1 -1 -1 -1 -1 +1 ...
+1 -1 +1 -1 +1 +1 -1 +1 -1 +1 -1 -1 -1 -1 -1 +1 +1 +1 -1 +1 +1 -1 -1 +1 +1 -1 +1 -1 +1 -1 +1 -1 -1 +1 -1 ...
+1 +1 +1 +1 -1 +1 +1 -1 +1 -1 -1 -1 +1 +1 -1 +1 -1 -1 +1 -1 -1 -1 -1 -1 -1 +1 -1 +1 -1 -1 +1 +1 -1 +1 +1 ...
-1 +1 +1 -1 +1 +1 -1 +1 -1 +1 -1 +1 -1 -1 +1 -1 0 0 0 -1 +1 -1 +1 -1 -1 +1 -1 -1 -1 +1 -1 +1 -1 -1 -1 ...
+1 +1 +1 -1 +1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 +1 +1 -1 +1 -1 -1 -1 -1 +1 +1 +1 +1 +1 -1 -1 +1 -1 -1 +1 ...
+1 -1 -1 -1 -1 +1 -1 +1 +1 -1 -1 +1 +1 +1 -1 -1 +1 -1 -1 -1 -1 +1 -1 +1 +1 -1 -1 +1 -1 +1 +1 -1 +1 +1 -1 ...
+1 +1 -1 +1 +1 -1 +1 -1 +1 -1 -1 +1 +1 -1 -1 -1 -1 +1 +1 +1 -1 -1 -1 -1 +1 -1 -1 -1 +1 +1 +1 -1 +1 0 0 ];

## Slide 16: SP #2
DLTF-244:244 = [ ...
-1 -1 -1 -1 +1 +1 -1 +1 -1 -1 -1 +1 +1 +1 -1 -1 +1 -1 -1 -1 +1 -1 +1 +1 -1 +1 -1 +1 -1 -1 +1 +1 -1 -1 +1 ...
+1 +1 -1 +1 -1 +1 -1 +1 -1 -1 -1 -1 -1 -1 +1 -1 +1 +1 +1 -1 +1 +1 -1 -1 -1 +1 -1 -1 -1 -1 +1 -1 -1 +1 +1 ...
-1 +1 +1 +1 +1 -1 +1 -1 -1 -1 -1 -1 -1 -1 -1 +1 +1 +1 -1 +1 +1 +1 +1 -1 +1 +1 +1 -1 +1 +1 -1 +1 -1 +1 +1 ...
+1 -1 +1 +1 -1 +1 +1 +1 +1 +1 +1 -1 -1 -1 -1 +1 +1 +1 -1 -1 +1 -1 -1 -1 +1 -1 +1 -1 -1 +1 -1 -1 +1 +1 +1 ...
+1 +1 -1 +1 +1 +1 +1 -1 -1 +1 +1 +1 +1 -1 +1 -1 -1 -1 -1 +1 +1 +1 +1 +1 +1 -1 +1 +1 -1 +1 -1 +1 +1 +1 +1 ...
-1 -1 +1 +1 -1 -1 +1 +1 -1 -1 -1 +1 -1 +1 +1 +1 +1 +1 -1 -1 -1 -1 -1 -1 +1 -1 -1 +1 +1 -1 +1 -1 +1 -1 +1 ...
-1 -1 +1 +1 -1 +1 +1 -1 +1 +1 +1 +1 +1 +1 -1 -1 -1 +1 -1 -1 +1 +1 +1 -1 +1 +1 +1 -1 -1 -1 +1 +1 0 0 0 ...
0 0 -1 +1 +1 +1 -1 -1 -1 -1 +1 -1 -1 -1 +1 -1 +1 +1 +1 +1 +1 -1 +1 -1 +1 +1 -1 -1 +1 -1 -1 -1 +1 +1 +1 ...
-1 +1 +1 -1 +1 +1 +1 +1 -1 -1 -1 -1 -1 +1 -1 +1 -1 +1 +1 -1 -1 -1 +1 +1 +1 -1 -1 +1 +1 +1 +1 -1 -1 -1 +1 ...
+1 -1 -1 -1 -1 -1 +1 -1 +1 +1 +1 +1 -1 -1 +1 -1 +1 +1 -1 +1 -1 +1 +1 +1 -1 +1 -1 -1 +1 -1 +1 +1 -1 +1 +1 ...
+1 -1 +1 -1 -1 +1 +1 -1 +1 -1 +1 +1 +1 -1 +1 -1 +1 -1 -1 -1 -1 +1 +1 -1 -1 +1 +1 -1 -1 +1 -1 +1 +1 +1 -1 ...
-1 -1 -1 -1 +1 -1 -1 +1 -1 +1 +1 -1 +1 +1 -1 -1 -1 -1 -1 -1 +1 +1 +1 +1 +1 +1 -1 -1 +1 +1 -1 +1 -1 +1 -1 ...
-1 +1 +1 -1 -1 +1 -1 -1 -1 +1 +1 -1 +1 +1 -1 +1 -1 -1 +1 -1 +1 +1 -1 -1 +1 -1 +1 -1 -1 -1 +1 -1 -1 +1 -1 ...
+1 +1 +1 -1 +1 +1 -1 +1 +1 -1 +1 +1 -1 +1 +1 +1 -1 +1 -1 -1 -1 -1 -1 +1 +1 +1 -1 +1 -1 -1 +1 +1 -1 -1 ];
Do you agree to add to the 11bn SFD the following design for 40MHz 4xLTF for DRU?

## Slide 17: SP #3
DLTF-500:500 = [ ...
0 -1 +1 -1 +1 +1 +1 +1 -1 +1 +1 -1 -1 -1 +1 +1 -1 -1 -1 +1 -1 +1 -1 +1 -1 +1 -1 +1 -1 +1 +1 -1 -1 +1 +1 +1 +1 +1 -1 +1 +1 -1 -1 ...
-1 +1 +1 +1 -1 +1 +1 +1 +1 -1 -1 +1 +1 -1 -1 +1 -1 -1 -1 -1 -1 +1 +1 +1 -1 +1 +1 -1 -1 +1 -1 -1 +1 -1 -1 -1 +1 -1 +1 +1 -1 -1 -1 ...
-1 -1 -1 -1 -1 -1 -1 +1 +1 +1 -1 -1 +1 +1 -1 +1 -1 -1 -1 +1 -1 +1 +1 +1 +1 -1 -1 -1 +1 -1 -1 +1 +1 -1 +1 -1 -1 -1 -1 -1 +1 +1 -1 ...
+1 -1 -1 -1 +1 +1 -1 -1 +1 -1 -1 +1 +1 +1 -1 +1 -1 -1 -1 -1 +1 +1 +1 -1 -1 +1 +1 -1 +1 +1 +1 +1 -1 -1 +1 +1 -1 -1 +1 -1 -1 +1 +1 ...
-1 +1 -1 -1 -1 +1 -1 +1 -1 -1 -1 +1 -1 +1 -1 -1 -1 -1 +1 +1 -1 -1 -1 +1 -1 +1 +1 -1 +1 -1 +1 -1 +1 -1 -1 -1 +1 +1 +1 +1 +1 -1 -1 ...
-1 +1 -1 +1 +1 -1 -1 -1 +1 -1 -1 +1 +1 +1 +1 -1 -1 -1 +1 -1 -1 -1 -1 +1 +1 -1 -1 -1 -1 -1 -1 +1 +1 +1 +1 +1 +1 +1 +1 +1 +1 -1 +1 ...
+1 -1 +1 -1 +1 -1 -1 +1 +1 +1 +1 -1 -1 +1 +1 +1 +1 +1 -1 +1 -1 +1 -1 -1 +1 -1 +1 +1 +1 +1 +1 -1 +1 -1 +1 -1 -1 -1 +1 -1 -1 -1 +1 ...
-1 -1 +1 -1 -1 -1 -1 +1 +1 +1 -1 +1 -1 +1 +1 -1 -1 +1 +1 -1 -1 +1 -1 +1 -1 -1 -1 -1 -1 -1 +1 -1 -1 +1 -1 -1 -1 -1 -1 -1 -1 +1 -1 ...
+1 +1 +1 +1 +1 +1 -1 -1 +1 +1 +1 +1 -1 -1 -1 -1 +1 +1 +1 +1 -1 -1 -1 -1 -1 +1 +1 -1 +1 +1 -1 -1 +1 -1 +1 -1 +1 +1 -1 -1 -1 -1 +1 ...
+1 +1 +1 +1 -1 -1 +1 -1 +1 -1 -1 +1 -1 +1 +1 -1 +1 -1 +1 -1 -1 +1 +1 -1 +1 -1 -1 -1 -1 -1 -1 -1 -1 +1 -1 +1 +1 +1 -1 -1 +1 -1 -1 ...
-1 -1 +1 -1 +1 +1 +1 -1 +1 +1 +1 -1 -1 -1 +1 +1 +1 +1 -1 +1 -1 +1 -1 +1 -1 +1 +1 -1 +1 -1 -1 -1 -1 +1 -1 -1 +1 -1 -1 -1 +1 -1 -1 ...
+1 -1 -1 +1 +1 +1 -1 -1 -1 +1 +1 +1 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 ...
0 +1 -1 -1 -1 -1 +1 -1 +1 -1 +1 -1 -1 +1 -1 +1 -1 -1 +1 +1 -1 +1 +1 -1 +1 -1 +1 +1 -1 +1 -1 +1 +1 +1 -1 +1 +1 -1 -1 -1 +1 +1 -1 ...
-1 -1 +1 +1 -1 +1 -1 +1 -1 -1 +1 +1 +1 -1 +1 +1 -1 +1 -1 +1 +1 +1 -1 +1 -1 +1 -1 +1 -1 +1 +1 -1 -1 -1 -1 -1 -1 +1 +1 -1 -1 +1 +1 ...
+1 +1 -1 -1 +1 +1 +1 -1 +1 +1 -1 -1 -1 +1 +1 +1 -1 -1 +1 -1 +1 +1 -1 -1 -1 -1 +1 -1 -1 -1 -1 -1 +1 -1 -1 -1 -1 -1 +1 +1 +1 +1 -1 ...
-1 -1 -1 +1 +1 -1 +1 -1 -1 +1 +1 +1 -1 +1 -1 -1 +1 +1 +1 -1 +1 -1 -1 +1 +1 +1 -1 +1 +1 -1 +1 +1 -1 +1 +1 +1 -1 -1 -1 -1 +1 -1 +1 ...
+1 +1 +1 -1 +1 -1 +1 -1 -1 +1 +1 +1 -1 +1 -1 -1 +1 +1 -1 -1 +1 -1 +1 +1 -1 -1 +1 +1 +1 +1 +1 +1 +1 -1 -1 +1 +1 +1 +1 +1 +1 -1 -1 ...
+1 +1 -1 -1 +1 +1 +1 +1 -1 -1 +1 +1 +1 -1 -1 -1 -1 -1 -1 +1 +1 +1 +1 -1 -1 -1 +1 +1 +1 -1 -1 +1 +1 +1 -1 +1 -1 +1 -1 +1 -1 -1 +1 ...
-1 +1 -1 +1 -1 +1 +1 +1 +1 -1 +1 +1 -1 -1 -1 -1 +1 -1 -1 +1 -1 -1 +1 -1 -1 -1 -1 +1 -1 +1 -1 +1 -1 -1 -1 +1 -1 +1 -1 -1 -1 -1 -1 ...
-1 -1 -1 -1 +1 -1 -1 -1 +1 +1 +1 +1 +1 +1 -1 -1 +1 -1 +1 -1 -1 +1 -1 +1 -1 -1 +1 -1 +1 +1 +1 +1 +1 -1 -1 -1 -1 +1 +1 +1 -1 -1 +1 ...
+1 +1 +1 +1 +1 +1 -1 -1 +1 +1 -1 -1 +1 +1 -1 -1 -1 +1 +1 -1 +1 +1 -1 -1 +1 -1 -1 -1 -1 +1 -1 +1 +1 -1 -1 +1 +1 -1 -1 +1 +1 -1 +1 ...
-1 -1 -1 +1 +1 +1 -1 +1 -1 +1 -1 -1 +1 -1 -1 +1 -1 +1 -1 +1 +1 -1 +1 -1 -1 -1 -1 +1 +1 -1 +1 +1 +1 -1 +1 +1 +1 +1 +1 +1 -1 -1 -1 ...
+1 -1 -1 -1 -1 -1 -1 +1 -1 -1 -1 -1 -1 +1 +1 -1 +1 -1 +1 +1 -1 -1 -1 -1 -1 +1 -1 -1 +1 +1 +1 -1 -1 +1 +1 -1 +1 -1 +1 -1 +1 +1 +1 ...
+1 -1 -1 -1 -1 -1 +1 -1 -1 -1 +1 -1 ];
Do you agree to add to the 11bn SFD the following design for 80MHz 4xLTF for DRU?