## Slide 1: Sounding Design for C-BF
Date: 2024-09-08
Authors:
Name | Affiliations | Address | Phone | email
Ron Porat | Broadcom |  |  | ron.porat@broadcom.com
Srinath Puducheri | Broadcom |  |  | 
Karim Toussi | Broadcom |  |  | 

## Slide 2: Introduction
In the July meeting the group has motioned in C-BF.
Previously in [1] we provided simulation results of C-BF and introduced full rank and partial rank nulling. Using the insights gained from the simulation results we propose here a sounding design for C-BF
We propose both options of joint NDP and sequential NDP sounding,
  Joint NDP -sounding enables partial-rank nulling, which unlocks higher CBF gains.
  Sequential NDP -sounding is sufficient when only full-rank nulling is desired/possible and accommodates STA that will not support 8ss sounding needed for joint NDP sounding (with 2AP)
Our underlying design direction focuses on simplicity and minimizing deviation from the current sounding protocol and maintaining the same feedback format for single AP sounding

## Slide 3: Joint vs Sequential NDP Sounding
Joint NDP sounding:
  Both APs transmit NDP jointly, each transmitting on different spatial streams/dimensions
  STAs estimate composite channel H = [H1 H2] from both APs, and form a single MU-type feedback report based on H which suffices for partial rank nulling and doesn’t deviate from current BF feedback design.
Sequential NDP sounding:
  Each AP transmits NDP individually.
  STAs feedback separate MU-type reports per AP.

## Slide 4: From [1] Appendix C – Partial Rank Nulling Benefits
Partial rank nulling - in a scenario where a 2x2 STA receives only one stream from its AP, the other AP needs to null in only one direction, enabling transmission for more STA.
Below we compare CBF of two 4x4AP with 1STA vs. 2STA per AP: Nss = [2+2 vs. 1+1+1+1] by showing gains vs. single AP utilizing MU-MIMO to 2 STA.
 |  | Serving AP STA SNR (dB) |  |  |  |  | 
 |  | 35 | 30 | 25 | 20 | 15 | 10
X (db) | 0 | 0.98, 1.16 | 0.94, 1.23 | 0.83, 1.28 | 0.67, 1.05 | 0.61, 1.08 | 0.36, 1.15
 | 5 | 1.10, 1.25 | 1.06, 1.30 | 0.93, 1.39 | 0.75, 1.19 | 0.77, 1.22 | 0.61, 1.43
 | 10 | 1.16, 1.32 | 1.14, 1.34 | 1.05, 1.49 | 0.87, 1.38 | 0.93, 1.45 | 0.86, 1.62
 | 15 | 1.21, 1.41 | 1.24, 1.39 | 1.25, 1.59 | 1.04, 1.60 | 1.09, 1.76 | 1.07, 1.80
 | 20 | 1.30, 1.49 | 1.31, 1.51 | 1.41, 1.68 | 1.24, 1.79 | 1.19, 1.88 | 
 | 25 | 1.41, 1.55 | 1.37, 1.66 | 1.57, 1.77 | 1.43, 1.92 |  | 
 | 30 | 1.52, 1.63 | 1.48, 1.75 | 1.64, 1.92 |  |  | 

## Slide 5: Joint NDP Sounding
Each BSS’ STAs sounded separately
Frame sequence for AP1’s STAs:
Frame sequence for AP2’s STAs:
AP1 NDPA | SIFS | Joint NDP (AP1+AP2) | SIFS | AP1 BFRP | SIFS | STA BFR
AP2 NDPA | SIFS | Joint NDP (AP1+AP2) | SIFS | AP2 BFRP | SIFS | STA BFR

## Slide 6: Sequential NDP Sounding
Four part sequence:
  AP1 sounds its own STAs: unchanged from existing single-AP sounding sequence
  AP2 sounds AP1 STAs
  AP2 sounds its own STAs: unchanged from existing single-AP sounding sequence
  AP1 sounds AP2 STAs
AP1 NDPA | SIFS | AP2 NDP | SIFS | AP1 BFRP | SIFS | STA BFR
AP2 NDPA | SIFS | AP1 NDP | SIFS | AP2 BFRP | SIFS | STA BFR

## Slide 7: PHY Capabilities
We note that while C-BF with 4x4 AP is limited to 4ss, joint sounding requires support for 8ss
  This is different from single AP MU-MIMO where the same total Nss applies to both sounding and data PPDU
Hence we propose to have separate capabilities for sounding support and data PPDU support
  Devices may support 8ss sounding but only 4ss data PPDU

## Slide 8: Summary
Proposed that to enable C-BF we support both joint NDP and sequential NDP sounding
Proposed to have separate capabilities for sounding and data PPDU

## Slide 9: References
[1] 11-23-0776-01-0uhr-Performance of C-BF and C-SR

## Slide 10: SP#1
Do you support to include both sequential NDP and joint NDP sounding options for C-BF?

## Slide 11: SP#2
Do you support having two separate capabilities for the maximum number of spatial streams supported for reception in a UHR sounding NDP and the maximum total number of streams (across all users) supported for reception in UHR DL MU-MIMO and CoBF PPDUs?
  The only possible values for each capability are 4 and 8