## Slide 1: Enhancements on Relaying for UHR
Date: 2024-9-11
Authors:

## Slide 2: Introduction
Relay transmission is an important topic discussed in 802.11bn Task Group, both for range extension or for throughput improvement.
In this presentation we will provide some enhanced methods for relay operation.

## Slide 3: TXS based Relaying
TXS based relaying includes an AP allocating a time period to a Relay STA within a TXOP, for the relay STA both to receive and to transmit relayed data.
In the example, relay STA (STA-1) receives the data frame from AP and transmits to destination STA (STA-2) within t1.

## Slide 4: Relaying Failure due to Limited Time
Allocated time may not be sufficient for the relay to perform the end to end relay operation and another STA may access the medium before the relay STA can transmit the relayed frame to the destination.
  For example TXOP limit may only cover first data transmission from AP to the STA-1.
This may cause delivery delay of the relayed frame.

## Slide 5: Proposal
By indicating multilink relaying, AP can reduce the total operation time. The relay STA utilizes another link (link 2) to transmit relayed data to the destination STA.
When indicating a relay operation to a relay STA, the AP indicates a second link for the relay STA to transmit one or more relayed frames to the destination STA. ???
  relayed.

## Slide 6: Necessity of Relaying
Destination STA (STA-2) may be within the communication range of AP and relay STA (STA-1).
On hearing RTS frame, destination STA may set its NAV for the duration indicated in RTS and may remain idle.
If destination STA can successfully decode data frame, destination STA may be able to obtain the data transmitted in data frame.
  Subsequent frame transmissions of the relay procedure (including an ACK frame, an RTS frame, a CTS frame, a data frame and an ACK frame) become redundant as destination STA has already received the data frame.

## Slide 7: Proposal
AP transmits data frame to both relay STA and destination STA with the indication that both relay STA and destination STA should decode the data frame.
Relay STA buffers the data frame and waits for a trigger frame from AP before transmitting to the destination STA.

## Slide 8: Proposal
AP compares MPDUs correctly received by the destination STA and Relay STA (based on ack frames received from the destination STA and the relay STA).
AP transmits a Trigger Frame to the relay STA to send any MPDUs incorrectly received by the destination STA.
Merge them

## Slide 9: Link Quality Variation during Relaying
Source STA may receive information about the link status between the candidate Relay STAs and the Destination STA, to select the Relay STA for the data transmission.
If there is a change in the quality of the link between Relay STA and Destination STA, source STA may use this information to adjust its own transmission parameters used for transmission to the Relay STA.
  For example, the Modulation and Coding Scheme between source and relay may need to be updated.

## Slide 10: Current Status
Current procedure does not allow Source STA to determine and set the transmission parameters used by Relay STA to the Destination STA.
  Relay STA determines the transmission parameters by itself.
This may result in sub-optimal resource allocation and/or increased interference in the Basic Service Set.
  For example, lack of knowledge and/or control of these transmission parameters by source STA may result in source STA overestimating the amount of data that can be transmitted between source STA and Destination STA in a given TXOP obtained by the Source STA. This can lead to Source STA not being able to transmit all of the data frames scheduled for transmission during the current TXOP.
  In another aspect, the lack of knowledge and/or control of the transmission parameters by source STA may limit the ability of source STA to control the interference caused by transmissions of relay STA.

## Slide 11: Proposal
Source STA receives from the relay STA link adaptation feedback for the link between the relay STA and the destination STA.
If the link adaptation feedback is different than stored link adaptation feedback for the link, source STA transmits to the relay STA, a link adaptation information to be used by the relay STA for the link.
The link adaptation feedback/information may comprise information that may be used by STA to adapt an MCS, a number of spatial streams, and/or an RU allocation used.
Source
STA
Data
Data
Link. A.
Feedback
Link. A.
Information
Relay
STA
Destination
STA
BA
Link. A.
Feedback
BA

## Slide 12: Conclusion
In this presentation we provided multiple ideas to be considered for relay operation in UHR.