## Slide 1: Enhancements on Relaying for UHR
Date: 2024-9-11
Authors:

## Slide 2: Introduction
Relay operation is one of important topics discussed in 802.11bn Task Group, both for range extension or for throughput improvement.
In this presentation we will provide some enhanced methods for relay operation.

## Slide 3: Recap - TXS based Relaying
TXS based relaying includes an AP allocating a time period to a relay STA within a TXOP, for the relay STA both to receive and to transmit relayed data.
In the example, relay STA (STA-1) receives a data from AP and transmits the data to destination STA (STA-2) within the allocated time or the TXOP.
AP
STA
-
1
STA
-
2
Data
ACK
Data
MRTT
CTS
TXOP
ACK
t1

## Slide 4: Delay of relaying operation
However, the AP may not allocate a time enough for the relay STA to receive a data and forward the data to the destination STA
  For example, TXOP limit for the data may only cover first data transmission from AP to the relay STA.
  So, the relay STA’s transmission may happen in a different TXOP
In some cases, another STA may access the medium between two TXOPs
  E.g., before the relay STA transmits the relayed data frame to the destination STA.
This may cause delivery delay of the relayed frame.
RTS
RTS

## Slide 5: Proposal
To reduce the delay of the relaying operation, if a relay STA is affiliated with an MLD with more than two link, the relay STA MLD can decide to forward the received data to the destination STA MLD via a different link from a link that the data is received from the AP MLD
  E.g.1, If there are multiple links, the relay STA MLD may choose one of them based on the link availability
  E.g.2, AP MLD may indicate, the relay STA MLD, a link to be used for relaying the data to the destination STA MLD. Then, the relay STA MLD will consider the link when the relay STA MLD transmits the data to the destination STA MLD
AP MLD
AP MLD
Relay
STA MLD
Destination
STA MLD
Relay
STA MLD

## Slide 6: Necessity of Relaying
Destination STA (STA-2) may be within the communication range of AP and relay STA (STA-1).
On hearing RTS frame, destination STA may set its NAV for the duration indicated in RTS and may remain idle.
If destination STA can successfully decode data frame, destination STA may be able to obtain the data transmitted in data frame.
  Subsequent frame transmissions of the relay procedure (including an ACK frame, an RTS frame, a CTS frame, a data frame and an ACK frame) become redundant as destination STA has already received the data frame.

## Slide 7: Proposal
AP transmits data frame to both relay STA and destination STA with the indication that both relay STA and destination STA should decode the data frame.
Relay STA buffers the data frame and waits for a trigger frame from AP before transmitting to the destination STA.
AP compares MPDUs correctly received by the destination STA and Relay STA (based on ack frames received from the destination STA and the relay STA).
AP transmits a Trigger Frame for the relay STA to send any MPDUs incorrectly received by the destination STA.
AP
STA
-
1
STA
-
2
Data
MU
-
RTS
CTS
CTS
BA
ACK
Trigger
Frame
Data
ACK
BA
Request

## Slide 8: Conclusion
In this presentation we provided multiple ideas to be considered for relay operation in UHR.