## Slide 1: Discussion on DSO Operation
Date: 2024-10
Authors:
Name | Affiliation | Address | Phone | Email
Kaiying Lu James Yee Eason Chang Carlos Lai Frank Hsu Li-Hsiang Sun Yonggang Fang Gabor Bajko | MediaTek | 2840 Junction Ave., San Jose, CA | 408-3872160 | Kaiying.lu@mediatek.com
James Yee | MediaTek |  |  | 
Eason Change | MediaTek |  |  | 
Li-Hsiang Sun | MediaTek |  |  | 
Yonggang Fang | MediaTek |  |  | 
Gabor Bajko | MediaTek |  |  | 
Slide 1

## Slide 2: Introduction
IEEE 802.11bn task group has a lot of discussions on dynamic subband operation[1~8].
This contribution will share some considerations on DSO operation :
  DSO subband configurations
  Considerations on DSO initial control/control response frame
Slide 2

## Slide 3: DSO Subband Configurations
DSO operation is to target on the bandwidth mismatch between the AP and the non-AP.
By allowing the AP to configure one or more DSO subbands within the wide bandwidth, it will enable wideband AP to fully utilize the bandwidth resources by allocating RUs which are out of the operating bandwidth of intended recipients.
Theoretically there are many combinations of candidate DSO subband types and locations, for example:
  For a 320MHz BSS, there could be one candidate 160MHz DSO subband, 3 candidate 80MHz DSO subbands, 15 candidate 20MHz DSO subbands
  For a 160MHz BSS, there could be one candidate 80MHz DSO subband, 7 candidate 20MHz DSO subbands
  For a 80MHz BSS, there could be 3 candidate 20MHz DSO subbands
However, the more flexible DSO subband configurations may require higher complexity, more overheads, and larger memory consumption.

## Slide 4: Motivation for Proposed DSO Subband Configurations
To balance the flexibility of DSO subband combinations during a DSO TXOP with the complexity of scheduling, memory consumption for storing multiple calibration parameters and sounding overheads for multiple subband channel conditions, the number of DSO subband configurations should be limited.
To balance the flexibility of DSO subband utilization with spectrum efficiency (good throughput) of DSO subbands, the size of DSO subband bandwidth should also be carefully chosen.

## Slide 5: Proposed DSO Subband Configuration
The minimum DSO subband bandwidth is 80MHz.
DSO subband configurations can be defined corresponding to operating bandwidth of a BSS:
  Secondary 80MHz (S_80) is the DSO subband for 160MHz bandwidth
  S_80 and S_160 are DSO subbands for 320MHz bandwidth
  Whether allow S_160_low 80 and/or S_160_high 80 as a DSO subband or not is TBD
The DSO subband for a non-AP DSO STA can be defined based on the operating bandwidth of the STA, for example:
  S_80 as a DSO subband for a DSO STA with 80MHz operating bandwidth
  S_160 as a DSO subband for a DSO STA with 160MHz operating bandwidth

## Slide 6: General requirements for DSO ICF/ICR
DSO ICF can be BSRP and/or MU-RTS trigger frame
  Easy to support EMLSR DSO STAs
DSO ICF shall be able to provide enough DSO switching delay by transmitting intermediate FCS in the User Info field preceding padding and FCS field.
  TGbn has passed the motion “Define a way in 11bn to include in an initial control frame an intermediate FCS for UHR STA(s) that precedes padding and the FCS field”
The RU Allocation subfield in the User Info field of ICF addressed to the intended DSO STA indicates the RU allocation for ICR within the designated DSO subband.
  When ICF is MU-RTS, the RU allocation for ICR may not follow the same rule as primary subband.
    the AP does not need to be able to decode ICR on DSO subband
  When ICF is BSRP, the RU allocation for ICR follows the existing encoding of the PS160 and RU Allocation subfields defined in an EHT variant User Info field.

## Slide 7: General requirements for DSO ICF/ICR (ctnd.)
DSO ICF may implicitly indicate the DSO operation/subband by RU allocation, and/or explicitly indicate the DSO operation/subband switch in the User Info field. The explicit signaling is TBD.
  Explicit indication provides simple and unambiguous indication for a DSO STA to determine DSO switch operation
DSO ICF (BSRP) may request channel availability information from intended DSO responder(s)
  BQR/Channel availability request indication in User Info field
  DSO responder shall feedback Per 20 channel availability information within the DSO subband if requested
  ICR carries BSR/BQR in QoS null frame or other frame (e/g., MSBA)
An intended DSO STA switches to the assigned DSO subband and responds ICR on the DSO subband
  The ICF responders may perform CS check before responding to DSO ICF, (e.g., basic NAV, CCA during SIFS interval between ICF/ICR)

## Slide 8: DSO Initial Control Frame Exchange
When an AP transmits MU-RTS as DSO ICF to initiate a DL TXOP on 320MHz
E.g., STA1 is an 80MHz non-DSO device, STA2 is an 80MHz DSO device; STA3 and STA4 are 160MHz DSO devices
The AP allocates P80 subband to STA1, S80 DSO subband to STA2, L80 in 160 DSO subband to STA3 and H80 in 160 DSO subband to STA4
MU-RTS indicates RU allocations for CTS response frames from each STA within the allocated subbands.
The intended DSO STAs switch to the DSO subband to receive DL OFDMA PPDU
STA1
STA2
STA3
S80
S160_L80
P80
MU-RTS
CTS
STA4
S160_H80
AP
CTS
CTS
CTS
DL OFDMA PPDU to STA1
DL OFDMA PPDU to STA2
DL OFDMA PPDU to STA3
DL OFDMA PPDU to STA4
BA
BA
BA
BA

## Slide 9: DSO Initial Control Frame Exchange
When an AP transmits BSRP as DSO ICF to initiate an UL TXOP on 320MHz
E.g., STA1 is an 80MHz non-DSO device, STA2 is an 80MHz DSO device; STA3 and STA4 are 160MHz DSO devices
BSRP indicates ICR RU allocations: P80 subband to STA1, S80 DSO subband to STA2, L80 in 160 DSO subband to STA3 and H80 in 160 DSO subband to STA4
The intended DSO STAs switch to the designated DSO subbands and respond ICR on the corresponding assigned RU
The AP requests BSR/BQR feedback and identifies the ICR from intended recipients
The AP then triggers UL TB PPDU from the responders and allocate resources based on the received feedback
Note: BSRP as DSO ICF can also be used for DL TXOP
STA1
STA2
STA3
S80
S160_L80
P80
BSRP
ICR
STA4
S160_H80
M-BA
UL TB PPDU from STA4
AP
ICR
ICR
ICR
Trigger
UL TB PPDU from STA1
UL TB PPDU from STA2

## Slide 10: Intermediate FCS Field In DSO ICF
The intermediate FCS field in DSO ICF
  is a special User Info field
  contains a 32-bit CRC. The FCS field value is calculated over all of the fields of the MAC header and the Frame Body field including all User Info fields before the intermediate FCS field.
  separates FCS into two parts
    FCS-1 has 4 bits of FCS occupying B0-B3 of the User Info field
    FCS-2 has 28 bits of FCS occupying B12-B39 of the User Info field
  includes an 8-bit Intermediate-FCS indicator in B4-B11 of the User Info field
    B0~B11 in Intermediate-FCS field is guaranteed by the AP to be ignored by legacy.
  I-FCS field may be immediately after the User Info fields of DSO STAs with padding delay requirements
FCS-1 | Intermediate -FCS Indicator | FCS-2
Intermediate-FCS field format
B0
B3
B11
B4
B12
B39

## Slide 11: Summary
11
This contribution discussed some details for the DSO operation.
  DSO subband configurations
    Default DSO subbands for 160MHz and 320MHz operating bandwidth are discussed
    One or more non-default 80MHz DSO subband(s) in 320MHz BSS operating bandwidth may be indicated if supported
  General DSO ICF/ICR requirements
    MU-RTS and BSRP trigger frame can be DSO ICF with the possibility to support EMLSR DSO devices
    RU Allocation rules for ICR based on ICF are discussed
    Channel availability info request can be indicated in BSRP ICF
  Intermediate FCS field in DSO ICF is proposed

## Slide 12: SP1
Do you support that
  DSO STAs shall be UHR STAs with operating bandwidth of 80MHz or above
  Secondary 80MHz in 160MHz BSS can be a DSO subband
  Secondary 160MHz in 320MHz BSS can be a DSO subband
  One 80MHz subband in 320MHz BSS can be a DSO subband
  Whether allow more than one 80MHz subband in 320MHz BSS is TBD
  The DSO ICF-ICR exchange and the PPDUs that follows it shall only be between UHR STAs
Slide 12

## Slide 13: SP2
Do you agree that an AP shall initiate a DSO initial Control frame (ICF) to allocate resources to a DSO STA in a DSO subband?
  BSRP trigger frame shall be a DSO ICF for DL/UL DSO TXOP.
  Whether MU-RTS trigger frame is a DSO ICF is TBD
  RU allocation field in ICF indicates the resource allocation for ICR within the DSO subband
    Whether an explicit indication to a DSO STA to determine DSO operation is TBD
Slide 13

## Slide 14: SP3
Do you agree that an AP, that supports transmitting intermediate FCS, shall include an intermediate FCS in initial control frame to initiate a DSO TXOP, if needed by at least one scheduled DSO STA?
  Whether mandatory or optional support for transmitting intermediate FCS is TBD.
  Note: intermediate FCS may not be needed, if no DSO STAs scheduled in the DSO TXOP requires padding. It is TBD whether an intermediate FCS can be avoided if a MIC is present.
Slide 14

## Slide 15: Reference
Slide 15
[1] 11-24/0209 Specification framework for TGbn
[2] 11-22/2204 Dynamic Subband Operation
[3] 11-23/1496 EMLSR Dynamic Subband Operation
[4] 11-23/2141 Further discussion on Dynamic Subband Operation
[5] 11-23/1892 Thoughts on Dynamic Subchannel Operation
[6] 11-24/0299 Initial Control Frame for Bandwidth Switching mode
[7] 11-24/0449 Considerations on Dynamic Subchannel Operation follow up
[8] 11-24/0493 Dynamic Channel Switch Operation