## Slide 1: ‘Chirp’—brief summary
Date: 2024-09-11
r0 (September 11, 2024): Initial version
This presentation provides a compressed summary of basic ‘chirp’ operation, in support of a straw poll to be run on Thursday, September 12, 2004
Reference documents: 24/0284r2, 24/1183r1

## Slide 2: Basic chirp operation in EDCA
A mode requiring essentially no spec work:
AP
STAn
4+ ms
STA1
4+ ms
STA1 contends as usual in EDCA
Transmits in its normal slot
Transmits only 4+ ms part short training
  Does not change EDCA states
(Intended) AP gains medium access later
Required functionality for AP?
(AP response could be optional)
If supported, AP that receives a chirp in an otherwise idle channel, with no pending BSS traffic, shall issue a poll within xx ms
  “Poll” can be any of several options
This is enough to show that the AP can detect a chirp
Chirps are detectable but signal no duration
We cannot rely on legacy devices deferring
(Cf. [3], which takes another approach)
Easiest to treat chirp in EDCA as informational
A basic “I’m here” signal that requests a poll
AP(s) can then poll as needed (on request)
  Instead of (each) AP having to poll regularly
From 24/1183r1 (slide 15)

## Slide 3: Summary and straw poll
Unscheduled UL access can be problematic
  Low Tx power STAs, and/or STAs at significantly extended range, esp. in dense environment
  Co-channel STAs will not defer, and intended receiver (below some Rx level) will discard
  In some cases, RTS will work, but requires no-interference window of 7 slots; failed RTSs increase latency, waste power, cause interference for others
  ‘Chirp’ provides method to alert AP that there is some STA that wishes to transmit (e.g., be triggered); no interference outside one slot; no repeated retransmissions
  Does not attempt to seize the medium (and so is independent of HiP EDCA and others)
Straw poll:
Do you support adding in TGbn a short common signal (enough for legacy 11g+ STAs to detect) that may be sent in EDCA whenever a STA may send a PPDU, fitting within one slot, and not requiring TGbn STAs to defer?