## Slide 1: Further Considerations For Generalized MAP Framework
Date: 20-Sep-2024
Authors:

## Slide 2: Abstract
In this contribution, we highlight our thoughts regarding the generalized framework of multi-AP coordination for 802.11bn.

## Slide 3: Introduction
  Multi-AP (MAP) Coordination is one of the key features considered for IEEE 802.11bn.
  MAP coordination enhances network efficiency by reducing interference and improving overall throughput by coordinating transmissions among multiple APs.
  MAP coordination improves coverage by ensuring seamless coverage and better signal quality through techniques like coordinated beamforming and joint transmission.
  MAP coordination reduces latency by minimizing delays and optimizing the timing of transmissions through coordinated mechanisms like TDMA and TWT.
  Different forms of MAP coordination have been discussed:
    Coordinated TWT
    Coordinated TDMA
    Coordinated Spatial Reuse
    Coordinated Beamforming
    Joint Transmission
    Coordinated Channel Usage
Notes: TWT: target wake time

## Slide 4: Introduction (2)
Camp-1:
Focuses on the operations and dynamics of specific MAP coordination modes.
Examples include coordinated TWT and TDMA.
Discusses the level of protection, advertisement of TWT SPs, TXOP allocations, and NAV protection rules.
Assumes MAP coordination primarily for managed/enterprise networks where APs are centrally controlled and typically from the same vendor, avoiding the need for discovery and negotiation steps.
Camp-2:
Encompasses all the discussions from Camp-1.
Additionally addresses discovery, negotiation, and modification/termination.
Emphasizes support for both enterprise and non-enterprise (residential) use cases.
Aims to provide tools for MAP coordination between APs from different vendors.
Highlights the need for a generalized framework to facilitate MAP coordination across diverse environments and scenarios.
Based on [1], two Camps in Multi-AP Coordination have been discussed.
Notes: SPs service period
TWT target wake time

## Slide 5: Recap (1)
Generalized MAP framework proposed in [1] where for different MAP coordination mechanisms, there can be some procedures/steps that are reusable for any mode of MAP coordination.
The proposed framework in [1] is illustrated in the following figure.

## Slide 6: Further Considerations
  In addition to the aforementioned parameters, further considerations can be taken into account for multi-AP coordination
  Backhaul capability
  User related information (link quality indication)
  System requirements (latency)
  Scheme selection availability

## Slide 7: Summary
  In 802.11bn, a generalized framework of MAP coordination is proposed in [1] where further considerations need to be taken into account such as backhaul capability, user related information, system requirements, scheme selection availability.

## Slide 8: References
[1]: “Requirements and functionalities for multi-AP framework”, IEEE 802.11-24/0511r1