## Slide 1: Usage of Expiration Time for LL Traffic
Date: 2024-05-05
Authors:
Name | Company | Address | Phone | Email
Liangxiao Xin | OPPO |  |  | v-xinliangxiao@oppo.com
Liuming Lu |  |  |  | 
Chaoming Luo |  |  |  | 
Wei Dong |  |  |  | 
Ning Gao |  |  |  | 
Yapu Li |  |  |  | 

## Slide 2: Introduction
A successful delivery of LL traffic is to deliver the LL traffic before its expiration time.
However, 802.11 network has different aspects of delay which hinders the successful delivery of LL traffic.
In this presentation, we discuss how expiration time of LL traffic can affect those types of delay.

## Slide 3: Delay of LL Data
Delay of LL data consists of
  Delay at transmitter: Queuing delay + contention (EDCA) / scheduling delay (TF)
  Delay over the air: Transmission delay + retransmission delay
  Delay at receiver: MAC processing delay (e.g., HOL blocking delay)
LL Data
BA
LL data arrives at the MAC of transmitter
① delay at transmitter
② delay over the air
③ delay at receiver
LL data arrives at the MAC of receiver
LL data leaves the MAC of receiver

## Slide 4: Definition of Expiration Time
Delay bound: the maximum time between the time LL data arrives at the MAC of transmitter and the time LL data arrives at the MAC of receiver
Expiration Time: the latest time that LL data leaves the MAC of receiver
LL Data
BA
LL data arrives at the MAC of transmitter
①
②
③
LL data arrives at the MAC of receiver
LL data leaves the MAC of receiver
Bound delay
Expiration time

## Slide 5: Definition of Expiration Time
Delay bound: the maximum time of ① + ②
Expiration Time:
  Option 1: the latest time that LL data leaves the MAC of receiver
  Option 2: the latest time that LL data arrives at the MAC of receiver
LL Data
BA
LL data arrives at the MAC of transmitter
①
②
③
LL data arrives at the MAC of receiver
LL data leaves the MAC of receiver
Bound delay
Expiration time

## Slide 6: Impact on Queueing Delay
Transmitter should prioritize the MSDUs with earlier expiration time in its queue
  Expiration time of MSDU: T1 < T2 < T3 < T4
Without Expiration Time
With Expiration Time
MSDU4
MSDU3
MSDU2
MSDU1
…
…
…
…
EDCAF of ACz
TIDx
TIDy
MSDU4: T4
MSDU1: T3
MSDU3: T2
MSDU2: T1
…
…
…
…
EDCAF of ACz
TIDx
TIDy
…
…

## Slide 7: Impact on Scheduling/Transmission Delay
AP should manage its TXOP resource to finish the transmission of MSDU before its expiration time.
  If a STA is not triggered in a TXOP  the delay is a TXOP time
  If a STA is not assigned to proper RU size  the delay is a PPDU time
TF
TB PPDU 1 (Expired!!)
TB PPDU 2
BA
TF
TB PPDU 1
BA
Expiration time of MSDUs in TB PPDU1
TF
TB PPDU 2
BA
Without Expiration Time
With Expiration Time

## Slide 8: Impact on HOL Blocking Delay
STA should pass MSDUs in the receive reordering buffer to the next MAC procedure before its expiration time even if the MSDU with SN=WinStartB (i.e., WinStartB = X) is not received.
  Assume there is only one SCS traffic stream in the TID in the figure below
Receive Reordering Buffer (Per TA/TID) |  | 
MSDUs | Received? | Expiration Time
SN = X | N | 
SN = X+ 1 | Y | T1
SN = X+ 2 | Y | T1
… | … | 
According to current spec, MSDUs (SN=X+1, X+2) cannot be passed to the next process since MSDU (SN=X) is not received.
However, MSDUs (SN=X+1, X+2) should be passed to the next process before expiration time T1
Next MAC process

## Slide 9: Observation
Expiration time of LL data has impact on the transmission of LL data at both transmitter side and receiver side.
  Both transmitter and receiver need to know the expiration time of LL data.
Transmitter can know the expiration time when the LL data arrives its MAC.
  For example, Expiration time = LL data arrival time at the MAC of transmitter + delay bound
However, receiver does not know the expiration time of LL data
  Receiver does not know the delay bound before it receives the LL data  AP has problem to assign proper RUs at proper time
  Receiver does not know when LL data arrives at the MAC of transmitter
Therefore, we need to design a mechanism to let receiver know the expiration time of LL data.

## Slide 10: Summary
In this contribution, we provide the definition of the expiration time of LL data
We discussed the impact of expiration time on the different types of delays during the transmission of LL data.

## Slide 11: SP1
Do you support to include the following in SFD?
  11bn shall define a mechanism to provide the expiration time of LL data to the receiver.