## Slide 1: 11bn signaling design for extra MCS, UEQM, 2xLDPC
Date: 2024-10-16
Authors:
Name | Affiliations | Address | Phone | Email
You-Wei Chen | Mediatek | 2840 Junction Ave. San Jose, CA, 95134 |  | You-Wei.Chen@mediatek.com
Jianhan Liu |  |  |  | 
Shengquan Hu |  |  |  | 
Thomas Pare |  |  |  | 

## Slide 2: Introduction
In Sept IEEE F2F meeting, multiple signaling design related motions [1] passed:
  UEQM patterns for Nss=2 , 3, 4
  1-bit EQM/UEQM indication
  UHR defines unequal modulation only for LDPC
  4 extra MCSs added to 11bn
Signaling design principles:
  It is preferred to minimizing the modifications from 11be.
  Clear and independent definition for each subfield such that implementation is simpler.
In this contribution, we would like to discuss the signaling design for MU-PPDU of 11bn with new features enabled, such as extra MCSs, UEQM, 2xLDPC, etc.

## Slide 3: Extra MCS signaling
With 4 additional MCSs added to 11bn, 4bits MCS table just does not work.
  Now we have 20 MCSs in total.
In [2], expanding 4bits MCS field in 11be to 5bits in UHR was proposed. The 5bits MCS subfield can be applied to non-MU-MIMO and MU-MIMO user fields.
In [3], a lookup table of NSS, MCS, and UEQM (similar concept as 11n) was proposed for non-MU-MIMO user field.
  This approach introduces unnecessary complexity for resolving signaling field.
We prefer to using 5bit for 11bn MCS table.
  5bits MCS tables can be applied for non-MU-MIMO and MU-MIMO user fields as well as user info field in a trigger frame.
  Existing MCSs (index 0-15) indication is same as 11be to avoid extra complexity.

## Slide 4: Recap: UEQM patterns
In Sept IEEE F2F meeting, 9 UEQM patterns [1] passed
  M is the constellation index
  M-1 refers to the constellation that is one order lower than M
  M-2 refers to the constellation that is two orders lower than M.
2SS | 1SS E-QAM
0 | (M/M-1)
1 | (M/M-2)
2 | 
3 | 
3SS | 1SS E-QAM
0 | (M/M/M-1)
1 | (M/M/M-2)
2 | (M/M-1/M-2)
3 | 
4SS | 1SS E-QAM
0 | (M/M/M/M-1)
1 | (M/M/M/M-2)
2 | (M/M/M-1/M-2)
3 | (M/M-1/M-1/M-2)

## Slide 5: UEQM pattern signaling
Total 9 UEQM patterns passed motion in Sept meeting.
If 1bit EQM/UEQM indication set to the UEQM mode, some options for UEQM pattern signaling were discussed:
  Option 1: 2bit UEQM pattern [4]. LDPC only and Tx BFed are assumed. Those bits can be repurposed to indicate UEQM patterns.
  Option 2: rephrase NSS subfield [2,4]
  Option 3: indicated by a mixed NSS, MCS, UEQM patterns [3].
We think Option 1 makes the most sense.
  3bits NSS subfield cannot accommodate total 9 UEQM patterns. An additional extension subfield is needed.
  Mixed table changes the interpretation from 11be.
  Option 1 minimizes the modifications from 11be and simple for implementation (unused entries shown in the previous slide can be reserved).

## Slide 6: 2xLDPC signaling
An explicit indication of using 2xLDPC or not has quite a few benefits.
  It provides transmitter the freedom and flexibility to use 2xLDPC, for example, for short packets, the transmitter may choose using 1x LDPC for other implementation considerations.
  It is easier for receiver to resolve the signaling on the use of 2x LDPC.
We propose to use 1 bit for 2xLDPC indication in non-MU-MIMO and MU-MIMO user fields as well as user info field in a trigger frame.
  For example, when Coding field indicates LDPC, then this bit set to 1: TX encodes LDPC using code size as 2x1944; set to 0: TX encode LDPC using code size of 648, 1296, or 1944.

## Slide 7: Non-MU-MIMO user field
We propose a harmonized signaling method. (color codes are applied for different features)
  5bits for MCS subfield (reserved bit 15 is used for MCS indication).
  Current consideration of max NSS=8, thus NSS subfield can be 3 bits.
  Bit 19 is used to indicate EQM/UEQM and reusing Bfed bit and Coding bit for UEQM pattern indications (2 bits).
    Note UEQM only applied to Bfed case and LDPC only.
  Adding 1bit (bit 22) for explicit indication of 2xLDPC
0 |  |  | 10 | 11 |  |  | 15 | 16 |  | 18 | 19 | 20 | 21 | 22
STA-ID |  |  |  | MCS |  |  |  | NSS |  |  | UEQM | Bfed | Coding | 2xLDPC
 |  |  |  |  |  |  |  |  |  |  |  | UEQM patterns |  | 

## Slide 8: MU-MIMO user field
We propose a harmonized signaling method. (color codes are applied for different features)
  5bits for MCS subfield.
  Current consideration of max NSS=8, thus spatial configuration can be 4 bits (like 11ax).
  Adding 1bit (bit 22) for explicit indication of 2xLDPC
0 |  |  | 10 | 11 |  |  | 15 | 16 |  |  | 19 | 20 | 21 | 22
STA-ID |  |  |  | MCS |  |  |  | Spatial Configuration |  |  |  | Res. | Coding | 2XLDPC

## Slide 9: Summary
  We review the existing proposals and propose our signaling designs for non-MU-MIMO, MU-MIMO user field.

## Slide 10: Straw Poll #1
Do you support the following signaling design for MU MIMO user info field?
  When Coding field indicates LDPC, then 2XLDPC indication:
    Bit22 set to 1: TX encode LDPC using code size as 2x1944
    Bit22 set to 0: TX encode LDPC using code size of 648, 1296, or 1944.
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22
STA-ID |  |  |  |  |  |  |  |  |  |  | MCS |  |  |  |  | Spatial Configuration |  |  |  | Res | Coding | 2XLDPC

## Slide 11: Straw Poll #2
Do you support the following signaling design for non-MU MIMO user info field?
  UEQM indication
    Bit19 set to 1: UEQM is applied, B20-21 are redefined to indicate UEQM patterns.
    Bit19 set to 0: EQM is applied. (B20 and B21 are Bfed and Coding bits)
  When Coding field indicates LDPC, then 2XLDPC indication:
    Bit22 set to 1: TX encode LDPC using code size as 2x1944
    Bit22 set to 0: TX encode LDPC using code size of 648, 1296, or 1944.
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22
STA-ID |  |  |  |  |  |  |  |  |  |  | MCS |  |  |  | MCS | NSS |  | 2xLDPC | UEQM | Bfed | Coding | 2xLDPC
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | UEQM patterns |  | 

## Slide 12: References
[1] TGbn Motions List - Part 1, 24/0171r15.
[2] Signaling for MCS and UEQM in 11bn, 24/1427r0
[3] UHR preamble signalling, 24/1461r0
[4] Signaling for UHR PPDU, 24/1411r0