## Slide 1: Collision detection mark for enhanced channel access
Date: 2024-10-15
Authors:

## Slide 2: Introduction
11bn aims at reducing 95th percentile of latency which is largely caused by channel access delay
Several channel access enhancements have been proposed for 11bn
  Collision avoidance enhancements (CW optimization [1], short contention phase [2])
  Short signal for channel access request (during contention [3], overlapped with PPDU [4])
  Defer signal to enable high priority contention [5-7]
ELR PPDU format has been proposed for 11bn
  ELR mark can facilitate robust packet detection and BSS identification [8-9]
Proposal: Collision resolution mechanism for low UL channel access delay
  Non-AP STA includes an PHY collision detection mark (CD mark) in preamble
  AP sends collision response granting access to least 1 colliding STA

## Slide 3: Issue of channel access delay
Additional channel access delay STA 1
Busy
Collisions result in exponential increase of channel access delay
  A collision leads to lost airtime when intended receiver cannot decode frames
  The colliding STAs increase CW to reduce collision probability resulting in additional delay
Busy
Busy
Busy
Timeout
Timeout
Busy
Busy
AP
STA 1
PPDU
Collision
2xCW -1
CW
x2
Busy
PPDU
STA 2
2xCW -1
CW
x2
PPDU
BAck
BAck
PPDU
STA 3
EIFS
AIFS
AIFS
AIFS
AIFS
PPDU
PPDU
BAck
BAck
Lost airtime
Additional channel access delay STA 2
AIFS
PPDU
…
PPDU
PPDU
BAck
BAck
Collisions
Increase CW
Exponential delay

## Slide 4: Proposal for fast collision resolution
Busy
Busy
Busy
PPDU
Non-AP STAs include a collision detection mark (CD mark) in preamble
  CD mark facilitates detection and identification of the transmitting non-AP STA
AP detects CD mark and sends collision response (CR)
  Indicates that a collision occurred and at least one non-AP STA with granted channel access
  Resolves the collision and avoids the exponential backoff for other non-AP STAs
Busy
Busy
AP
STA 1
Collision
Busy
PPDU
STA 2
CW
CW
x1
PPDU
BAck
BAck
PPDU
STA 3
AIFS
AIFS
PPDU
PPDU
BAck
BAck
Lost airtime
Additional channel access delay STA 2
AIFS
…
PPDU
PPDU
BAck
BAck
CD mark
CR
Busy
CD mark
CD mark
CD mark

## Slide 5: CD mark design as legacy modulated field (1/2)
Non-HT PPDU format:
ELR PPDU format:
  ELR PPDU format can also be used for enhanced collision detection
  Can define an ELR-CD mark to support collision detection
  ELR-CD mark would identify BSS (or BSS color) and transmitting STA
L-STF
L-LTF
L-SIG
NonHT-Data
CD mark
ELR-Data
ELR-SIG
L-STF
L-LTF
L-SIG
ELR-CD mark
RL-SIG
U-SIG
ELR-LTF
ELR-STF

## Slide 6: CD mark design as legacy modulated field (2/2)
CD mark signal
  Aim to design signals with low cross-correlation between STAs
    Consider that colliding PPDUs are not synchronized
  Use legacy 48 data tones and assign a group of tones to each STA
  Modulate tones with BPSK or QBPSK sequence
    Each contending STA should be uniquely identifiable
    BSS identification can be part of sequence
  Example:
    Create 8 groups of 6 tones each (can identify 8 STAs)
    Assume several CD mark length options
      4us : 1 symbol 3.2 us + CP of 0.8 us
      8us : 2 symbols 6.4 us + CP of 1.6 us
STA 2
STA 1
STA 3
STA 4
STA 5
STA 6
STA 7
STA 8
Guard
Guard
DC
CD mark symbol
Subcarriers
CP
Sym 1
Sym N
…
CD mark

## Slide 7: PPDU with CD mark enables identification of at least one colliding STA
Simulation set up
  Colliding PPDUs
    Format: Non-HT carrying RTS (20MHz)
    CD mark inserted after L-SIG in all PPDUs
  Impairments
    Time offset: Uniform dist. [0 9us]
    CFO: Uniform dist. [0 200Hz]
Probability of identifying at least one CD mark is comparable to L-STF packet detection
SNR = 5dB,
CD mark Len = 4us
SNR = 25dB,
CD mark Len = 4us
SNR = 5dB,
CD mark Len = 8us
SNR = 25dB,
CD mark Len = 8us

## Slide 8: PPDU with CD mark enables identification of at least one colliding STA with legacy STA collision
Simulation of collision between two PPDUs
  Two PPDUs carrying RTS (20MHz)
    One legacy PPDU (No CD mark included)
      Fixed TX power (to achieve 5 dB SNR at RX)
    One PPDU including CD mark
      Varying TX power
  Independent impairments on both PPDUs
    Time offset: Uniform dist. [0 9us]
    CFO: Uniform dist. [0 200Hz]
  Receiver synchronizes and decodes without prior knowledge
    Always checks if CD mark if present after L-SIG
One CD mark miss detection vs L-SIG decoding error
  6 to 10 dB SINR gain around 0.15 error rate
  60% to 70% lower error floor
CD mark Len = 4us
CD mark Len = 8us
6dB
10dB
~70%
~60%
L-STF
L-LTF
L-SIG
Data
CD mark
L-STF
L-LTF
L-SIG
Data
Random
TO_2
Random
TO_1

## Slide 9: Convergence of channel access enhancements for 11bn
Key approaches proposed for channel access enhancements
  Short contention phase [2]
  Short signal for channel access request [3]
  Defer signal to enable high priority contention [5-7]
Potential way forward
  CD mark can be an enabler for previous proposals on enhanced channel access
    Can support robust STA and BSS identification
    Can be used before or during a short contention phase
    Acts as a short channel access request with basic backward compatibility
    Can act as a defer signal

## Slide 10: Conclusion
Channel access enhancements are important for improving latency in 11bn
A collision detection mark in PPDU preamble can enable collision resolution with high reliability
  95% probability of AP identifying at least one colliding STA
  6 to 10 dB SINR gain compared to L-SIG decoding when colliding with legacy STAs
  AP can send a collision response to avoid exponential channel access delay
Propose to define a PPDU format for enhanced channel access
  Include a CD mark to identify transmitting STA within a collision

## Slide 11: References
[1] 11-24/0772r1 CSMA collision analysis
[2] 11-24/0773r1 CSMA with enhanced collision avoidance
[3] 11-24/1183r1 Low latency low collision low power medium access continued
[4] 11-24/0811r1 Overlapped indication for aperiodic low latency traffic
[5] 11-24/0840r0 hip EDCA proposal
[6] 11-24/0467r1 hip EDCA follow up legacy impact
[7] 11-24/1193r0 EDCA for high priority access
[8] 11-24/1478r2 ELR PPDU design
[9] 11-24/1571r1 Extended Long Range (ELR) Mark Symbol Design