## Slide 1: DRU Tone Plan for 20 MHz Distribution Bandwidth
Date: 2024-10-28
Authors:

## Slide 2: Abstract
In this contribution, we discuss several recommendations on DRU tone allocation
  We propose a tone allocation plan for 20 MHz based on the contribution in [1]

## Slide 3: DRU Tone Plan Recommendations
Recommendation 1: DRU tones should be shifted versions of each other to ensure they perform similarly in fading channels
  For example, 26-tone DRU 9 and 26-tone DRU 5 will perform differently as the corresponding tones are not shifted versions of other 26-tone DRUs for the tone plan in [1]
  Tone plans in [1] for 40 MHz and 80 MHz do not have this issue
Recommendation 2: DRU tone plan should avoid distortions by providing more DC tones given the available subcarriers
Data and pilot subcarrier indices for Distributed Tone RUs (DRUs) in a 20 MHz UHR PPDU [1] |  |  |  |  | 
DRU type | DRU index and subcarrier range |  |  |  | 
26-tone DRU i=1:9 | DRU1 [-120:9:-12, 6:9:114] | DRU2 [-116:9:-8, 10:9:118] | DRU3 [-118:9:-10, 8:9:116] | DRU4 [-114:9:-6, 12:9:120] | DRU5 [-112:9:-4, 5:9:113]
 | DRU6 [-119:9:-11, 7:9:115] | DRU7 [-115:9:-7, 11:9:119] | DRU8 [-117:9:-9, 9:9:117] | DRU9 [-113:9:-5, 4:9:112] | 
52-tone DRU i=1:4 | DRU1 26-tone [DRU1, DRU2] |  | DRU2 26-tone [DRU3, DRU4] |  | 
 | DRU3 26-tone [DRU6, DRU7] |  | DRU4 26-tone [DRU8, DRU9] |  | 
106-tone DRU i=1:2 | DRU1 26-tone [DRU1~4], [-3, 3] |  | DRU2 26-tone [DRU6~9], [-2, 2] |  | 
DRU2 = DRU1 + 4
DRU3 = DRU1 + 2
DRU4 = DRU1 + 6
DRU5 = ?
DRU6 = DRU1 + 1
DRU7 = DRU1 + 5
DRU8 = DRU1 + 3
DRU9 = ?
Mahmoud Kamel, InterDigital

## Slide 4: DRU Tone Plan Constraints
Recommendation 3: Pilot indices should be spread across the BW to exploit frequency diversity
  For instance, 106-tone DRU 2 can span from indices -119 to 112 whereas the pilot indices are from -56 to 103 for the tone plan in [1]
Pilot indices for DRU transmission over 20MHz [2] | 
DRU size | KdRxx_i
DRU26, i = 1:9 | { -111 15 }, { -89 37 }, { -100 26 }, { -78 48 }, { -67 59 }, { -56 70 }, { -34 92 }, { -45 81 }, { -23 103 }
DRU52, i = 1:4 | { -111 -89 15 37 }, { -100 -78 26 48 }, { -56 -34 70 92 }, { -45 -23 81 103 }
DRU106, i = 1:2 | { -111 -78 15 48 }, { -56 -23 70 103 }
Mahmoud Kamel, InterDigital

## Slide 5: Proposed 20 MHz DRU Tone Plan
Data and pilot subcarrier indices for Distributed Tone RUs (DRUs) in a 20 MHz UHR PPDU (Proposed) |  |  |  |  | 
DRU type | DRU index and subcarrier range |  |  |  | 
26-tone DRU i=1:9 | DRU1 [-121:9:-13, 5:9:113] | DRU2 [-117:9:-9, 9:9:117] | DRU3 [-119:9:-11, 7:9:115] | DRU4 [-115:9:-7, 11:9:119] | DRU5 [-113:9:-5, 13:9:121]
 | DRU6 [-120:9:-12, 6:9:114] | DRU7 [-116:9:-8, 10:9:118] | DRU8 [-118:9:-10, 8:9:116] | DRU9 [-114:9:-6, 12:9:120] | 
52-tone DRU i=1:4 | DRU1 26-tone [DRU1, DRU2] |  | DRU2 26-tone [DRU3, DRU4] |  | 
 | DRU3 26-tone [DRU6, DRU7] |  | DRU4 26-tone [DRU8, DRU9] |  | 
106-tone DRU i=1:2 | DRU1 26-tone [DRU1~4], [-4, 3] |  | DRU2 26-tone [DRU6~9], [-3, 4] |  | 
With the proposed tone plan in this contribution,
  The DRU1-DRU9 are shifted versions of each other
  Two more DC tones are available for 106-DRU as this tone plan ranges from -121 to -3 and 3 to 121, instead of -120 to -2 and 2 to 120 in [1]
Pilot tone indices are TBD
Mahmoud Kamel, InterDigital
DRU2 = DRU1 + 4
DRU3 = DRU1 + 2
DRU4 = DRU1 + 6
DRU5 = DRU1 + 8
DRU6 = DRU1 + 1
DRU7 = DRU1 + 5
DRU8 = DRU1 + 3
DRU9 = DRU1 + 7

## Slide 6: Conclusion
An enhanced version of the tone plan in [1] is proposed, the tone plan:
  Makes all the DRUs shifted versions of each other
  Allows for two extra DC tones

## Slide 7: SP 1
Do you agree that the tone indices of different DRUs with the same size and distribution bandwidth within the same operating bandwidth should be shifted versions of each other to ensure they perform similarly in fading channels?

## Slide 8: References
[1] 11/24-0468r2 DRU Tone Plan for 11bn, Mediatek
[2] 11/24-1230r1 Pilot Tone Design in DRU Transmission, Qualcomm
Mahmoud Kamel, InterDigital