## Slide 1
Discussion of AID use during the transition period – Buffered frame retrieval
Date: 2024-10-25
Authors:
Name | Affiliations | Address | Phone | Email
Carol Ansley | Cox Communications |  | +1-404-229-1672 | carol@ansley.com

## Slide 2
Abstract
This submission proposes to improve EDP operation during the transition period between epochs.

## Slide 3: Summary
During a transition period, the same AID might be assigned to two different non-AP MLDs from two different FA parameter sets.
This submission is based on 24/796 which proposed a method of handling that overlap, through a combination of restricting which FA parameter set is used during a transition period, suspending AID-related messaging during the transition period and/or using a spare bit in AID-related messages.

## Slide 4: Requirements
The following requirement deals with changing a STA’s AID.
11 | 11bi shall define a mechanism for a CPE Client and CPE AP to change the CPE Client’s AID to an uncorrelated new value in Associate STA State 4, without any loss of connection when the OTA MAC address of the CPE Client is changed.

## Slide 5: Summary of Transition Period assumptions
The transition period happens when a new EDP epoch begins.
A non-AP MLD is expected to be able to receive and correctly act upon frames with its new FA parameters, including new AID, once the transition period has begun.
The purpose of the transition period is to allow stored/buffered frames or frames subject to retransmission an opportunity to be transmitted versus just being deleted to clear the buffers.
This presentation looks at frames buffered while the non-AP MLD was in doze/power save.

## Slide 6: Example Interaction with AID tie-ins (1)
Multi-Link Traffic Indication element in Beacon frame includes Per-Link traffic Indication Bitmap with bit corresponding to AID of non-AP MLD = 1
PS-Poll frame sent by a STA affiliated with the non-AP MLD to retrieve buffered traffic
AP MLD sends the buffered traffic to the non-AP MLD over an appropriate link
AP MLD receives traffic for non-AP MLD currently in PS and stores it in a buffer
AP MLD
Non-AP MLD

## Slide 7: Details – PS-Poll frame
A PS-Poll frame is generated by a STA, which can be an affiliated STA that is part of a non-AP MLD.
The PS-Poll frame indicates that the transmitting STA has left PS mode and generally wants to retrieve any buffered traffic.
Since the PS-Poll frame is generated by the non-AP MLD’s affiliated STA, the STA can choose to which AID to use (and other FA parameters).

## Slide 8: Example Interaction with AID tie-ins (2)
Multi-Link Traffic Indication element in Beacon frame includes Per-Link traffic Indication Bitmap with bit corresponding to AID of non-AP MLD = 1
PS-Poll frame sent by a STA affiliated with the non-AP MLD to retrieve buffered traffic
AP MLD receives traffic for non-AP MLD currently in PS and stores it in a buffer
AP MLD
Non-AP MLD
Transition start
OLD AID
OLD AID or NEW AID
AP MLD sends the buffered traffic to the non-AP MLD over an appropriate link
OLD parameters or NEW parameters

## Slide 9: Details – PS-Poll frame – case 2
In case 2, the use of a new AID in the PS-Poll frame could allow an observer to link the old AID and the new AID.
If the non-AP STA affiliated with a non-AP MLD sends the PS-poll with an old AID, then the AP MLD needs to respond using the previous set of FA parameters (PN/SN, MAC address, etc.)
If the non-AP STA affiliated with a non-AP MLD sends the PS-poll with a new AID, then the AP MLD needs to respond using the new set of FA parameters (PN/SN, MAC address, etc.)

## Slide 10: Details – PS-Poll frame
Proposed text:
9.3.1.5 PS-Poll frame format
9.3.1.5.2 Non-BDT variant of the PS-Poll frame format
Tif the STA is not an EDP non-AP MLD affiliated STA, the Duration/ID field contains the AID value assigned to the STA transmitting the frame by the AP in the (Re)Association Response frame that established that STA’s current association, with the two MSBs set to 1.
If the STA is an EDP non-AP MLD affiliated STA, the STA shall use the AID value assigned to it in the current FA parameter set, unless a transition period is active. During a transition period, the STA shall use the AID used by the AP MLD in its most recent Multi-Link Traffic Indication element.

## Slide 11: Example Interaction with AID tie-ins (3)
Multi-Link Traffic Indication element in Beacon frame includes Per-Link traffic Indication Bitmap with bit corresponding to AID of non-AP MLD = 1
PS-Poll frame sent by a STA affiliated with the non-AP MLD to retrieve buffered traffic
AP MLD sends the buffered traffic to the non-AP MLD over an appropriate link
AP MLD receives traffic for non-AP MLD currently in PS and stores it in a buffer
AP MLD
Non-AP MLD
Transition start
OLD AID
OLD AID
OLD parameters or NEW parameters

## Slide 12: Details – PS-Poll frame – case 3
In case 3, the use of parameters from the new FA parameter set could allow an observer to correlate the old AID/MAC with the new AID MAC for that STA.
The AP MLD should respond with frames using the previous FA parameter set.

## Slide 13: Details – PS-Poll frame – case 3
Proposed text:
35.3.12.4 Traffic indication (modify paragraph 17 and add new 18th paragraph)
When an AP affiliated with an AP MLD receives a PS-Poll frame or a U-APSD trigger frame from a non-EDP non-AP STA affiliated with an associated non-AP MLD that is in power save mode, it shall transmit buffered BU(s) to the STA, if the buffered BU(s) are available and not discarded for implementation dependent reasons, otherwise, it may transmit a QoS Null frame.
When an AP affiliated with an AP MLD receives a PS-Poll frame or a U-APSD trigger frame from an EDP non-AP STA affiliated with an associated non-AP MLD that is in power save mode, it shall transmit buffered BU(s) to the STA using FA parameters for those buffered frames from the same FA parameter set as the STA used in the PS-Poll frame or U-APSD trigger frame, if the buffered BU(s) are available and not discarded for implementation dependent reasons, otherwise, it may transmit a QoS Null frame.

## Slide 14: Example Interaction with AID tie-ins (4)
Multi-Link Traffic Indication element in Beacon frame includes Per-Link traffic Indication Bitmap with bit corresponding to AID of non-AP MLD = 1
PS-Poll frame sent by a STA affiliated with the non-AP MLD to retrieve buffered traffic
AP MLD sends the buffered traffic to the non-AP MLD over an appropriate link
AP MLD receives traffic for non-AP MLD currently in PS and stores it in a buffer
AP MLD
Non-AP MLD
Transition start
NEW AID
NEW AID
NEW parameters
Based on MLO model, this should be fine.

## Slide 15: Details – PS-Poll frame – case 4
Case 4 should be covered by the texts already proposed.

## Slide 16: Straw Poll
Do you approve the direction taken in the proposed text updates for handling buffered frame retrieval?