## Slide 1
Discussion of AID obfuscation during the transition period
Date: 2024-10-24
Authors:
Name | Affiliations | Address | Phone | Email
Carol Ansley | Cox Communications |  | +1-404-229-1672 | carol@ansley.com

## Slide 2
Abstract
This submission proposes to improve EDP operation during the transition period between epochs.

## Slide 3: Summary
During a transition period, the same AID might be assigned to two different non-AP MLDs from two different FA parameter sets.
This submission is based on 24/796 and proposes a method of handling that overlap, through using a spare bit in Trigger frame messages.

## Slide 4: Requirements
The following requirement deals with changing a STA’s AID.
11 | 11bi shall define a mechanism for a CPE Client and CPE AP to change the CPE Client’s AID to an uncorrelated new value in Associate STA State 4, without any loss of connection when the OTA MAC address of the CPE Client is changed.

## Slide 5: AID Subfield discussion - background
In our discussions, we have targeted initially MLDs as the only devices to have access to MAC randomization during association.
A non-AP MLD gets a single AID to use for all of its associated non-AP STAs. (35.3.5.1 in TGbeD7.0. p550.26)
We have discussed reserving a block of AIDs for EDP non-AP MLDs so that the AP can rotate the AIDs while not disturbing the legacy STAs and legacy non-AP MLDs.
The issue is that during a transition period, we need space for 2x MAC addresses (not a problem) and 2x AIDs (a problem).
This problem is important because it will restrict the number of STAs and non-AP MLDs that an AP MLD can associate.

## Slide 6: Summary of Transition Period assumptions
The transition period happens when a new EDP epoch begins.
An MLD is expected to be able to receive and correctly act upon frames with its new AID once the transition period has begun.
The purpose of the transition period is to allow stored/buffered frames or frames subject to retransmission an opportunity to be transmitted versus just being deleted to clear the buffers.

## Slide 7: Discussion – Trigger frame
9.3.1.22 Trigger frame format
Based on the changes in TGbeD7.0, a Special User Info field is always present when an EHT User Info field is used. One of the reserved bits in that field can be used by the AP to indicate if the EHT AIDs of EDP non-AP STAs are from the current FA parameter set or from the previous set.

## Slide 8: Discussion – Trigger frame
Proposed text defines a currently reserved bit for use to indicate the presence of AIDs from the previous FA parameter set.
Because of the variety of Trigger frames and Trigger frame uses, this change would contain the needed text alterations to a single section versus trying to note the change in all of the different uses.
Alternatively, the AP could be instructed to only use AIDs from the current FA parameter set. This approach would use text similar to the NDP Announcement frame text added to 35.2.1.2.1, 35.2.2.1, and maybe other sections as appropriate.

## Slide 9: Discussion – Trigger Frame
Proposed text: (section 9.3.1.22.3 - change to table 9-90d and new text)
The format of the Special User Info field is defined in Figure 9-90d (Special User Info field format).
During an EDP transition period, the Transition Active subfield of the BA Control field is set to 1 if the AIDs in the AID TID Info subfield are from the FA parameters of the previous EDP epoch. The Transition Active subfield is set to 0 if the AIDs in the AID TID Info subfield are from the current EDP epoch.
NOTE—A Trigger frame can only contain AIDs for EDP non-AP MLDs from a single set of FA parameters.
Reserved
Transition Active
Reserved
Trigger Dependent User Info
1 2 variable
B37 B38

## Slide 10: Straw Poll
Do you support the proposal to change the format of the Special User Info field to allow indication of FA parameter set during transition period?