## Slide 1: Unified AutoEncoder based CSI Feedback in MU-MIMO for Next Generation WLANs
Date: 2024-10-31
Authors:

## Slide 2: Introduction
During the AIML TIC, we have explored various AIML use-cases and their feasibility for WLAN networks, which include [1]
    CSI feedback compression
    Distributed channel access
    Roaming enhancement
    Multi-AP coordination
In the topic of CSI feedback compression, studies have shown that AIML technique can significantly reduce the CSI feedback overhead and improve system throughput.
    Motivated by the fact that CSI may fall into different clusters due to similarity of nearby non-AP STA channels, [2] applies the unsupervised learning, i.e., K-means algorithm, to classify the CSI angle vectors.
    Using the fact that any unitary matrix can be expressed by multiplication of two unitary matrices, i.e., V = V1 V2, a dual CSI feedback scheme was proposed in [3], which decomposes a large sized CSI into a sub-band CSI (V1) using the codebook from K-means algorithm and a sub-carrier CSI (V2) using the Givens rotation.

## Slide 3: Introduction
Another unsupervised learning technique, Deep Neural Network AutoEncoder (DNN-AE) can also be applied to CSI feedback compression [4],[5],[6].
    Experimental results show that in SU-MIMO the algorithm reduces the feedback overhead by more than 50% and significantly increases the network throughput.
However, studies covered in AIML TIC have limitations in that the performance gains were shown only in SU-MIMO.
Compared with SU-MIMO,
    MU-MIMO performance is very sensitive to CSI accuracy to support the inter-user interference cancellation.
    And, thus it requires larger CSI feedback overhead (with inclusion of the MU-exclusive delta-SNR information)
      e.g.) Quantization bits for {} is {9, 7} for MU and is {6, 4} for SU, respectively.
    In addition, more frequent sounding transmission is required for MU-MIMO.
Therefore, the issue of CSI feedback compression is more critical in MU-MIMO rather than SU-MIMO.

## Slide 4: Main Contributions
In this contribution, we investigate the DNN-AE based CSI feedback scheme, focusing on MU-MIMO with following objective
  Minimizing CSI feedback overhead while maintaining packet error rate (PER) performance.
The key advantages the proposed scheme are
  A single unified DNN-AE can be applied universally to different combinations of CSI types, bandwidth, transmit and receive antenna numbers, MIMO-modes.
    CSI type: , , and SNR
    BW: 20/40/80/160/320 MHz
    Transmit and receive antenna number: 4x2, 8x2, 16x2, etc.
    MIMO mode: SU-MIMO / MU- MIMO
  This structure not only alleviate burden on training efforts but also reduce HW complexity.

## Slide 5: Recap: Principle of DNN-AE
DNN-AE
  DNN-AE is an unsupervised learning based neural network to reduce data dimension, which is composed of Encoder and Decoder.
    Encoder transforms the input data to a compressed representation.
    Decoder reconstructs the input data from the compressed representation.

## Slide 6: Conventional DNN-AE based CSI Feedback
Two Separate DNN-AEs
  Different DNN-AEs are designed for and angles respectively.
    For ’s DNN-AE, node configuration is 52 8 3 8 52.
    For ’s DNN-AE, node configuration is 52 4 8 4 52.
  To avoid unbiased training, experimentally determined pre-processing is employed such as [7]
f

## Slide 7: Conventional DNN-AE based CSI Feedback
Limitation
  The node configurations of the DNN-AE was designed to optimized to a specific IEEE 802.11 protocol.
    E.g., 20MHz bandwidth, 312.5 KHz subcarrier spacing in IEEE 802.11ac.
  This means another optimization process is required according to variation of environment such as 80MHz bandwidth and 78.125 KHz subcarrier spacing used in IEEE 802.11ax/be.
    This increases the engineering efforts for training.
  Two separate DNN-AEs increase the HW size and it can be a problem, especially in non-AP STAs with a limited form factor.

## Slide 8: Proposed DNN-AE based CSI Feedback
A Single Unified DNN-AE
  The proposed unified DNN-AE is designed on top of the existing Givens rotation based CSI compression structure for backward compatibility.
    Subset of beamformees may feed back CSI with existing way when there is no need to compress the CSI via DNN-AE. (e.g. to maintain CSI accuracy)
  Various sizes of CSI vector () are reshaped into a common matrix form ().
    where is the number of subcarriers for which CSI is sent back to the AP, which is a function of the bandwidth and subcarrier grouping ()
      E.g.) is 250 for = 4 in IEEE 802.11be under 80MHz.
    and and is set as .
  In order to accommodate various CSI types (e.g., , , and SNR), a generalized pre-processor is incorporated in a closed-form.
    The function is a continuous bijective function where the function values in the first and the last value of the domain are similar.
    The detail description of the generalized pre-processor will be shown in the following contribution.

## Slide 9: Proposed DNN-AE based CSI Feedback
The overall structure of the transceiver incorporating with the unified DNN-AE is depicted in figure below.
  Note that in order to perform the corresponding post-processing in decoder, pre-processing information is required to be fed back to beamformer.

## Slide 10: CSI Feedback Overhead Analysis
Existing Method
    (Number of subcarriers) (Number of angles for each subcarrier)
    (Number of bits for each angle),
Proposed Method
    (Number of output nodes in DNN-AE) (Number of angles for each node)
    (Number of bits for each angle) + (Number of bits for pre-processing info.),
Parameters | Description
 | Number of bits to quantize defined in existing 802.11 WLAN
 | Number of bits to quantize defined in existing 802.11 WLAN
 | Number of bits to quantize Delta SNR defined in existing 802.11 WLAN
 | Number of subcarriers defined in existing 802.11 WLAN
 | Number of bits to quantize defined in DNN-AE
 | Number of bits to quantize defined in DNN-AE
 | Number of bits to quantize Delta SNR defined in DNN-AE
 | Number of output nodes in DNN-AE
 | Number of angles per subcarrier
 | Number of bits for pre-processing information
 | Number of spatial streams
Parameters | Description
 | Number of bits to quantize Delta SNR defined in existing 802.11 WLAN
 | Number of subcarriers defined in existing 802.11 WLAN
 | Number of bits to quantize Delta SNR defined in DNN-AE
 | Number of output nodes in DNN-AE
 | Number of angles per subcarrier
 | Number of bits for pre-processing information
 | Number of spatial streams

## Slide 11: Simulation Results
Parameters
Class | Parameters | Description
IEEE 802.11be Parameters | Frame format | EHT-MU
 | MIMO mode | MU-MIMO
 | Number of transmit antennas ( | 4
 | Number of receive antennas ( | 2
 | Number of spatial streams ( | 1
 | Number of users in MU-MIMO | 4
 | Bandwidth (BW) | 80 MHz
 | Feedback subcarrier group ( | 4
 | NDPA format | NonHT-DUP
 | CBR format | EHT-MU, 1ss, MCS4
DNN-AE Parameters | Nodes configuration | 64 x 32 x 16 x 32 x 64
 | Number of layers | 5
 | Activation function | Relu
 | Optimizer | Adam
 | Number of bits for () | 10
 | Number of bits for () | 12
 | Number of bits for Delta-SNR () | 7
 | Number of output nodes () | 64
 | Number of bits for pre-processing () | 1
Class | Parameters | Description
IEEE 802.11be Parameters | Frame format | EHT-MU
 | MIMO mode | MU-MIMO
 |  | 4
 |  | 2
 |  | 1
 | Number of users in MU-MIMO | 4
 | Bandwidth (BW) | 80 MHz
 |  | 4
 | NDPA format | NonHT-DUP
 | CBR format | EHT-MU, 1ss, MCS4
DNN-AE Parameters | Nodes configuration | 64 x 32 x 16 x 32 x 64
 | Number of layers | 5
 | Activation function | Relu
 | Optimizer | Adam
 |  | 10
 |  | 12
 |  | 7
 |  | 64
 |  | 1

## Slide 12: Simulation Results
It can be seen that the DNN-AE, which has not been pre-processed, suffers from about 3.5dB degradation due to the loss of compression accuracy.
  However, the proposed unified DNN-AE shows almost the same PER performance as the target performance with about 50% reduction in CSI feedback overhead in the compressed beamforming report (CBR).

## Slide 13: Simulation Results
To evaluate the throughput considering the time required for CSI feedback, i.e., , the throughput is calculated as follows.
    Throughput (bps/Hz) =
    where
  The proposed unified DNN-AE based method can provide a throughput increase of about 30%, which satisfies the goal of UHR WLANs [8].

## Slide 14: Summary
In this contribution, we presented a unified DNN-AE design for CSI feedback for MU-MIMO in next-generation WLANs.
  In order to apply a single DNN-AE universally to various types of system configurations, a generalized pre- (and post-) processor was integrated into DNN-AE in a closed-from.
  This design not only alleviates training efforts (and HW size) but also has the advantages of improving the compression accuracy of the DNN-AE.
Link level simulation results have shown that the proposed unified DNN-AE based CSI feedback method can reduce the CSI feedback overhead by more than 50% with negligible PER performance degradation in MU-MIMO.

## Slide 15: Reference
[1] IEEE P802.11, “IEEE 802.11 AIML TIG Technical Report Draft,” IEEE AIML TIG/0987r23, Nov. 2023.
[2] M. Deshmukh, Z. Lin, H. Lou, M. Kamel, R. Yang, I. Guvenc, “Intelligent Feedback Overhead Reduction (iFOR) in Wi-Fi 7 and Beyond,” in Proc. IEEE Veh. Technol. Conf. (VTC), Jun. 2022.
[3] E. Jeon, M. Kim, M. Ahn, J. Kim, S. Kim, I. Kim, and J. Kim, “Machine Learning Aided CSI Feedback for Smooth Beamforming in Next Generation WLANs,” in Proc. IEEE Veh. Technol. Conf. (VTC), Jun. 2023.
[4] 802.11-23/0275r2, “Improved AIML Enabled Index Based Beamforming CSI Feedback Schemes,” May 2023.
[5] 802.11-23/0290r2, “Study on AI CSI Compression,” Sep. 2023.
[6] 802.11-23/0755r0, “AIML Assisted Complexity Reduction For Beamforming CSI Feedback Using Autoencoder,” May 2023.
[7] P. K. Sangdeh, H. Pirayesh, A. Mobiny, H. Zeng, “LB-SciFi: Online Learning-Based Channel Feedback for MU-MIMO in Wireless LANs,” in Proc. IEEE International Conference on Network Protocols (ICNP), Oct. 2020.
[8] IEEE P802.11 Wireless LANs, “Joint Proposal: UHR Proposed PAR,” doc.: IEEE 802.11-23/0480, Jul. 2023.