## Slide 1: Consideration on 11bn Trigger frame for PHY Signaling
Date: 2024-11-10
Authors:
Name | Affiliation | Address | Phone | Email
Dongguk Lim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | dongguk.lim@lge.com
Eunsung Park |  |  |  | Ensung.park@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Insik Jung |  |  |  | insik0618.jung@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Sanggook Kim |  | 10680 Treena St San Diego, CA 92131 |  | sanggook.kim@lge.com
November. 2024

## Slide 2: Introduction
In the previous meeting, we agreed to apply the new MCS and defined the signaling to indicate the UEQM transmission.
  Additionally, some related information ,i.e., UEQM pattern and coding for UEQM was discussed.
Since not only UEQM and new MCS but also other 11bn features can be considered in TB PPDU, we should consider how to configure the 11bn Trigger frame for efficient UL transmission.
In this contribution, we consider the design of the 11bn Trigger frame by taking into account the various 11bn PHY features.

## Slide 3: Trigger frame for 11bn (1/3)
Considering the new features defined in 11bn, the Trigger frame for 11bn should include some information for those features.
  For example, the common info field and user info field of the trigger frame for 11bn may be composed differently from the EHT trigger frame.
Therefore, for transmitting information of 11bn features, we should consider the method to distinguish a new variant of the trigger frame by non-AP UHR STA and for that, we can consider the following options.
  Option 1: Define a new indication bit in common info field
  Option 2: Use PHY version identifier in the special user info field.

## Slide 4: Trigger frame for 11bn (2/3)
Option 1: Define a new indication bit in common info field
  We can consider assigning 1 bit to the indication of the UHR variant of the trigger frame.
    For example, B56 can be assigned for this indication.
  Similar to the method for indication of the HE/EHT variant, this can be used with B54 and B55.
    For example, the same combinations of B54 and B55 to indicate the EHT variant can be reused with B56 to indicate the UHR variant.
      The Details of the combination for indication need further discussion.
  Since the UHR variant is indicated by using additional signaling, we can design some information in the common info field and user info field for the UHR variant.

## Slide 5: Trigger frame for 11bn (3/3)
Option 2: Use PHY version identifier in the special user info field
  The common info field of the UHR variant is composed same to it of the EHT variant because the classification of which variant is used is determined with the special user info field.
    The B54 and B55 of the common info field of the UHR variant are set to equal values as defined in 11be spec, meanwhile, the PHY version identifier field in the special user info field for the UHR variant is set to 1.
    Thus, information for 11bn features can be included in the special user info field and UHR variant user info field.
  This is a simple way to identify the trigger frame of the UHR variant without additional signaling and complexity due to the reuse of the EHT variant common field. So, we prefer option 2 to identify the UHR variant.

## Slide 6: Information for UHR features
The consideration of required bits for signaling of UHR features
  EQM/UEQM indication : 1 bit
  UEQM pattern : 2 bits
    In [1], it was proposed that the UEQM pattern is indicated differently according to NSS.
  MCS : 5 bits
    To accommodate the new MCS, current MCS field should be extended[2].
  Information related to DRU[3]
    DBW : 2 bits
    CSD indication : 3 bits
  We assumed that the use of DRU is indicated by RU allocation.
  2x LDPC : 1 bits
Note: even though some information is not defined yet and needs more discussion, we consider all possible information here.

## Slide 7: Signaling of the UHR features (1/4)
Depending on the features used for TB PPDU, the bits for signaling of UHR features can be changed.
So, we may consider that the UHR variant user info field consists differently according to the used UHR features for TB PPDU.
  If RRU&EQM are used
    It does not need related information for DRU as well as UEQM pattern information .
    As proposed in [2], since Max NSS may be set to 8, the Starting Spatial Stream field can be reconfigured as 3bits and the remaining 1bit can be used for defining of the UEQM/EQM indication.
    The UHR variant user info field is defined based on the EHT variant user info field
    The UL Target Receive power field may consist of 6 bits to ensure a consistent format of various UHR variant user info fields. For that, we need further discussion.
  Example of UHR variant user info field for RRU&EQM
AID12 | RU Allocation | UL FEC Coding Type | UL UHR- MCS | EQM/UEQM indication | Starting Spatial Stream | Reserved | Number Of Spatial Streams | UL Target Receive Power | PS160 | Trigger Dependent User Info
Bits: 12 | 8 | 1 | 5 | 1 | 3 | 1 | 2 | 6 | 1 | variable
      Note : it is assumed no 2x LDPC indication.

## Slide 8: Signaling of the UHR features (3/4)
  If RRU&UEQM are used
    We defined that LDPC is only used on UEQM, so the UL FEC Coding Type field is reserved or set to fix value.
      To retain consistency with the EQM case, it may be better to keep the 1bit as the UL FEC Coding Type.
    Since MU-MIMO may not be used in the UEQM, the Starting Spatial Stream field can be reconfigured to indicate the UEQM pattern.
    Based on the UHR variant user info field of RRU&EQM, the UHR variant user info field for RRU&UEQM can be configured as below.
    Example of UHR variant user info field for RRU&UEQM
AID12 | RU Allocation | UL FEC Coding Type /Reserved | UL UHR - MCS | EQM/UEQM indication | UEQM pattern | Reserved | Number Of Spatial Streams | UL Target Receive Power | PS160 | Trigger Dependent User Info
Bits: 12 | 8 | 1 | 5 | 1 | 2 | 2 | 2 | 6 | 1 | variable
      Note : it is assumed no 2x LDPC indication.

## Slide 9: Signaling of the UHR features (2/4)
  If DRU&EQM are used
    It was defined that Max NSS = 2 and MU-MIMO is not supported in the DRU transmission.
      So, in this case, the Number Of Spatial Streams is not needed and can be reconfigured for information on DRU such as DBW and CSD indication.
      Also, the NSS field can be reduced to one bit.
    Based on the UHR variant user info field of the previous slide, the UHR variant user info field for EQM&DRU can be configured as below.
      Here, we don’t address the 2x LDPC, and the CSD indication can be indicated by the reserved field and some bits from the UL Target Receive Power field as described in [3]
    Example of UHR variant user info field for EQM&DRU
AID12 | RU Allocation | UL FEC Coding Type | UL UHR - MCS | EQM/UEQM indication | CSD | DBW | Number Of Spatial Streams | UL Target Receive Power | PS160 | Trigger Dependent User Info
Bits: 12 | 8 | 1 | 5 | 1 | 3 | 2 | 1 | 6 | 1 | variable

## Slide 10: Signaling of the UHR features (4/4)
  If DRU&UEQM are used
    By considering the support of both DRU and UEQM, we can control the NSS and UEQM pattern.
      Based on the defined parameters of each UEQM and DRU, NSS is fixed as 2 when both UEQM and DRU are applied. Thus, NSS can be omitted
      Also, the UEQM pattern can be reconfigured to one bit because of only the use of 2SS in this case.
      For the indication of more features, the reserved bits and some bits from UL Target Receive Power can be used as in [3].
    Example of UHR variant user info field for DRU&UEQM
AID12 | RU Allocation | UL FEC Coding Type /Reserved | UL UHR - MCS | EQM/UEQM indication | CSD | DBW | UEQM pattern | UL Target Receive Power | PS160 | Trigger Dependent User Info
Bits: 12 | 8 | 1 | 5 | 1 | 3 | 2 | 1 | 6 | 1 | variable
      Note : it is assumed no 2x LDPC.

## Slide 11: UHR variant user info field
Comparison of contents of UHR variant user info field
DRU&UEQM | 
Fields | Bits
AID12 | 12
RU Allocation | 8
UL FEC Coding Type /Reserved | 1
UL UHR - MCS | 5
EQM/UEQM indication | 1
CSD | 3
DBW | 2
UEQM pattern | 1
UL Target Receive Power | 6
PS160 | 1
RRU&EQM | 
Fields | Bits
AID12 | 12
RU Allocation | 8
UL FEC Coding Type | 1
UL UHR - MCS | 5
EQM/UEQM indication | 1
Starting Spatial Stream | 3
Reserved | 1
Number Of Spatial Streams | 2
UL Target Receive Power | 6
PS160 | 1
RRU&UEQM | 
Fields | Bits
AID12 | 12
RU Allocation | 8
UL FEC Coding Type /Reserved | 1
UL UHR - MCS | 5
EQM/UEQM indication | 1
UEQM pattern | 2
Reserved | 2
Number Of Spatial Streams | 2
UL Target Receive Power | 6
PS160 | 1
DRU&EQM | 
Fields | Bits
AID12 | 12
RU Allocation | 8
UL FEC Coding Type | 1
UL UHR - MCS | 5
EQM/UEQM indication | 1
CSD | 3
DBW | 2
Number Of Spatial Streams | 1
UL Target Receive Power | 6
PS160 | 1

## Slide 12: Summary
We have investigated the two methods to identify the UHR variant Trigger frame.
  In terms of signaling overhead and complexity, we prefer to identify the UHR variant by using the PHY version identifier in the special user info field.
    In the UHR variant, the PHY version identifier is set to 1.
Considering the signaling of the UHR features, we have also investigated how to configure the UHR variant user info field.
  We have looked into the required signaling bits for information on UHR features in the UHR variant user info fields.
  Depending on the UHR features used, the UHR variant user info field can be configured differently.

## Slide 13: Straw poll 1
Do you agree to add the following text to the 11bn SFD?
  TGbn defines the UHR variant of Trigger frame.
  Y/N/A

## Slide 14: Straw poll 2
Do you agree to add the following text to the 11bn SFD?
  The UHR variant of Trigger frame includes the special user info field.
    PHY Version Identifier subfield in special user info field is used for identifying for UHR variant of trigger frame and is set to 1.
  Y/N/A

## Slide 15: Straw poll 3
Do you agree to add the following text to the 11bn SFD?
  The UHR variant of Trigger frame includes the UHR variant user info field.
    It has the same length as the EHT variant user info field.
  Y/N/A

## Slide 16: Straw poll 4
Do you agree to add the following text to the 11bn SFD?
  For a UHR TB PPDU transmission, there exists a 1-bit EQM/UEQM indication in a user info field for UHR variant of Trigger frame.
  Y/N/A

## Slide 17: Straw poll 5
Do you agree to add the following text to the 11bn SFD?
  For a UHR TB PPDU transmission, there exists a 5-bit UL UHR MCS in a user info field for UHR variant of Trigger frame.
  Y/N/A

## Slide 18: Straw poll 6
Do you agree to add the following text to the 11bn SFD?
  When RRU and EQM are used, the UHR variant user info field consists of the following fields.
    Other fields are TBD.
  Y/N/A
Fields | Bits
AID12 | 12
RU Allocation | 8
UL FEC Coding Type | 1
UL UHR - MCS | 5
EQM/UEQM indication | 1
Starting Spatial Stream | 3
Number Of Spatial Streams | 2
UL Target Receive Power | TBD
PS160 | 1

## Slide 19: Straw poll 7
Do you agree to add the following text to the 11bn SFD?
  When RRU and UEQM are used, the UHR variant user info field consists of the following fields.
    Other fields are TBD.
  Y/N/A
Fields | Bits
AID12 | 12
RU Allocation | 8
UL FEC Coding Type | 1
UL UHR - MCS | 5
EQM/UEQM indication | 1
UEQM pattern | 2
Number Of Spatial Streams | 2
UL Target Receive Power | TBD
PS160 | 1

## Slide 20: Reference
[1] 11-24-0474-03-00bn-uhr-unequal-modulation-pattern-and-new-mcs
[2] 11-24-1427-01-00bn-Signaling for MCS and UEQM in 11bn
[3] 11-24-1753-00-00bn-Signaling for DRU in Trigger frame Follow-up