## Slide 1: Antenna selection for UHR
Date: 2024-11-04
Authors:
Name | Affiliations | Address | Phone | email
Ross Jian Yu | Huawei |  |  | ross.yujian@huawei.com
Wei Ruan |  |  |  | 
Ming Gan |  |  |  | 

## Slide 2: Introduction
Smart antennas have been widely used in Wi-Fi networks to provide the following benefits [1]:
  Better coverage
  Higher throughput
  Higher reliability
This aligns very well with UHR PAR.
An antenna array is made up of a series of small antennas. Each small antenna can be an omnidirectional antenna or a directional antenna. One example is shown as follows [1].

## Slide 3: Antenna selection in 11n
802.11n defines antenna selection procedure that supports up to eight antennas and up to four RF chains.
Transmit ASEL
Receive ASEL
TXASSI: transmit antenna selection sounding indication
TXASSR: transmit antenna selection sounding request
RXASSI: receive antenna selection sounding indication
RXASSR: receive antenna selection sounding request
ASEL: antenna selection
Channel reciprocity

## Slide 4: Antenna selection in 11n
11n ASEL procedure only applies only to HT and non-HT PPDUs. With smart antennas applied more widely on WLAN devices, including both APs and non-AP STAs (e.g., high-end mobile phones), it is beneficial to extend 11n ASEL to 11bn.
For 11bn, we intend to design the procedure based on 11n procedure to simplify the procedure.

## Slide 5: Proposed Tx antenna selection for 11bn
The proposed transmit antenna selection procedure is as follows.
The procedure can be extended to trigger based procedure to enable Tx ASEL with multiple STAs.

## Slide 6: Proposed Rx antenna selection for 11bn
The proposed receive antenna selection procedure is as follows.
The procedure can be extended to trigger based procedure to enable Rx ASEL with multiple STAs.

## Slide 7: ASEL signaling in 802.11n
The ASEL signaling is carried in HT variant of HT control field. Details info of ASEL Command and ASEL Data can be found in the appendix.

## Slide 8: ASEL signaling in 802.11bn
For 802.11bn, the related signaling can be in NDPA frame, A-control subfield, and UHR-SIG field of a UHR sounding PPDU. Details can be further discussed.

## Slide 9: Summary
In this contribution, we propose to enable ASEL in 802.11bn.
Details can be further discussed.

## Slide 10: Reference
https://e.huawei.com/en/material/networking/wlan/f5fc602b529944c09f61e51492a20216
IEEE P802.11 Revme D7.0

## Slide 11: Appendix – Table 9-20—ASEL Command and ASEL Data subfields
ASEL Command | Interpretation of ASEL Command | ASEL Data
0 | Transmit Antenna Selection Sounding Indication (TXASSI) | Number of remaining sounding PPDUs to be transmitted See NOTE
1 | Transmit Antenna Selection Sounding Request (TXASSR) or Transmit ASEL Sounding Resumption | 0 when the command is Transmit ASEL Sounding Request A number in the range 1 to 15, the number being the number of the first sounding PPDU to be transmitted when the command is Transmit ASEL Sounding Resumption, where 0 corresponds to the first sounding PPDU in the original ASEL training sequence
2 | Receive Antenna Selection Sounding Indication (RXASSI) | Number of remaining sounding PPDUs to be received See NOTE
3 | Receive Antenna Selection Sounding Request (RXASSR) | Number of sounding PPDUs required
4 | Sounding Label | Sequence number of the sounding PPDU corresponding to a channel state information (CSI) frame in ASEL feedback
5 | No Feedback Due to ASEL Training Failure or Stale Feedback | The number of the first sounding PPDU that was not received properly, where 0 corresponds to the first sounding PPDU in the ASEL training sequence, or 0 if no sounding PPDUs were received properly, or 0 if this is a request for a full retraining sequence
6 | Transmit Antenna Selection Sounding Indication requesting feedback of explicit CSI (TXASSI-CSI) | Number of remaining sounding PPDUs to be transmitted See NOTE
7 | Reserved | Reserved