## Slide 1: Timing Issue for AMP
Date: 2024-11-11
Authors:
Name | Affiliation | Address | Phone | Email
Yinan Qi | OPPO |  |  | v-qiyinan@oppo.com
Weijie Xu |  |  |  | 
Chuanfeng He |  |  |  | 
Doc.: IEEE 802.11-24/1782r0
November 2024

## Slide 2: Abstract
In this contribution, we discuss the timing issues including timing inaccuracy, drifting, etc.
Doc.: IEEE 802.11-24/1782r0

## Slide 3
DLUL Transition
  Active Tx device
    Normal timing with lower processing capability
    Transition time components: propagation, MAC processing, etc.
    Different/separate DL/UL PPDUs
  Backscattering
    Rx  backscattering
    Different/separate DL/UL PPDUs
    Different/separate fields within one PPDU
      DL: sync+SIG+data
      UL: excitation containing sync+data
      Transition time component: propagation, PHY/MAC processing, e.g., UL configuration in SIG [1], RF circuit switching, etc.
      Critical for AMP devices due to its simplicity and limited processing capability
Yinan Qi (OPPO)
Slide 3
Doc.: IEEE 802.11-24/1782r0
November 2023

## Slide 4
ULDL Transition
  Active Tx device
    Normal timing with lower processing capability
    Transition time components: propagation, MAC processing, etc.
    Different/separate UL/DL PPDUs
  Backscattering
    Backscattering  Rx
    Different/separate UL/DL PPDUs
    Different/separate fields within one PPDU
      UL: excitation containing sync and data
      DL: Sync+SIG+data
      Transition time component: propagation, PHY/MAC processing from AP perspective, RF circuit switching, etc.
      Not critical for AP
Yinan Qi (OPPO)
Slide 4
Doc.: IEEE 802.11-24/1782r0
November 2023

## Slide 5
Distributed PPDU
  Legacy preamble
    From AP/ energizer
  AMP segment
    Excitation from AP/energizer
    Containing Sync + data
  Timing inaccuracy
    AMP device: When to start backscattering after legacy preamble?
      May start earlier or later
      Energizer may send sync to help AMP devices
    AP: when to receive backscatter signal from AMP device?
      Can be based on UL sync
Yinan Qi (OPPO)
Slide 5
Doc.: IEEE 802.11-24/1782r0
November 2023
UL Sync+ UL Data
Preamble
SYNC
Excitation

## Slide 6
Drifting
  Duration of one PPDU
    Duration of one DL PPDU is not limited
      The combination of excitation+DL Tx can be repeated multiple times
    Timing inaccuracy can be accumulated from beginning to the end of a single PPDU due to drifting
    Not a problem for active Tx but essential for backscattering
    Drifting rates can be different for different AMP device types
    Drifting rate should be defined
  TDM
    Timing inaccuracy accumulated from time slot 1 to time slot N
    Both slot duration and number of TDM slots are limited by drifting without re-sync
Yinan Qi (OPPO)
Slide 6
Doc.: IEEE 802.11-24/1782r0
November 2023
Excitation
Preamble
SYNC
SIG
Data
WPT + DL + charging/backscattering for UL and WPT + DL + charging/backscattering for UL…
Excitation
SYNC
SIG
Data
Excitation

## Slide 7
PPDU
  Long PPDU
    Not preferred for non-standalone deployment where legacy devices exist since channel can be occupied for long time
    Can be useful for standalone deployment without legacy devices
    Sync is not necessarily inserted in front of every data field
      Trade-off between signalling overhead and synchronization
    Multiple sync within one PPDU
      Where to insert Sync depends on the length of one PPDU and drifting rate
Yinan Qi (OPPO)
Slide 7
Doc.: IEEE 802.11-24/1782r0
November 2023
Excitation
Preamble
SYNC
SIG
Data
Excitation
SYNC
SIG
Data
Excitation
Excitation
Preamble
SYNC
SIG
Data
Excitation
SIG
Data
Excitation

## Slide 8
TDM
  Multiple time slots
    Timing inaccuracy may be accumulated due to drifting of the clock
    Re-sync is needed per n time slots
    n depends on the trade-off between signalling overhead and TDM efficiency
Yinan Qi (OPPO)
Slide 8
Doc.: IEEE 802.11-24/1782r0
November 2023
Time Slot 1 with Sync
Time Slot 2 without Sync
Time Slot 3 with Sync
Time Slot 4 without Sync
Timing inaccuracy

## Slide 9
Summary
  In this submission, we discussed the timing issues due to inaccuracy of the AMP clock covering the following aspects:
    Transition time
    Synchronization requirement for backscattering
    Clock drifting and its impacts
Yinan Qi (OPPO)
Slide 9
Doc.: IEEE 802.11-24/1782r0
November 2023

## Slide 10: Reference
IEEE 802.11-24/1780r0 Further Discussion on AMP PPDU Design
Doc.: IEEE 802.11-24/1782r0
November 2023

## Slide 11
SP1
  Do you agree that the DL to UL transition time with in one PPDU should be defined?
    The components of such transition time are TBD.
Yinan Qi (OPPO)
Slide 11
Doc.: IEEE 802.11-24/1782r0
November 2023

## Slide 12
SP2
  Do you agree that the UL to DL transition time with in one PPDU should be defined?
    The components of such transition time are TBD.
Yinan Qi (OPPO)
Slide 12
Doc.: IEEE 802.11-24/1782r0
November 2023

## Slide 13
SP3
  Do you agree that when and where to insert AMP-sync preceding AMP-Data should depend on clock drifting rate?
Yinan Qi (OPPO)
Slide 13
Doc.: IEEE 802.11-24/1782r0
November 2023