## Slide 1: Interference Mitigation Pilots - Definitions
Date: November 9, 2024
Authors:

## Slide 2: Introduction
Interference Mitigation as a means to significantly improve the reliability has been presented in multiple technical contributions, e.g. [1]
A motion to incorporate additional IM pilots (used for interference estimation and mitigation) passed in the September meeting [2]:
In this contribution we suggest some definitions/constraints w.r.t. IM

## Slide 3: Suggested IM Pilot Definitions
In order to simplify the use and definition of IM Pilots, we suggest to limit the operation of Interference Mitigation to the following cases:
  Works only with LDPC
  Works only with regular RUs (not applicable to dRUs)
  Number of IM Pilots is fixed per BW size (values TBD) – simplifies design/signaling
  IM Pilots are used in every OFDM symbol of the data field and are located in fixed subcarrier positions (enables regularized hardware + supports immediate identification of interference that begins anywhere within the data portion)
Also worth noting:
  IM is less applicable for DL MU-MIMO (i.e., in this operation mode it is only applicable in relatively marginal cases where STAs have more Rx Degrees of Freedom than the number of MU-Interference streams)

## Slide 4: Summary
We suggested some constraints and design properties of IM pilots which will simplify their design both in the spec and in products

## Slide 5: Straw Poll #1
Do you support that the Interference Mitigation feature is only defined with LDPC?

## Slide 6: Straw Poll #2
Do you support that the Interference Mitigation feature is not defined for dRUs?

## Slide 7: Straw Poll #3
Do you support that for each bandwidth, there is a fixed number of IM pilots (value TBD)?

## Slide 8: Straw Poll #4
Do you support that within any transmission that uses IM pilots, they are used in every data OFDM symbol and in the same corresponding subcarriers positions, for a given BW?

## Slide 9: References
[1] 11-24-1264r0: Supporting Rx Interference Mitigation in TGbn (Shimi Shilo et al)
[2] 11-24-171r15: TGbn Motions List Part 1 (Alfred Asterjadhi)
Notes: at least one mode of operation capable of improved support, compared to 802.11be, for applications with stringentworst-case latency and jitter requirementscompared to 802.11be // i.e., avoid “worst-case”