## Slide 1: Design Considerations of DL Data Rate and SYNC
Date: 2024-11-09
Authors:

## Slide 2: Introduction
The low power tag hardware characteristics have been discussed and compared [1, 2]
More relaxed design is needed to accommodate and facilitate ambient power device design
In this presentation, we continued the discussion on the DL data rates and SYNC design proposals.

## Slide 3: Recap: Mono-static Backscattering Tag [2]
AMP + UHF: one tag for both B2B and B2C applications
  B2B: sub-1GHz backscattering with ~10m range
  B2C: 2.4GHz backscattering with ~10cm range
AMP mono-static backscattering tag should share common or similar RF/hardware requirements
900MHz + 2.4GHz
Antenna
Z_ant
Modulator
AMP
Logic
Memory
RFID
Logic

## Slide 4: SYNC design
In Sept. meeting,
  SYNC field is agreed to be part of the DL PPDU format
    Initial synchronization of AMP DL PPDU
  Manchester coding for DL PPDU data portion
A shorter SYNC than 11ba is suggested in [3],
  to cover all integrated energizer case with up to 70dB link budget
  SNR is not the limitation factor

## Slide 5: DL PPDU Rx for AMP Tag
Design requirement for backscattering Tag Rx [2]:
  At least 2us pulse duration
    Limitation due to envelope detector sensitivity and 2MHz clock rate
    Each pulse of SYNC field needs to be at least 2us
    250kbps max data rate with Manchester coding
  100k ppm requires per-pulse synchronization
SYNC design:
  Low false trigger rate on data portion with Manchester coding
    Invalid Manchester code, e.g. 3 consecutive ON/OFF pulses
  Limited consecutive OFF pulses to avoid regular WiFi receiver: suggested max 3 OFF pulses same as WUR SYNC
  Zero-DC to simplify Rx design
  Good cross-correlation properties

## Slide 6: SYNC Sequences
Sequence 1: [0 1 1 1 0 1 0 0 0 1 1 1 0 0 0 1]
Sequence 2: [1 1 0 1 0 0 0 1 1 0 0 0 1 1 1 0]
Sequence 3: [1 1 0 0 0 1 0 1 1 1 0 0 0 1 1 0]

## Slide 7: SYNC Performance
Simulation settings:
  2MHz Tag Rx nominal clock rate
  Tag clock ppm: [0, +/-10k, +/-50k, +/-100k] ppm
  SYNC performance waveform:
    160 Manchester Encoded data bits (250kbps) + SYNC
  Rx SYNC detection:
    Counter based per-bit transition detection
    Pmiss: miss detection probability of SYNC
  Reference Manchester data performance: no initial timing estimation
  SNR = “ON” pulse power – noise power
  AWGN channel
  Note: SYNC sequence 2

## Slide 8: Performance
SYNC 1% Pmiss SNR requirement matches with 250kbps PER
Note: Pfalse = 0

## Slide 9: Discussions
SNR = 16dBm [3] – Pathloss (db) – (-85dBm)
  Noise floor = -95dBm (80MHz BW)
  Noise figure: 10dB
Sensitivity of ~9dB for 100k ppm
Maximum supported pathloss = 92dB
The supported range can be even longer with advanced preamble detection
Length 16 SYNC is sufficient to support main use cases

## Slide 10: Summary
Discuss AMP DL PPDU SYNC design requirement
  Minimum 2us pulse width
  Bit-level synchronization
  Invalid code for avoid false trigger in Manchester data portion
Several SYNC design proposals and performance evaluation
  Length 16 SYNC is sufficient to support the link budget requirement

## Slide 11: References
[1] 11-24/1475, Discussion on ultra-low power timing clock
[2] 11-24/1237, AMP-Tag-requirements-for-Mono-static-Backscattering
[3] 11-24/1163, WUR for Integrated Energizer Case
[4] EPC UHF Gen2 Air Interface Protocol | GS1

## Slide 12: SP
Do you agree to add the following to TGbp SFD?
  AMP DL PPDU SYNC field is defined based on pulse duration of 2us?

## Slide 13: SP
Do you agree to add the following to TGbp SFD?
  AMP defines one data rate of 250kbps for DL transmission?

## Slide 14: SP
Do you agree to add the following to TGbp SFD?
  AMP DL PPDU defines SYNC of length 16?