## Slide 1: Sync field for AMP PPDU
Date: 2024-09-03
Authors:
Name | Affiliation | Address | Phone | Email
Wang Ke | OPPO |  |  | wangke6@oppo.com
Jinyu Zhang |  |  |  | xuweijie@oppo.com
Weijie Xu |  |  |  | v-qiyinan@oppo.com
Yinan Qi |  |  |  | 
Sehngjiang Cui |  |  |  | 
Doc.: IEEE 802.11-24/1803r0
Nov. 2024

## Slide 2: Abstract
In this contribution, we will firstly discuss the requirement the Sync field and then propose candidate sync sequence.
Doc.: IEEE 802.11-24/1803r0

## Slide 3: Requirements for AMP sync
The following requirements need to be considered for AMP sync.
  Different sync sequences for DL/UL for indication.
  Support two different AMP DL rate
    1Mbps and 250kbps using 2 different sync
    A correlator can distinguish between Sync length 16 and 32.
  The Sync sequence has the same number of 1 and 0.
  Good auto-correlation
  The sequence have 3 consecutive 1/0, which can help distinguish synchronization field and data field with Manchester coding.
Doc.: IEEE 802.11-24/1803r0

## Slide 4: Auto-Correlation Metrics
For high data rate：[]
For low data rate: [S S]
Local reference sequence:
Doc.: IEEE 802.11-24/1803r0

## Slide 5: Cross-Correlation Metrics
The Sync sequence will be correlated with other filed of the UL/DL PPDU e.g., random Manchester coding symbols to see the cross-correlation property
  The sync sequence shall maintain low cross-correlation with other filed of UL/DL PPDU
Doc.: IEEE 802.11-24/1803r0

## Slide 6: Sync sequence length(1)
For length 8, the auto-correlation is not so good and cross-correlation with random Manchester symbols become unacceptable.
  The best sequence after computer searching is '10001101'
Doc.: IEEE 802.11-24/1803r0
AC_H: -4 AC_L: 2
Cross-correlation with Random Manchester symbols

## Slide 7: Sync sequence length(2)
For length 16, the auto-correlation is better and cross-correlation with random Manchester symbols is good
  One candidate sequence after computer searching is '1100100101011100'
Doc.: IEEE 802.11-24/1803r0
AC_H: -4 AC_L: 2
Cross-correlation with Random Manchester symbols

## Slide 8: Summary
In this submission, sync sequence for AMP is discussed. Based on the discussion, the following is proposed.
  Basic sync length is 16, one proposed sequence is
    S1= '1100100101011100’
Doc.: IEEE 802.11-24/1803r0