## Slide 1: Frame Format Discussion
Date: 2024-11-10
Authors:

## Slide 2: Recap: 802.11 Frame Format
The different versions of frame formats are defined in 802.11: PV0, PV1, WUR.
The frame of PV0 has the following format:
0 or 6
Control frame format
Data frame format
Management frame format
The frame of PV1 has the following format:
The frame of WUR has the following format:

## Slide 3: Purpose of Frame Format
The MAC header includes the information about the various frame format.
The identifier of peer device and the transmitter at frame header are needed for
  the acknowledgement of the soliciting frame.
  The handshake of the request management frame and response management frame in the different TXOP.
  The information of the STAs being maintained at associated AP.
  The information of the AP being maintained at associated STA.
The FCS at the end of the frame verifies whether the MAC header and frame body of the received frame has error or not.

## Slide 4: Use Cases of 11bp
Use cases per RFID.
  RFID message is carried in 11bp where the RFID defines the format of the message.
    The interpretation of the RFID message is up to RFID protocol.
  AMP tag (11bp tag) is read by the AMP reader.
    No power save mode for AMP tag.
    No state/management information maintained in AMP reader of AMP tag except RFID message of the read AMP tag.
Use Cases per wakeup radio.
  The wakeup of a STA in power save mode needs to maintain the STA’s state in the associated AP.
    The wakeup information needs to carry the identifier of the STA being woken up.
    No other protocol defines the format of the wakeup information unless the WUR frame is used here.
      Whether or no WUR frame is used, the frame format carrying the wakeup information needs to be clarified.

## Slide 5: Frame Format Indication
The potential 11bp PPDU format could be one of the following:
  802.11 non-HT LTF + 802.11 STF + 802.11 SIG + AMP Sync + PSDU
  802.11 non-HT LTF + 802.11 STF + 802.11 SIG + AMP Sync + AMP SIG + PSDU
When 11bp PPDU doesn’t include AMP SIG, the different format of PSDU is indicated by FC field in PSDU:
  Frame format 1: FC (frame control) field + frame body + FCS field where the frame body carries RFID message defined by RFID.
  Frame format 2: similar to WUR frame format.
When 11bp PPDU includes AMP SIG, the different format of PSDU is indicated by AMP SIG:
  Frame format 1: RFID message.
  Frame format 2: same as WUR frame format.

## Slide 6: Summary
The various frame formats of 11bp are discussed:
  The frame formats are different for the different use cases.
  The frame formats are different based on whether 11bp PHY has the indication of the different frame formats.