## Slide 1: UL Data Continuity Improvement for Seamless Roaming
Date: 2024-11-11
Authors:

## Slide 2: Introduction
Seamless roaming has been discussed in TGbn and there has been agreements on some basic procedures in the SFD [1].
However, UL suspension occurs during roaming procedure between AP MLDs [2-3].
UL suspension may result in UL data discontinuity, and it causes a significant impact on interactive use cases and mission-critical use cases [4] that require low latency and high reliable UL transmission.
  UL suspension occurs during the roaming procedure regardless of architecture such as FT-based roaming [5] or SMD-based roaming [6].
This contribution proposes and discusses some protocols to solve the data discontinuity caused by UL suspension during the roaming procedure.

## Slide 3: Recap: Roaming procedure and UL suspension
The roaming procedure is initiated by sending a request frame.
  Non-AP STA sends a roaming request frame (non-AP initiated roaming) [1].
  AP may also send a roaming request frame (AP initiated roaming).
The roaming procedure performs context transfer to the Target AP and performs necessary DS mapping change [1].
Once the roaming procedure is initiated, UL transmission to Current AP is suspended.
  Non-AP STA can send UL traffic to Target AP after reception of notification of the DS mapping change or reception of the roaming response frame.
Roaming req.
may Ack
Context transfer
DS mapping change
Roaming res.
may Ack
UL suspension
Non-AP STA
Current AP
Target AP

## Slide 4: Necessity of UL data continuity improvement
In some use cases, low latency UL transmission is required.
  XR (e.g. See-through) use cases: UL pose/control information need to be delivered in certain period because DL video traffic is generated based on the UL traffic.
  Haptics use cases: Real-time and bidirectional communication are required. In case of Industrial IoT, it could be mission critical use cases [4].
If non-AP STA is buffering low latency traffic for such use cases during roaming procedure, data continuity of the traffic can not be maintained due to UL suspension.
Hence, we will address improvement of UL data continuity, minimizing the impact on roaming procedure.
 | Haptics (Automotive) | XR
Reliability | 99.999 (w/compr.) % | 99 %
Latency | 1-10 ms | 10 ms
Requirements [7-8]
Roaming req.
UL1
UL2
Roaming res.
Drop
UL suspension
Non-AP STA
Current AP
Target AP
Buffered traffic
Lifetime
Lifetime

## Slide 5: Proposals
Proposal 1: Non-AP STA sends an indication of initiating roaming procedure at desired timing.
Proposal 2: Non-AP STA sends low latency UL traffic before the roaming response frame.
Proposal 3: Non-AP STA sends its buffer status to enable low latency transmission after the roaming response frame.
Buffered UL
Proposal 2
Current AP
Roaming req.
Pre-negotiation
Non-AP STA
Roaming res.
Lifetime
Proposal 1
Non-AP STA
Current AP
UL traffic with roaming procedure indication
Pre-negotiation
Roaming res.
Proposal 3
Target AP
Roaming req.
Notify
buffer status
Non-AP STA
Roaming res. with trigger

## Slide 6: Proposal 1
Problem Statement:
If roaming procedure, during which UL transmission is suspended, is initiated while non-AP STA is buffering traffic, the lifetime of the traffic will expire due to UL suspension.
  In case of AP-initiated roaming, AP may send a roaming request frame to non-AP STA that is buffering low latency traffic.
  In case of STA-initiated roaming, non-AP STA may send a roaming request frame before low latency UL traffic if roaming request frame has higher priority or is queued earlier.
Proposal 1 Statement:
Non-AP STA sends an indication to initiate roaming procedure at desired timing.
  Non-AP STA includes the indication in UL traffic (MAC header) so that low latency traffic can be reliably sent before roaming request frame.
  In case non-AP STA cannot send low latency UL traffic by expiration, the roaming initiation time may be set.
Buffered UL
Lifetime
Roaming req. and may Ack exchange
Non-AP STA
Current AP
Lifetime
Proposal 1
UL traffic with roaming procedure indication
Pre-negotiation
Current AP
Non-AP STA
Roaming res.
Notes: Proposal 1 is effective when the low latency UL traffic has periodicity.

## Slide 7: Proposal 2
Problem Statement:
Unexpected low latency UL traffic may be generated during roaming procedure, and the expiration time is before the roaming response frame.
In that case, the traffic may have to be sent before the roaming response frame.
Proposal 2 Statement:
Non-AP STA sends low latency UL traffic before the roaming response frame.
There are three cases of UL transmission.
  UL traffic is sent to Current AP and then delivered to the DS
  UL traffic is sent to Current AP, forwarded to Target AP and then delivered to the DS
  UL traffic is sent to Target AP and then delivered to the DS
Non-AP STA
Roaming req.
Current AP
Roaming res.
DS
Non-AP STA
Target AP
Roaming req.
DS
Roaming res.
Non-AP STA
Current AP
Roaming req.
Roaming res.
Target AP
DS

## Slide 8: Details of Proposal 2
Concerns:
In case non-AP STA sends UL traffic to Current AP before the roaming response frame, there are concerns about DS mapping change or context change.
  If DS mapping change is initiated, Current AP cannot deliver UL traffic to the DS.
  If Current AP delivers UL traffic to the DS, the context shared with Target AP changes.
Solutions:
Current AP can deliver UL traffic to the DS during specified period.
Current AP can only send permitted UL traffic during roaming procedure and verifies changed contexts with Target AP at (before) the roaming response frame exchange.
UL data forwarding is also one of the solutions.
Context transfer
Non-AP STA
Current AP
Roaming req.
Target AP
Roaming res.
DS
DS mapping timing
Context change
Disable to deliver
Non-AP STA
Current AP
Roaming req.
Roaming res.
Target AP
DS
Verify changed contexts
Specified period

## Slide 9: Proposal 3
Problem Statement:
Unexpected low latency UL traffic may be generated during roaming procedure, and the expiration time is after the roaming response frame.
In that case, the traffic may not have enough lifetime left after roaming procedure.
Proposal 3 Statement:
Non-AP STA sends its buffer status to enable low latency transmission after the roaming response frame.
  Examples to enable low latency UL transmission:
    Current AP sends an indication that Non-AP STA has low latency traffic (Fig. a).
    Target AP triggers low latency UL traffic with the roaming response frame (Fig. b).
Buffered traffic
Roaming req.
Non-AP STA
Roaming res.
Current AP
Target AP
Fig. a
Indication
may send buffer status and request low latency transmission
Current AP
Roaming req.
Non-AP STA
Roaming res. with trigger
Target AP
may send buffer status and request low latency transmission
Fig. b

## Slide 10: Summary
UL suspension occurs during roaming procedure between AP MLDs.
UL suspension may result in data discontinuity for low latency UL traffic, and it causes a significant impact on interactive and mission-critical use cases.
Thus, we discussed how to improve UL data continuity, minimizing the impact on roaming procedure:
    Proposal 1: Non-AP STA sends an indication to initiate roaming procedure at desired timing.
    Proposal 2: Non-AP STA sends low latency UL traffic before the roaming response frame.
    Proposal 3: Non-AP STA sends its buffer status to enable low latency transmission after the roaming response frame.
We can combine these three proposals.
 | Source AP | Target AP
Before roaming procedure | Proposal 1 | Useless
During roaming procedure | Proposal 2 | Proposal 2
After roaming procedure | Useless | Proposal 3

## Slide 11: References
[1] 24/171r15, “TGbn Motion Lists,” Alfred Asterjadhi (Qualcomm Inc.)
[2] 24/0052r0, “Seamless Roaming Details, ” Duncan Ho (Qualcomm Inc.)
[3] 24/1086r0, “Data forwarding for seamless roaming,” Ryuichi Hirata (Sony)
[4] 24/1493r1, “Use Cases for Wi-Fi Business Solutions in UHR,” Akira Kishida (NTT)
[5] 24/0349r3, “Enhance Fast BSS Transition,” Guogang Huang (Huawei)
[6] 24/0396r2, “Seamless Roaming within a Mobility Domain – Follow Up,” Binita Gupta (Cisco Systems)
[7] O. Holland et al., "The IEEE 1918.1 “Tactile Internet” Standards Working Group and its Standards," in Proceedings of the IEEE, vol. 107, no. 2, pp. 256-279, Feb. 2019.
[8] “Study on XR (Extended Reality) evaluations for NR,” 3GPP TR 38.838 v 17.0.0, Dec. 2021.

## Slide 12: Appendix 1: Effective case of Proposal 1
Lifetime
Current AP
Non-AP STA
Roaming res.
Other Non-AP STA
Roaming req.
Traffic periodicity
Traffic periodicity
Buffered roaming req.
Buffered traffic
Although non-AP STA has no buffered low latency UL traffic when roaming procedure is initiated, there is a possibility that the initiation timing of roaming procedure is not optimal.
  Next low latency UL traffic may be buffered immediately after roaming procedure is initiated
If Non-AP STA knows the timing of next UL traffic generation, Non-AP STA may adjust the initiation timing of roaming procedure by Proposal 1.

## Slide 13: Appendix 2: Effective case of Proposal 2 (Case 1)
In case R-TWT is adopted between Non-AP STA and Current AP, next UL traffic transmission from Non-AP STA can be expected.
In that case, DS mapping change is initiated after R-TWT SP to deliver UL traffic to the DS.
Current AP
Non-AP STA
Roaming req.
DS
R-TWT SP
DS mapping
Roaming res.

## Slide 14: Appendix 3: Supplement to Proposal 2 (Case 3)
Lifetime
Target AP
Non-AP STA
Roaming res.
Roaming req.
Buffered traffic
In case non-AP STA sends UL traffic Target AP, and then Target AP delivers UL traffic to the DS, UL traffic is delivered to the DS after both DS mapping change and context transfer are performed.
  Non-AP STA can send UL traffic to Target AP during roaming procedure, but Target AP cannot deliver it to the DS until context transfer and DS mapping change has been completed.
DS
Context transfer and DS mapping
Deliver UL traffic after context transfer and DS mapping
Non-AP STA can send UL traffic to Target AP, but
Target AP cannot delivery it to the DS

## Slide 15: Appendix 4: Supplement to Proposal 3
Lifetime
Current AP
Non-AP STA
Roaming res.
Roaming req.
Buffered traffic
In case of roaming procedure with single link [2], Current AP has to notify no buffer indication to send roaming response from Target AP.
  In case of roaming procedure with single link, link with Target AP is enabled after Current AP flushes remaining queued packets.
Non-AP STA’s buffer status information can be sent from Current AP when Current AP notifies no buffer indication.
Target AP
Context transfer and DS mapping
Current AP flushes remaining queued packets.
Notify no buffer indication and non-AP’s buffer status

## Slide 16: Appendix 5: Combination of three Proposals
Although we discuss three solutions, we can combine three proposals to improve data continuity for UL traffic.
  e.g.
  UL periodicity is 4 ms.
  The expiration of UL traffic is 5 ms.
  Duration from roaming request to roaming response is 10 ms.
Current AP
UL traffic with roaming indication
(Proposal 1)
Non-AP STA
Roaming res. with trigger
(Proposal 3)
Target AP
Buffered traffic
Duration from roaming req. to roaming res. = 10 ms
Lifetime
Pre-negotiation
DS
UL transmission to Current AP
Proposal 2
5 ms
DS mapping change

## Slide 17: Appendix 6: Motions of Seamless Roaming
Motion 2
11bn defines a mechanism that enables a non-AP MLD to roam from one AP MLD to another AP MLD and the non-AP MLD remains in state 4 (see 11.3) during and after roaming to the other AP MLD
Motion 8
11bn defines a mechanism that when a non-AP MLD roams from one AP MLD to another AP MLD, the context related to the non-AP MLD is transferred from the one AP MLD to the other AP MLD such that it preserves the data exchange context for the non-AP MLD.
  Details of the context (e.g., security association context) that can be transferred are TBD
  Framework to transfer the context is TBD.
Motion 26
Define in 11bn that when a non-AP MLD is in the process of roaming from the current AP MLD to a target AP MLD, the context related to the non-AP MLD is transferred to the target AP MLD such that it preserves the data exchange context for the non-AP MLD or the context can be renegotiated with the target AP MLD
  Details on what context can be transferred and what context can be renegotiated are TBD
  How to transfer the context is TBD.

## Slide 18: Appendix 7: Motions of Seamless Roaming
Motion 27
As part of the seamless roaming procedure, during roaming,
  after the request/response exchange that initiates notification of the DS mapping change from the current AP MLD to the target AP MLD,
    The current AP MLD may deliver buffered DL data frames for a TBD period of time.
    The non-AP MLD may retrieve buffered DL data frames from the current AP MLD
    The non-AP MLD may send UL data to target AP MLD.
    It is assumed that the target AP MLD is able to deliver data frames to non-AP MLD after the DS mapping change
  The current AP MLD may forward DL data to the target AP MLD.
    When and how to initiate the forwarding of DL data is TBD
Motion 28
Define in 11bn that a non-AP MLD can gather information on candidate AP MLD(s) over the DS via the current AP MLD
Motion 44
Define a request frame sent by a non-AP MLD in state 4 to initiate the roaming procedure
The roaming procedure performs context transfer to the target AP MLD and perform the necessary changes of the DS mapping from the current AP MLD to the target AP MLD
Define a response frame sent to the non-AP MLD to indicate readiness for the non-AP MLD to send class 3 frames to the target AP MLD
TBD on data transmission from non-AP MLD to current AP MLD during the request/response frame exchange
NOTE – What context is transferred is TBD.
NOTE – TBD on which request/response frame to use