## Slide 1: UL Data Continuity Improvement for Seamless Roaming
Date: 2024-11-11
Authors:

## Slide 2: Introduction
Seamless roaming has been discussed in TGbn and there has been agreements on some basic procedures in the SFD [1].
However, UL suspension occurs during the roaming procedure between AP MLDs [2-3].
UL suspension may result in UL data discontinuity, and it causes a significant impact on interactive use cases and mission-critical use cases [4] that require low latency and high reliable UL transmission.
  UL suspension occurs during the roaming procedure regardless of architecture such as FT-based roaming [5] or SMD-based roaming [6].
This contribution proposes and discusses some protocols to solve the data discontinuity caused by UL suspension during the roaming procedure.

## Slide 3: Recap: Roaming procedure and UL suspension
The roaming procedure is initiated by sending a request frame.
  Non-AP STA sends a roaming request frame (non-AP initiated roaming) [1].
  AP may also send a roaming request frame (AP initiated roaming).
Context transfer and necessary DS mapping change are performed as a part of roaming procedure [1].
Once the context transfer and DS mapping change (roaming procedure) are initiated, UL transmission to Current AP is suspended.
  Non-AP STA can send UL traffic to Target AP after reception of notification of the DS mapping change or reception of the roaming response frame.
Roaming request
Context transfer
DS mapping change
Roaming response
UL suspension
Non-AP STA
Current AP
Target AP

## Slide 4: Necessity of UL data continuity improvement
In some use cases, low latency UL transmission is required.
  XR (e.g. See-through) use cases: UL pose/control information needs to be delivered in certain period because DL video traffic is generated based on the UL traffic.
  Haptics use cases: Real-time and bidirectional communication are required. In case of Industrial IoT, it could be mission critical use cases [4].
If non-AP STA is buffering low latency traffic for such use cases during the roaming procedure, data continuity of the traffic can not be maintained due to UL suspension.
Hence, we will address improvement of UL data continuity, minimizing the impact on the roaming procedure.
 | Haptics (Automotive) | XR
Reliability | 99.999 (w/compr.) % | 99 %
Latency | 1-10 ms | 10 ms
Requirements [7-8]
Roaming request
UL1
UL2
Roaming response
Drop
UL suspension
Non-AP STA
Current AP
Target AP
Buffered traffic
Lifetime
Lifetime

## Slide 5: Proposals
Proposal 1: Non-AP STA sends an indication to initiate the roaming procedure at the desired timing.
Proposal 2: Non-AP STA sends low latency UL traffic before the roaming response frame.
Proposal 3: Non-AP STA sends its buffer status to enable low latency transmission after the roaming response frame.
Buffered UL
Proposal 3
Target AP
Roaming req.
Notify
buffer status
Non-AP STA
Roaming res. with trigger
Proposal 1
Non-AP STA
Current AP
UL traffic with a roaming procedure indication
Frame exchange before the roaming procedure
Roaming res.
Lifetime
Proposal 2
Target AP
Roaming req.
Non-AP STA
Roaming res.
Frame exchange before the roaming procedure
UL traffic
Frame exchange before the roaming procedure

## Slide 6: Proposal 1
Problem Statement:
If roaming procedure, during which UL transmission is suspended, is initiated while non-AP STA is buffering traffic, the lifetime of the traffic will expire due to UL suspension.
  In case of AP-initiated roaming, AP may send a roaming request frame to non-AP STA that is buffering low latency traffic.
  In case of STA-initiated roaming, non-AP STA may send a roaming request frame before low latency UL traffic if roaming request frame has higher priority or is queued earlier.
Proposal 1 Statement:
Non-AP STA sends an indication to initiate the roaming procedure at the desired timing.
  Non-AP STA includes the indication in UL traffic (MAC header) so that low latency traffic can be reliably sent before roaming procedure.
  In case non-AP STA cannot send low latency UL traffic by expiration, the roaming initiation time may be set.
Buffered UL
Lifetime
Roaming request
Non-AP STA
Current AP
Proposal 1
UL traffic with a roaming procedure indication
Current AP
Non-AP STA
Roaming res.
Frame exchange before the roaming procedure
(capability/roaming initiation conditions/roaming initiation time/…)
initiate the roaming procedure
Notes: Proposal 1 is effective when the low latency UL traffic has periodicity.

## Slide 7: Proposal 2
Problem Statement:
Unexpected low latency UL traffic may be generated during the roaming procedure, and the expiration time is before the roaming response frame.
In that case, the traffic may have to be sent before the roaming response frame.
Proposal 2 Statement:
Non-AP STA sends low latency UL traffic before the roaming response frame.
There are two cases of UL transmission.
  UL traffic is sent to Target AP and then delivered to the DS
  UL traffic is sent to Current AP, forwarded to Target AP and then delivered to the DS
Non-AP STA
Current AP
Roaming req.
Roaming res.
Target AP
DS
Non-AP STA
Target AP
Roaming req.
DS
Roaming res.

## Slide 8: Details of Proposal 2
Non-AP STA
Current AP
Target AP
DS
Concerns:
In case non-AP STA sends UL traffic to Current AP before the roaming response frame, there are concerns about DS mapping change or context change.
  If DS mapping change is initiated, Current AP cannot deliver UL traffic to the DS.
  If Current AP delivers UL traffic to the DS, the context shared with Target AP changes.
Solutions:
Non-AP STA sends limited UL traffic to Target AP, and Target AP maintains it until roaming procedure has been completed.
UL data forwarding is also one of the solutions.
Context transfer and DS mapping change
Non-AP STA
Current AP
Roaming req.
Target AP
Roaming res.
DS
Disable to deliver
Roaming req.
Roaming res.
Frame exchange before the roaming procedure
Able to deliver

## Slide 9: Proposal 3
Problem Statement:
Unexpected low latency UL traffic may be generated during the roaming procedure, and the expiration time is after the roaming response frame.
In that case, the traffic may not have enough lifetime left after the roaming procedure.
Proposal 3 Statement:
Target AP receives low latency traffic information and/or an indication to solicit low latency UL transmission.
  Examples to enable low latency UL transmission:
    Current AP sends an indication that non-AP STA has low latency traffic (Fig. a).
    Target AP triggers low latency UL traffic with the roaming response frame (Fig. b).
Buffered traffic
Roaming req.
Non-AP STA
Roaming res.
Current AP
Target AP
Fig. a
Indication
may send buffer status and request low latency transmission
Current AP
Roaming req.
Non-AP STA
Roaming res. with trigger
Target AP
may send buffer status and request low latency transmission
Fig. b
Frame exchange before the roaming procedure
Frame exchange before the roaming procedure

## Slide 10: Summary
UL suspension occurs during roaming procedure between AP MLDs.
UL suspension may result in data discontinuity for low latency UL traffic, and it causes a significant impact on interactive and mission-critical use cases.
Thus, we discussed how to improve UL data continuity, minimizing the impact on roaming procedure:
    Proposal 1: Non-AP STA sends an indication to initiate the roaming procedure at the desired timing.
    Proposal 2: Non-AP STA sends low latency UL traffic before the roaming response frame.
    Proposal 3: Non-AP STA sends its buffer status to enable low latency transmission after the roaming response frame.
We can combine these three proposals.
 | Current AP | Target AP
Before roaming procedure | Proposal 1 | Useless
During roaming procedure | Proposal 2 | Proposal 2
After roaming procedure | Useless | Proposal 3

## Slide 11: References
[1] 24/171r15, “TGbn Motion Lists,” Alfred Asterjadhi (Qualcomm Inc.)
[2] 24/0052r0, “Seamless Roaming Details, ” Duncan Ho (Qualcomm Inc.)
[3] 24/1086r0, “Data forwarding for seamless roaming,” Ryuichi Hirata (Sony)
[4] 24/1493r1, “Use Cases for Wi-Fi Business Solutions in UHR,” Akira Kishida (NTT)
[5] 24/0349r3, “Enhance Fast BSS Transition,” Guogang Huang (Huawei)
[6] 24/0396r2, “Seamless Roaming within a Mobility Domain – Follow Up,” Binita Gupta (Cisco Systems)
[7] O. Holland et al., "The IEEE 1918.1 “Tactile Internet” Standards Working Group and its Standards," in Proceedings of the IEEE, vol. 107, no. 2, pp. 256-279, Feb. 2019.
[8] “Study on XR (Extended Reality) evaluations for NR,” 3GPP TR 38.838 v 17.0.0, Dec. 2021.

## Slide 12: SP1 (Not SFD Proposal)
Do you agree to define some protocols in 11bn to reduce the impact on the UL suspension during the roaming request/response exchange to improve UL data continuity?

## Slide 13: SP2
Do you agree to add the following text to 11bn SFD?
Do you agree that a non-AP MLD sends an indication, after sending the roaming request frame, to initiate the roaming at the desired timing?
Notes: non-AP MLD and current AP MLD may negotiate how to initiate the roaming and non-AP MLD may send UL traffic with an indication as a TBD Request frame to initiate roaming.

## Slide 14: SP3
Do you agree to add the following text to 11bn SFD?
A non-AP MLD that performs roaming may send TBD UL traffic before the roaming response frame under TBD conditions.
  TBD UL traffic is delivered to the DS via the target AP MLD.

## Slide 15: SP4
Do you agree to add the following text to 11bn SFD?
Define a mechanism for a non-AP MLD to notify a target AP MLD of low latency traffic information and/or a request, enabling the target AP MLD to solicit low latency transmission from the non-AP MLD immediately after the roaming request/response exchange?
  Details of low latency traffic information and request are TBD.
  Whether the non-AP MLD sends low latency traffic information and/or the request directly to the target AP or via the current AP MLD is TBD.

## Slide 16: Appendix 1: Ideal timing for the roaming
The ideal timing for the roaming can improve UL data continuity.
  The ideal timing is when non-AP STA has no low latency traffic and just after non-AP STA sends low latency traffic.
  Propsoal1 is effective especially when the next traffic generation is predictable.
Target AP
Current AP
Non-AP STA
Roaming Request
Roaming Response
Target AP
Current AP
Non-AP STA
Roaming Request
Roaming Response
UL buffered
UL buffered
Target AP
Current AP
Non-AP STA
Roaming Request
Roaming Response
UL buffered
× Bad (Worst) timing
〇 Ideal timing
× Bad timing
UL buffered
UL buffered
UL buffered
When non-AP STA sends Roaming request,
(×) non-AP STA is buffering low latency traffic
(×) the next UL traffic generation is just after roaming procedure
When non-AP STA sends Roaming request,
(〇) non-AP STA has no low latency traffic
(×) the next UL traffic generation is just after roaming procedure
When non-AP STA sends Roaming request,
(〇) non-AP STA has no low latency traffic
(〇) the next UL traffic generation is not just after roaming procedure

## Slide 17: Appendix 2: Example 1 of Proposal 1
Frame exchange before the roaming procedure is necessary to realize Proposal 1.
  Non-AP STA and AP negotiate roaming procedure conditions in order to initiate the roaming procedure at desired timing.
  This frame from non-AP STA may correspond to Roaming request frame.
Target AP
Current AP
Non-AP STA
Roaming decision
Roaming preparation frame exchange
(Target AP selection/Multilink setup/Static context transfer/PTK deviation/Capability…)
Roaming procedure
Context transfer initiation
DS mapping change initiation
Roaming Response frame exchange
Link Disablement
Frame exchange (Roaming procedure conditions/Capability/…)
UL traffic with a roaming procedure indication

## Slide 18: Appendix 3: Example 2 of Proposal 1
Non-AP STA may send the frame corresponding to Roaming request frame to Target AP.
  Current AP triggers context transfer by sending context transfer request frame.
Target AP
Current AP
Non-AP STA
Roaming decision
Roaming preparation frame exchange
(Target AP selection/Multilink setup/Static context transfer/PTK deviation/Capability/Roaming procedure conditions …)
Roaming procedure
Context transfer request/response
DS mapping change initiation
Roaming Response frame exchange
Link Disablement
Frame exchange (Capability/…)
UL traffic with roaming initiation indication

## Slide 19: Appendix 4: Roaming initiation time of Proposal 1
The roaming initiation time is the pre-negotiated time to begin roaming procedure.
  In case non-AP STA cannot send UL traffic for a long time for some reasons, Current/Target AP may return Roaming response frame with Status Code ‘Reject’ by due to timeout.
  One of the examples setting roaming time is the lifetime of the UL traffic.
  Current AP or Target AP may trigger the roaming procedure.
Target AP
Current AP
Non-AP STA
Roaming procedure
Context transfer request/response
DS mapping change initiation
Roaming Response frame exchange
Lifetime
May trigger roaming procedure
Drop
Roaming initiation time

## Slide 20: Appendix 5: Details of problem statement of Proposal 3
Unexpected low latency UL traffic may be generated during roaming procedure, and the expiration time is after the roaming response frame.
  Additionally, short periodic traffic may be generated during the roaming procedure.
In that case, the traffic may not have enough lifetime left after roaming procedure.
Target AP
Current AP
Non-AP STA
Roaming Request
Context transfer (Dynamic)
DS mapping change
Roaming Response
Lifetime
Residual lifetime is short

## Slide 21: Appendix 6: Buffer status information
The non-AP STA’s low latency traffic information is not always shared between Current AP and Target AP.
  SCS is not a mandatory function.
  R-TWT may not be accepted by Target AP, or the buffered low latency traffic may not enough lifetime even if R-TWT is accepted by Target AP.
Current AP
Roaming req.
Non-AP STA
Roaming res.
Target AP
may send buffer status and request low latency transmission
Non-AP STA sends buffer status to Target AP or Current AP during roaming procedure (Of course, low latency traffic information sharing by context transfer is effective. )

## Slide 22: Appendix 7: Details of Proposal 3
If Target AP or Current AP is aware of buffer status of non-AP STA, low latency transmission can be realized.
Fig. a shows a case where non-AP STA sends buffer status to Current AP.
  Current AP sends an indication to Target AP in order to trigger UL to non-AP STA after Roaming response.
Fig. b shows a case where non-AP STA sends buffer status to Target AP.
  Target AP sends Roaming response with trigger in order to enable low latency traffic that has not enough lifetime.
Roaming req.
Non-AP STA
Roaming res.
Current AP
Target AP
Fig. a
Indication
may send buffer status and request low latency transmission
Current AP
Roaming req.
Non-AP STA
Roaming res. with trigger
Target AP
may send buffer status and request low latency transmission
Fig. b
Fig. b is more effective than Fig. a.
Frame exchange
Frame exchange

## Slide 23: Appendix 8: Frame exchange before the roaming procedure
Frame exchange before the roaming procedure is necessary to realize Proposal 3.
  PTK status confirmation for frame exchange during roaming procedure.
  What information can be exchanged during roaming procedure.
  Whether STA has Low latency (LL) traffic or not. (see. Appendix 9)
  To which AP can non-AP STA send a notification frame (buffer status frame).
Current AP
Roaming request
Non-AP STA
Roaming response
Target AP
may send buffer status and request low latency transmission
Frame exchange before the roaming procedure

## Slide 24: Appendix 9: Applications example of Proposal 3
If multiple non-AP STAs initiate and end the roaming procedure simultaneously, channel competitions between STAs that have low latency traffic and STAs that have non-low latency traffic may arise.
  Proposal 3 is available to identify STAs that have low latency traffic.
  Non-AP non low latency (LL) STA may be extended for a certain period.
Target AP
Current AP
Non-AP LL STA
with LL traffic
Roaming procedure
Non-AP LL STA
without LL traffic
Non-AP non-LL STA
* LL: Low latency
Roaming response
(with trigger)
Roaming response
(with UL resumption)
Roaming response (extension of UL suspension)
Shift the resumption timing

## Slide 25: Appendix 10: Combination of three Proposals
Although we discuss three solutions, we can combine three proposals to improve data continuity for UL traffic.
  e.g.
  UL periodicity is 4 ms.
  The expiration of UL traffic is 5 ms.
  Duration from roaming request to roaming response is 10 ms.
Current AP
UL traffic with a roaming procedure indication
(Proposal 1)
Non-AP STA
Roaming res. with trigger
(Proposal 3)
Target AP
Buffered traffic
Duration from roaming req. to roaming res. = 10 ms
Lifetime
Frame exchange
DS
UL transmission to Current AP
Proposal 2
5 ms
DS mapping change
UL data forwarding