## Slide 1: COBF Design for UHR
Date: 2024-11-11
Authors:
Name | Affiliations | Address | Phone | email
Sameer Vermani | Qualcomm Technologies Inc. |  |  | svverman@qti.qualcomm.com
Alice Chen |  |  |  | 
Bin Tian |  |  |  | 
Manideep Dunna |  |  |  | 
Youhan Kim |  |  |  | 
Meriam Rezk |  |  |  | 
Alice Chen |  |  |  | 
Deniz Rende |  |  |  | 
Ahmed Elsherif |  |  |  | 

## Slide 2: Outline
Number of users and spatial streams in COBF
COBF PPDU design details
  Common pre-UHR portion preamble across two APs
  PPDU type indication: COBF as a separate PDDU type
  How to resolve BSS color for per-user SIG fields in COBF PPDUs
  BSS-wise partitioning of per-user SIG field section
Design for NDPA
  NDPA variant remains same as EHT
  Using special STA info field; Unified design for Joint and Sequential
  We show that just one STA info field is enough
Straw-polls related to above

## Slide 3: Number of users and spatial streams in COBF
In 11-1542r0, we proposed restricting the number of APs to two in a COBF transmission
We would further like to restrict the max number of STAs to 4 in a COBF transmission
  For the typical scenario, if we have more than 3 users belonging to an AP in a transmission, the AP is unlikely to have spare dimensions for nulling
  4 total users provides opportunities for good amount of spatial multiplexing while keeping the processing at STA similar to regular MU-MIMO
To further simplify the signaling and testing, we propose
  Limit max total spatial streams to 4
  Limit the per-STA spatial streams to 2

## Slide 4: Preamble Design: Common section of preamble across APs
Propose having a non-BFed pre-UHR section of the preamble
  Simpler precoding
  U-SIG can be decoded at by-stander devices
  Closer to single cell MU-MIMO PPDU format
Obvious consequence: Pre-UHR portion needs to be identical across two APs
  Need most things in the pre-UHR portion to be pre-negotiated
Non-BFed Pre-UHR portion
BFed UHR
portion
L-STF
L-LTF
L-SIG
RL-SIG
U-SIG
UHR-SIG
UHR-STF
UHR-LTF
Data
Common contents across two APs

## Slide 5: Indication for COBF in U-SIG
COBF transmission needs indication in U-SIG that the packet is for COBF
  Special treatment of BSS Colors
    Multiple BSS colors for the participant APs may be needed in COBF PPDU’s preamble
    Per-user SIG field differentiation and for more accurate medium-use information
  The per-user SIG fields need to be differentiated
    Which AP are they coming from ?
    More on next slide
  Some preamble content may be simplified compared to regular UHR PPDU
    Maybe spatial reuse field is not needed for these PPDUs
    UHR-SIG MCS maybe fixed to a low MCS as we have longer delay spread to deal with
Proposal: U-SIG to carry an indication when the PPDU is for COBF

## Slide 6: Per-user-SIG fields Issue: Need to resolve BSS label
Need to differentiate the per-user SIG fields in the common preamble
  Which BSS/AP do they belong to?
Our proposal for differentiating the per-user SIGs of the two APs
  Place the two BSS colors in the preamble
  Have a 1-bit field in the per-user SIG field to differentiate between the two APs
AP1
AP2
BSS2
BSS1
Same STAID (collision)
How does the STA know which
per-user SIG field to decode?
Nulls

## Slide 7: Per-user SIG Field Partitioning
Prefer to separate the two BSSs per user-field sections
  E.g., All BSS-1 user fields and then all the BSS-2 user-fields or vice-versa
An AP transmits on contiguous spatial stream indices
With Nss_total <=4, it is possible, with some restrictions to the order of BSSs, to preserve the old spatial config field design
  See table below for more details
Scenario | Nss/User in AP1 | Nss/User in AP2 | Ordering of User Fields According to BSS
Each BSS has a user with 2ss | [2] | [2] | The user field of either BSS can go first
Only one BSS has a user with 2ss | [2] | [1] or [1 1] | The user field of BSS1 goes first
 | [1] or [1 1] | [2] | The user field of BSS2 goes first
No BSS has a user with 2ss | [1] or [1 1] | [1] or [1 1] | The user field(s) of either BSS can go first

## Slide 8: New NDPA or NDP variants ?
The NDPA in UHR can still use the EHT variant
  Special STA info field to convey information to a second AP for COBF case
No need to define a UHR NDP
  Can reuse the EHT NDP, even for the joint NDP
  But the BSS color needs to be the BSS color of the AP transmitting the NDPA

## Slide 9: NDPA Design for UHR
Exchange the information needed for sounding between APs for sounding via NDPA
  A special STA info field with a STAID addressed to the AP is needed
  Unified design for joint sounding as well as cross-BSS section of sequential sounding
  Prefer a self-contained design so may need two STA info fields to convey this information
Special STA info field addressed to shared AP gives info about how to transmit the NDP, e.g.,
  BW, TxOP and punctured channel information
  NLTF in NDP (P-matrix size)
    4 or 8
  Starting stream index for shared AP and Nsts for shared AP in NDP
    Which rows of P-matrix to use
    GI+LTF (at-least for joint NDP)

## Slide 10: Summary
We proposed the following
  Maximum of 4 users in a COBF transmission
  Max total Nss of 4 for COBF with per-STA streams limited to 2
  For COBF PPDU
    Identical preamble across 2 APs for the pre-UHR portion
    Two BSS colors with shared AP’s color in the version independent section
    1 bit in per-user SIG to resolve BSS color
    Per-user fields of one BSS and then per-user fields of the other BSS
  NDPA for COBF with a special STA info field
    Unified design for joint and sequential sounding cases

## Slide 11: SP1
Do you support transmitting the pre-UHR portion of the COBF packet in a non-beamformed (omni) manner?

## Slide 12: SP2
Do you support that the pre-UHR portion of a COBF PPDU will have identical content across two APs?

## Slide 13: SP3
Do you support to indicate a COBF data transmission in U-SIG for 802.11bn?

## Slide 14: SP4
Do you support that in a COBF transmission the maximum spatial streams given to one user will be 2?

## Slide 15: SP5
Do you support to have 2 BSS colors in the preamble of a COBF PPDU
  One BSS color for the sharing AP and another BSS color for the shared AP

## Slide 16: SP6
Do you support to have a 1-bit indication in the per-user SIG field to resolve the BSS color for COBF transmissions?
  The coding bit is re-purposed for this indication
  LDPC is the only coding mode for COBF

## Slide 17: SP7
Do you support that we can re-use EHT variant for the NDPA and re-use the EHT NDP for sounding in UHR?

## Slide 18: SP8
Do you support that for COBF case, the information in the NDPA for the responding AP has a unified design for joint-NDP based sounding as well as cross-BSS section of sequential sounding?

## Slide 19: SP9
Do you support that the spatial config field in the user-SIG field of COBF PPDUs in UHR will re-use the same design as in UHR DL MU-MIMO?
  Encoding table will be same as 11ax

## Slide 20: SP10
Do you support that for a COBF PPDU, all the user-fields in UHR-SIG belonging to an AP and the corresponding spatial streams are contiguous?
  The user fields of one AP are together followed by the ones of the other AP and the same holds for spatial streams

## Slide 21: appendix
Other details

## Slide 22: Protection for COBF transmissions
Note that there are going to be some frames exchanged between the two APs before the COBF transmission
A frame from initiating AP (e.g., a COBF trigger) may be used to set the NAV in BSS1
We may also place the responding AP’s BSS color in the version independent section of the U-SIG for protection inside BSS2
  Note that even WiFi 7 devices understand the BSS color in U-SIG at that location
Additionally, suggest having a rule in the specification for the case when the STA can decode U-SIG with a version number it doesn’t understand
  Disable OBSS_PD based SR for such cases
  Note that SR field is not in the version independent section so whenever a WiFi 7 STA sees a UHR PPDU, it will not have access to the SR field

## Slide 23: Explanation of protection mechanism for COBF
Below we show protection mechanisms to achieve good protection in both BSSs
DL PPDU
Sharing AP
DL PPDU
Shared AP
COBF
Invite
COBF
Response
COBF
trigger
Protects in sharing AP’s BSS
Contains BSS color
of shared AP in U-SIG version
independent section