## Slide 1: 11bn Non-ELR Signaling Design for New Features
Date: 2024-11-09
Authors:
Name | Affiliations | Email
Alice Chen | Qualcomm | alicel@qti.qualcomm.com
Sameer Vermani |  | svverman@qti.qualcomm.com
Eugene Baik |  | eugeneb@qti.qualcomm.com
Bin Tian |  | btian@qti.qualcomm.com
Youhan Kim |  | youhank@qti.qualcomm.com

## Slide 2: Introduction
EHT [1] has two U-SIG formats for MU PPDU and TB PPDU, respectively
In UHR (when PHY Version Identifier is set to 1) [2], there will be at least three U-SIG formats for the three PPDU types
  MU PPDU
  TB PPDU
  ELR PPDU [3-4]
U-SIG in UHR MU PPDUs need some changes to accommodate signaling for new features
  Multi-AP features: Coordinated beamforming (CoBF), Coordinated spatial reuse (C-SR)
  User specific features: New MCS, spatial domain unequal modulation (UEQM), 2x LDPC
  Scheme related to frequency resource allocation: Interference mitigation (IM)
In this presentation, we have a comprehensive discussion on U-SIG and UHR-SIG design in UHR to accommodate new features

## Slide 3: U-SIG Overview
The 2-bit PPDU Type and Compression Mode field [3-4] in U-SIG differentiates basic transmission modes
  Including ELR
In the following, we discuss
  U-SIG in UHR TB PPDUs
  U-SIG & UHR-SIG in UHR MU PPDUs, with signaling discussion for new features
UL/DL | PPDU Type And Compression Mode | Transmission Mode | PPDU Type
0 (DL) | 0 | DL OFDMA | MU PPDU
0 (DL)/1 (UL) | 1 | SU transmission/NDP | MU PPDU
0 (DL) | 2 | DL non-OFDMA MU-MIMO | MU PPDU
0 (DL)/1 (UL) | 3 | ELR | ELR PPDU
1 (UL) | 0 | TB | TB PPDU
1 (UL) | 2 | Validate | N/A

## Slide 4: U-SIG in UHR TB PPDUs
Propose to keep the same U-SIG field structure as in EHT TB PPDUs [1]
PHY Version Identifier is set to 0 or 1 to differentiate EHT & UHR [2]
U-SIG Field in EHT/UHR TB PPDU |  |  | 
 | Bits | Field | Number of Bits
U-SIG-1 | B0-B2 | PHY Version Identifier | 3
 | B3-B5 | Bandwidth | 3
 | B6 | UL/DL | 1
 | B7-B12 | BSS Color | 6
 | B13-B19 | TXOP | 7
 | B20-B25 | Disregard | 6
U-SIG-2 | B0-B1 | PPDU Type And Compression Mode | 2
 | B2 | Validate | 1
 | B3-B6 | Spatial Reuse 1 | 4
 | B7-B10 | Spatial Reuse 2 | 4
 | B11-B15 | Disregard | 5
 | B16-B19 | CRC | 4
 | B20-B25 | Tail | 6

## Slide 5: Preamble Change in MU PPDUs
The remaining slides focus on preamble change in MU PPDUs
This part includes
  Signaling discussion for new features in MU PPDUs
  Discussion on the preamble design in the following order
    User field formats
    U-SIG
    UHR-SIG common field

## Slide 6: Signaling Discussion for 2x LDPC (1/2)
2x LDPC (codeword size of 3888) [6] is likely an optional feature in 11bn
Traditionally the usage of codeword size is solely based on
For 2x LDPC, on top of similar way to choose the codeword size, there is additional benefit to add a signaling bit to indicate 2x LDPC (i.e., using nominal codeword size of 3888)
  Broadcast packets cannot use 2x LDPC if STA Rx support of 2x LDPC is optional
    Transmitter cannot be certain that only 2x-LDPC capable STAs will be decoding the packet
  Currently, no PHY signaling exists which identifies a broadcast packet
    Even 2x LDPC-capable receivers cannot be sure if 2x LDPC is being used in a PPDU
  This signaling bit also allows more flexibility in turning ON 2x LDPC for appropriate packet sizes at the transmitter

## Slide 7: Signaling Discussion for 2x LDPC (2/2)
Signaling design & Rx behavior
  Propose to use 1 bit in user (info) fields to signal the use of the nominal codeword size of 3888 in a PPDU
    If this bit indicates ON, codeword size of 3888 is used in a PPDU
    If this bit indicates OFF, codeword size of 3888 is not used; Rx uses the existing codeword size selection procedure to choose codeword size
Tx Side 2x Codeword Size Selection
  Tx has freedom in choosing the nominal codeword size
  Still want to follow similar way as using the existing codeword size selection table so that Rx doesn’t have to deal with arbitrary usage of 2x LDPC
  Need basic guidelines to use the nominal codeword size of 3888
    If the packet size is smaller than a threshold, 2x LDPC is not used; use the existing codeword size selection to choose codeword size
    If the packet size is larger than the threshold, 2x LDPC may be used

## Slide 8: Signaling Discussion for New MCS & UEQM & User Field Formats
New MCS
  To add 4 new MCSs to 11bn [5], need to expand the MCS subfield from 4 bits to 5 bits, as proposed in [10]
  This change should be consistent in MU-MIMO and non-MU-MIMO user field formats as well as user info field in Trigger Frame
Spatial domain UEQM
  There will be a 1-bit UEQM flag [11]
  A 2-bit field could indicate all UEQM patterns [7-9] for a given Nss
User field formats discussion
  Propose the user field size to be 23 bits [13] instead of 22 bits [10-12] to accommodate the 2x LDPC indication
    Suggest to remove 1 Disregard bit in the UHR-SIG common field in non-OFDMA to keep a two symbol UHR-SIG (transmitted using MCS0) in SU transmission
  We like the ideas of 5-bit MCS field [10, 13], 3-bit Nss field [12-13] in non-MU-MIMO, 2-bit UEQM pattern field [13], and 4-bit spatial configuration field [10-13]
    Further propose to reuse the 4-bit 11ax Spatial configuration encoding in the MU-MIMO user field

## Slide 9: Signaling Discussion for Other Features
CoBF
  In UHR, propose that CoBF is only applicable to non-OFDMA transmission
  We proposed in [14] to include the following signaling in preamble
    An indication of a CoBF transmission
    Indicate a 2nd BSS color (separate from the version independent BSS Color) for a 2nd AP
    A 1-bit indication in the MU-MIMO user field format to differentiate the two BSSs and avoid STA ID collision
C-SR
  In UHR, propose that C-SR is only applicable to SU transmission in each BSS
  In C-SR, synchronization and common L-SIG, RL-SIG and U-SIG are desirable to make U-SIG reliable
    Need an indication of a C-SR transmission as well as a 2nd BSS color for a 2nd AP, similar to CoBF
IM [15]
  In UHR, IM should be for non-MU-MIMO transmission only, at least applicable to single-BSS SU transmission
  Need to indicate an IM transmission, in the case of non-OFDMA

## Slide 10: U-SIG Design in MU PPDU
Use U-SIG-2 B2 to indicate
  C-SR ON/OFF in SU transmission
  CoBF ON/OFF in non-OFDMA MU-MIMO
Use U-SIG-1 B20-B25 to indicate the 2nd BSS Color for CoBF/C-SR
  Otherwise, these 6 bits use same definition as in 11be, i.e., B20-B24 of U-SIG-1 are Disregard bits and B25 of U-SIG-1 is a Validate bit
 | Bits | Field | Number of Bits
U-SIG-1 | B0-B2 | PHY Version Identifier | 3
 | B3-B5 | Bandwidth | 3
 | B6 | UL/DL | 1
 | B7-B12 | 1st BSS Color | 6
 | B13-B19 | TXOP | 7
 | B20-B25 | 2nd BSS Color in CoBF/CSR or same definition as in 11be in other cases | 6
U-SIG-2 | B0-B1 | PPDU Type And Compression Mode | 2
 | B2 | CoBF/CSR indication | 1
 | B3-B7 | Punctured Channel Information | 5
 | B8 | Validate | 1
 | B9-B10 | UHR-SIG MCS | 2
 | B11-B15 | Number Of UHR-SIG Symbols | 5
 | B16-B19 | CRC | 4
 | B20-B25 | Tail | 6
Leave 1 Validate bit unchanged

## Slide 11: UHR-SIG Design in MU PPDU
Use a Disregard bit B13 in UHR-SIG common field in non-OFDMA transmission to indicate Interference Mitigation (IM) ON/OFF
Non-OFDMA with advanced feature ON | Bits | Field | Number of Bits
UHR-SIG Common | B0-B3 | Spatial Reuse | 4
 | B4-B5 | GI+LTF Size | 2
 | B6-B8 | Number Of UHR-LTF Symbols | 3
 | B9 | LDPC Extra Symbol Segment | 1
 | B10-B11 | Pre-FEC Padding Factor | 2
 | B12 | PE Disambiguity | 1
 | B13 | IM indication | 1
 | B14-B15 | Disregard | 2
 | B16-B18 | Number of Non-OFDMA Users | 3

## Slide 12: Summary
Discussed signaling for new features
  Multi-AP features: CoBF, C-SR
  User specific features: New MCS, spatial domain UEQM, 2x LDPC
  Scheme related to frequency resource allocation: IM
Presented our thoughts and proposal in U-SIG and UHR-SIG design

## Slide 13: Reference
IEEE 802.11be specification D7.0
11-24/0876r0, UHR PPDU PHY Version, Rui Cao, et al. (NXP)
11-24/1410r0, Legacy Preamble for ELR PPDU, Ross Jian Yu, et al. (Huawei)
11-24/1592r0, USIG fields in an ELR PPDU, Hari Ram Balakrishnan, et al. (NXP)
11-24/1186r1, New MCSs for 11bn Follow-up, Shengquan Hu, et al. (MediaTek)
11-23/1985r5, Longer LDPC Codeword, Rethna Pulikkoonattu, et al. (Broadcom/Qualcomm)
11-24/0474r3, UHR Unequal Modulation Pattern and New Mcs, Rui Cao, et al. (NXP)
11-24/498r2, Unequal Modulation in MIMO TXBF and New MCS for 11bn, Alice Chen, et al. (Qualcomm)
11-24/1409r0, Unequal Pattern Discussion Follow-up, Ross Jian Yu, et al. (Huawei)
11-24/1427r0, Signaling for MCS and UEQM in 11bn, Dongguk Lim, et al. (LG Electronics)
11-24/1411r1, Signaling for UHR PPDU, Ross Jian Yu, et al. (Huawei)
11-24/1461r0, UHR preamble signaling, Sigurd Schelstraete, et al. (MaxLinear)
11-24/1695r0, 11bn Signaling Design for Extra MCS, UEQM, 2xLDPC, You-Wei Chen, et al. (MediaTek)
11-24/1822r0, CoBF Design for UHR, Sameer Vermani, et al. (Qualcomm)
11-24/1264r0, Supporting Rx Interference Mitigation in TGbn, Shimi Shilo, et al. (Huawei)

## Slide 14: SP 1
Do you agree to include the following to the 11bn SFD?
  Reuse the U-SIG field structure in EHT TB PPDUs for the U-SIG in UHR TB PPDUs
    PHY Version Identifier is set to 0 or 1 to differentiate EHT & UHR
    How to set Disregard and Validate bits is TBD
Y
N
A

## Slide 15: SP 2
Do you agree to include the following to the 11bn SFD?
  Use B20-B25 of U-SIG-1 in UHR MU PPDUs to indicate the 2nd AP’s BSS color subfield in the case of CoBF/C-SR ON
  Otherwise, these 6 bits use same definition as in 11be, i.e., B20-B24 of U-SIG-1 are Disregard bits and B25 of U-SIG-1 is a Validate bit
Y
N
A

## Slide 16: SP 3
Do you agree to include the following to the 11bn SFD?
  Use the following U-SIG field design in UHR MU PPDUs
  B20-B25 of U-SIG-1 are used to indicate the 2nd AP’s BSS color subfield in the case of CoBF/C-SR ON. Otherwise, these 6 bits use same definition as in 11be
Y/N/A
 | Bits | Field | Number of Bits
U-SIG-1 | B0-B2 | PHY Version Identifier | 3
 | B3-B5 | Bandwidth | 3
 | B6 | UL/DL | 1
 | B7-B12 | 1st BSS Color | 6
 | B13-B19 | TXOP | 7
 | B20-B25 | 2nd BSS Color for CoBF/CSR or same definition as in 11be in other cases | 6
U-SIG-2 | B0-B1 | PPDU Type And Compression Mode | 2
 | B2 | CoBF/CSR indication | 1
 | B3-B7 | Punctured Channel Information | 5
 | B8 | Validate | 1
 | B9-B10 | UHR-SIG MCS | 2
 | B11-B15 | Number Of UHR-SIG Symbols | 5
 | B16-B19 | CRC | 4
 | B20-B25 | Tail | 6

## Slide 17: SP 4
Do you agree to include the following to the 11bn SFD?
  Use the following UHR-SIG common field design in non-OFDMA transmission
  Use B13 to indicate Interference Mitigation (IM) ON/OFF
  Compared to 11be, one Disregard bit is removed
Y/N/A
Non-OFDMA with advanced feature ON | Bits | Field | Number of Bits
UHR-SIG Common | B0-B3 | Spatial Reuse | 4
 | B4-B5 | GI+LTF Size | 2
 | B6-B8 | Number Of UHR-LTF Symbols | 3
 | B9 | LDPC Extra Symbol Segment | 1
 | B10-B11 | Pre-FEC Padding Factor | 2
 | B12 | PE Disambiguity | 1
 | B13 | IM indication | 1
 | B14-B15 | Disregard | 2
 | B16-B18 | Number of Non-OFDMA Users | 3

## Slide 18: SP 5
Do you agree to include the following to the 11bn SFD?
  Add a 1-bit 2x LDPC subfield in the MU-MIMO and non-MU-MIMO user field formats in UHR-SIG
  The 2x LDPC subfield is set to 1 to indicate 2x LDPC (nominal codeword size of 3888) is used, or set to 0 to indicate it’s not used, if the coding scheme is LDPC
  The 2x LDPC subfield is set to 1 and validated at Rx if Coding is BCC (0)
Y
N
A

## Slide 19: SP 6
Do you agree to include the following to the 11bn SFD?
  Use 23 bits for the user field formats in the UHR MU PPDU
Y
N
A

## Slide 20: SP 7
Do you agree to include the following to the 11bn SFD?
  Use the 11ax 4-bit spatial configuration subfield design in the MU-MIMO user field format in the UHR MU PPDU
Y
N
A

## Slide 21: Appendix

## Slide 22: U-SIG in UHR MU PPDUs
Currently, U-SIG has 8 reserved bits
UHR-SIG common field has 3 or 4 reserved bits
  1 less Disregard bit in the non-OFDMA case to keep the UHR-SIG in SU transmission to two symbols with MCS0
 | Bits | Field | Number of Bits
U-SIG-1 | B0-B2 | PHY Version Identifier | 3
 | B3-B5 | Bandwidth | 3
 | B6 | UL/DL | 1
 | B7-B12 | BSS Color | 6
 | B13-B19 | TXOP | 7
 | B20-B24 | Disregard | 5
 | B25 | Validate | 1
U-SIG-2 | B0-B1 | PPDU Type And Compression Mode | 2
 | B2 | Validate | 1
 | B3-B7 | Punctured Channel Information | 5
 | B8 | Validate | 1
 | B9-B10 | UHR-SIG MCS | 2
 | B11-B15 | Number Of UHR-SIG Symbols | 5
 | B16-B19 | CRC | 4
 | B20-B25 | Tail | 6
Non-OFDMA | Bits | Field | Number of Bits
UHR-SIG Common | B0-B3 | Spatial Reuse | 4
 | B4-B5 | GI+LTF Size | 2
 | B6-B8 | Number Of UHR-LTF Symbols | 3
 | B9 | LDPC Extra Symbol Segment | 1
 | B10-B11 | Pre-FEC Padding Factor | 2
 | B12 | PE Disambiguity | 1
 | B13-B15 | Disregard | 3
 | B16-B18 | Number of Non-OFDMA Users | 3
OFDMA | Bits | Field | Number of Bits
UHR-SIG Common (Before RU Allocation) | B0-B3 | Spatial Reuse | 4
 | B4-B5 | GI+LTF Size | 2
 | B6-B8 | Number Of UHR-LTF Symbols | 3
 | B9 | LDPC Extra Symbol Segment | 1
 | B10-B11 | Pre-FEC Padding Factor | 2
 | B12 | PE Disambiguity | 1
 | B13-B16 | Disregard | 4