## Slide 1: UHR NDPA Signaling
Date: 2024-11-11
Authors:
Name | Affiliations | Address | Phone | Email
Mahmoud Hasabelnaby | Huawei |  |  | Mahmoud.Hasabelnaby@huawei.com
Junghoon Suh |  |  |  | 
Osama Aboul-Magd |  |  |  | 
Yan Xin |  |  |  | 
Sara Norouzi |  |  |  | 
Notes: September 2012

## Slide 2: Background: NDPA Signaling Design
The NDP Announcement frame in the current 802.11 baseline is shown as follows.
The first two bits in the Sounding Dialog Token field have been used to indicate the NDP Announcement Variant of the NDPA frame
  The first two bits are already consumed to indicate 4 variants, VHT, Ranging, HE and EHT.
[Challenge]: There is no remaining space in the NDPA Announcement frame to indicate new variants like UHR and future NDPA frame versions.

## Slide 3: Background: Co-BF Sounding Parameters
The sharing AP may share with the shared AP some info about how to transmit the NDP, such as:
  BW and punctured channel information.
  NLTF in NDP (P-matrix size).
  Starting stream index and number of spatial streams for shared AP in NDP.
  GI and UHR LTF Type.
  TXOP duration.
  …..
In this contribution, we extend the NDP Announcement frame to accommodate the UHR and beyond variants, as well as considering the Co-BF sounding parameters, as discussed next.

## Slide 4: Proposed UHR NDPA Signaling Indication (1/2)
Frame Control | Duration | RA | TA | Sounding Dialog Token | Special NDPA STA Info | STA Info List | FCS
2 | 2 | 6 | 6 | 1 | 0 or 4 | 2 or 4 (Variant dependent) | 4
Frame Control | Duration | RA | TA | Sounding Dialog Token | Special NDPA STA Info | STA Info List | FCS
2 | 2 | 6 | 6 | 1 | 0 or 4 |  | 4
or
If the Sounding Dialog Token, with NDP Announcement Variant subfield equals zero, is followed by a STA Info field containing an AID between 1 and 2007, this NDPA frame corresponds to the VHT.
If the Sounding Dialog Token, with NDP Announcement Variant subfield equals zero, is followed by a STA Info field containing a “Special AID” greater than 2007 (e.g., a fixed value in the range of 2008 and 2047), the UHR STA will detect that this is a UHR NDPA frame.
Octets

## Slide 5: Proposed UHR NDPA Signaling Indication
An advantage of accommodating the UHR and Beyond NDPA variants indication alongside the VHT variant is:
  it allows for easy extension of the STA Info field size to 2×K bytes (with K = 3, 4, …) if needed, especially for future generations.
    This only requires setting each Disambiguation bit to 1.
In contrast, accommodating the UHR and Beyond NDPA variants indication with HE or EHT variants would pose challenges for the STA Info field expansion (if needed for future generations) since they use AID 11.

## Slide 6: Option 1: Proposed UHR NDPA Signaling Design
Frame Control | Duration | RA | TA | Sounding Dialog Token | Special NDPA STA Info | Co-BF NDPA Info | STA Info List | FCS
2 | 2 | 6 | 6 | 1 | 0 or 4 | 0 or 4 | 2 or 4 (Variant dependent) | 4
Frame Control | Duration | RA | TA | Sounding Dialog Token | Special NDPA STA Info | Co-BF NDPA Info | STA Info List | FCS
2 | 2 | 6 | 6 | 1 | 0 or 4 | 0 or 4 |  | 4
Octets
B0 B11 | B12 B14 | B15 | B16 B26 | B27 | B28 B31
Special AID | NDPA Extended Variant Types | Co-BF NDPA Info Flag | Reserved or other TBD Info | Disambiguation | Reserved or other TBD Info
12 | 3 | 1 | 11 | 1 | 4
Bits
Value | NDPA Extended Variant
0 | UHR NDP Announcement Frame
1-7 | Reserved for future generations
Indicate the presence of the Co-BF Info field

## Slide 7: Option 1: Proposed UHR NDPA Signaling Design
The Shared AP BSS Color (6 bits) is utilized to distinguish Co-BF NDPA Info across different shared APs, if applicable.
Other shorter AP identifiers may be used, allowing for additional bit savings.
  This frees up more space for incorporating more control information parameters (if needed) to be shared with the Shared AP.
Frame Control | Duration | RA | TA | Sounding Dialog Token | Special NDPA STA Info | Co-BF NDPA Info | STA Info List | FCS
2 | 2 | 6 | 6 | 1 | 0 or 4 | 0 or 4 | 2 or 4 (Variant dependent) | 4
Frame Control | Duration | RA | TA | Sounding Dialog Token | Special NDPA STA Info | Co-BF NDPA Info | STA Info List | FCS
2 | 2 | 6 | 6 | 1 | 0 or 4 | 0 or 4 |  | 4
Octets
B0 B5 | B6 B10 | B11 | B12 B14 | B15 B17 | B18 | B19 B25 | B26 | B27 | B28 B30 | B31
Shared AP BSS Color | Punctured Channel Info | Disambiguation | Starting of SS | NSS | GI AND UHR-LTF Type | Tx EVM or other TBD Info | N_LTF | Disambiguation | BW | Sounding Type
6 | 5 | 1 | 3 | 3 | 1 | 7 | 1 | 1 | 3 | 1
Bits
Avoid the wrong detection of AID
Avoid the wrong detection of AID
TXOP Info may be interpreted from the Duration field

## Slide 8: Option 2: Proposed UHR NDPA Signaling Design
Frame Control | Duration | RA | TA | Sounding Dialog Token | Special NDPA STA Info | Co-BF NDPA Info | STA Info List | FCS
2 | 2 | 6 | 6 | 1 | 0 or 4 | 0 or 4 | 2 or 4 (Variant dependent) | 4
Frame Control | Duration | RA | TA | Sounding Dialog Token | Special NDPA STA Info | Co-BF NDPA Info | STA Info List | FCS
2 | 2 | 6 | 6 | 1 | 0 or 4 | 0 or 4 |  | 4
B0 B11 | B12 B14 | B15 | B16 B18 | B19 B21 | B22 B26 | B27 | B28 | B29 B31
Special AID | NDPA Extended Variant Types | Co-BF NDPA Info Flag | Reserved | BW | Punctured Channel Info | Disambiguation | Sounding Type | Reserved
12 | 3 | 1 | 3 | 3 | 5 | 1 | 1 | 3
Octets
Bits
In option 2, some Co-BF Info parameters can be included in the Special NDPA STA Info field.
This saves more space at the Co-BF NDPA Info field to accommodate additional control information, if needed.
TXOP Info may be interpreted from the Duration field

## Slide 9: Option 2: Proposed UHR NDPA Signaling Design
Frame Control | Duration | RA | TA | Sounding Dialog Token | Special NDPA STA Info | Co-BF NDPA Info | STA Info List | FCS
2 | 2 | 6 | 6 | 1 | 0 or 4 | 0 or 4 | 2 or 4 (Variant dependent) | 4
Frame Control | Duration | RA | TA | Sounding Dialog Token | Special NDPA STA Info | Co-BF NDPA Info | STA Info List | FCS
2 | 2 | 6 | 6 | 1 | 0 or 4 | 0 or 4 |  | 4
Octets
Bits
TXOP Info may be interpreted from the Duration field
B0 B5 | B6 B8 | B9 B10 | B11 | B12 B14 | B15 B21 | B22 B24 | B25 B26 | B27 | B28 B31
Shared AP BSS Color | Starting of SS | GI AND UHR-LTF Type | Disambiguation | NSS | Tx EVM or other TBD Info | Reserved or other TBD Info | N_LTF | Disambiguation | Reserved or other TBD Info
6 | 3 | 2 | 1 | 3 | 7 | 3 | 2 | 1 | 4

## Slide 10: Summary
In this contribution, we extended the NDP Announcement frame to accommodate the UHR and beyond variants, as well as considering the Co-BF sounding parameters.
Particularly, we propose indicating UHR and Beyond NDPA variants alongside the VHT variant by setting the value of NDPA Variant subfield in the Sounding Dialog Token field to 0.
If the Sounding Dialog Token (with NDPA Variant = 0) is followed by a STA Info field containing:
  an AID12 in the range 1-2007, the NDPA frame corresponds to VHT.
  a “Special AID” (e.g., fixed value between 2008-2047), the UHR STA recognizes this as a UHR NDPA frame.
Benefits of VHT Variant Usage for UHR and Beyond NDPA Variants Indication:
  This simplifies STA Info field expansion to 2×K bytes (where K = 3, 4, …), if needed, enabling future scalability by simply setting every disambiguation bit to 1.
  Shared AP BSS Color (6 bits) or other “shorter” AP IDs can be used to distinguish the Co-BF NDPA Info field across different APs, freeing space for more control info, instead of using the first 11 or 12 bits for the shared AP ID.

## Slide 11: References
Junghoon Suh, et. al., “11-21/1977r0 NDPA for Future Amendments”.
Sameer Vermani, et. al., “11-24/1542r0 Sounding Schemes for Coordinated Beamforming”.
IEEE P802.11-REVme/D5.0
IEEE P802.11be/ D5.0