## Slide 1: UHR MU PPDU User Info Field Signaling
Date: 2024-11
Authors:

## Slide 2: Introduction
New PHY features are defined for UHR
  Unequal modulation
  New MCSs
  2x1944 LDPC code
Several contributions discuss about the UHR MU PPDU signaling the new features [1~5].
In this contribution, we proposes our preference of UHR-SIG design

## Slide 3: Recap: UHR MU PPDU
L-STF/LLTF/L-SIG/RL-SIG definition: no change
U-SIG: keep the encoding structure
  Version-independent fields (B1:B19): PHY version identifier  “1”
  Version-dependent fields
UHR-SIG: follow the same structure as EHT-SIG
  Common field: U-SIG over flow bits
  User specific field: changes needed to accommodate new features
L-SIG | RL-SIG
L-STF | LLTF
UHR-STF
UHR-LTF | UHR-Data
U-SIG
UHR-SIG

## Slide 4: New Features
UEQM: max four patterns per Nss
  Need 2-bits to indicate
New MCSs: four new MCS
  QPSK-2/3, 16QAM-2/3, 16QAM-5/6, 256QAM-2/3
  Expand current 4-bit to 5-bits
2x1944 code: 1-bit
Total Nss | 1st ss | 2nd ss | 3rd ss | 4th ss
2ss | M | M-1 |  | 
 | M | M-2 |  | 
3ss | M | M | M-1 | 
 | M | M | M-2 | 
 | M | M-1 | M-2 | 
4ss | M | M | M | M-1
 | M | M | M | M-2
 | M | M | M-1 | M-2
 | M | M-1 | M-1 | M-2

## Slide 5: User Field in UHR MU PPDU
Proposal: UHR user info field, expands 22-bits to 23-bits
Non-MUMIMO Allocation
  New MCS: expand to 5-bit MCS and shrink Nss to 3-bit (8 Nss)
  UEQM: 1-bit UEQM + 2-bit (BF and coding/Modulation pattern)
    Bit 19 set to 0 (EQM) : B20 (Beamforming) and B21 (Coding)
    Bit 19 set to 1 (UEQM): B20-B21 (Modulation pattern)
  One bit to indicate 2x1944 code
STA-ID B0-B10 | MCS B11-B15 | Nss B16-B18 | UEQM B19 | Beamforming B20 | Coding B21 | 2x1944 B22
STA-ID B0-B10 | MCS B11-B15 | UEQM B16 | Nss B17-B18 | Modulation pattern B20-B21 |  | 

## Slide 6: Non-MUMIMO Allocation (2)
Modulation pattern (B20-B21)
B20-B21 | Nss = 2 | Nss = 3 | Nss = 4
00 | [M, M-1] | [M, M, M-1] | [M, M, M, M-1]
01 | [M, M-2] | [M, M, M-2] | [M, M, M, M-2]
10 | Reserved | [M, M-1, M-2] | [M, M, M-1, M-2]
11 | Reserved | Reserved | [M, M-1, M-1, M-2]

## Slide 7: MUMIMO Allocation
  MUMIMO mode does not define unequal modulation
  Expand to 5-bit MCS subfield
  Reduce Spatial Configuration bits from 6 to 4, limit Nss,tot = 8
    same as HE-SIGB Spatial Configuration Table
  One bit to indicate 2x1944 code
STA-ID B0-B10 | MCS B11-B15 | Spatial configuration B16-B19 | Reserved B20 | Coding B21 | 2x1944 B22

## Slide 8: UHR SIG: Common field
U-SIG overflow bits for non-OFDMA transmission
  User info field increase to 23-bits
  SU transmission: good to keep UHR-SIG in two symbols for MCS0
    Total overflow bits: 20  19
UHR-SIG (U-SIG Overflow) | Spatial Reuse | 4
 | GI+LTF size | 2
 | Number of EHT-LTF symbols | 3
 | LDPC extra symbol segment | 1
 | Pre-FEC padding | 2
 | PE disambiguity | 1
 | Disregard | 43
 | Number of Non-OFDMA Users | 3
Total # of Overflow Bits |  | 19

## Slide 9: Summary
Propose UHR-SIG User info field design to indicate the new PHY features
  23-bits user info field design of non-MUMIMO and MUMIMO allocation
UHR-SIG U-SIG overflow bits for non-OFDMA transmission change to keep SU transmission to 2 symbols with MCS 0.

## Slide 10: Reference
[1] 11-24/1695, 11bn-signaling-design-for-extra-mcs-ueqm-2xldpc
[2] 11-24/1427, signaling-for-mcs-and-ueqm-in-11bn
[3] 11-24/1411, signaling-for-uhr-ppdu
[4] 11-24/1431, a-unified-signaling-scheme-for-eqm-and-ueqm
[5] 11-24-0876, uhr-ppdu-phy-version

## Slide 11: SP1
Do you agree that the “Disregard” bits reduce from 4 bits to 3 bits in UHR-SIG common field for a non-OFDMA transmission?
  Note: other bits definition unchanged

## Slide 12: SP2
Do you agree to define user info field for non-MUMIMO allocation in UHR MU PPDU as?
STA-ID B0-B10 | MCS B11-B15 | Nss B16-B18 | UEQM B19 | Beamforming B20 | Coding B21 | 2x1944 B22
STA-ID B0-B10 | MCS B11-B15 | UEQM B16 | Nss B17-B18 | Modulation pattern B20-B21 |  | 

## Slide 13: SP3
Do you agree to define user info field for MUMIMO allocation in UHR MU PPDU as?
STA-ID B0-B10 | MCS B11-B15 | Spatial configuration B16-B19 | Reserved B20 | Coding B21 | 2x1944 B22

## Slide 14: SP4
Do you support the four new MCSs are defined for both BCC and LDPC for UHR?
  Note: QPSK-2/3, 16QAM-2/3, 16QAM-5/6, 256QAM-2/3