## Slide 1
November 2024
Consideration on cascading channel switching for NPCA
Date: 2024-11-08
Authors:
Name | Affiliations | Address | Phone | email
Si-Chan Noh | Newracom |  |  | sc.noh@newracom.com
Joonsoo Lee |  |  |  | js.lee@newracom.com

## Slide 2: Abstract
This document discusses the NPCA channel switch triggering conditions for NPCA-supporting STAs from another perspective (i.e., not about the PPDU format, not based on TXOP/PPDU/Service Period(SP), etc) when the primary channel is occupied due to a transmission caused by the NPCA operation of OBSS

## Slide 3: Motivation
Non-Primary Channel Access (NPCA) channel switch trigger conditions have been discussed in TGbn [1-4]
  TXOP/PPDU/Service Period based NPCA
  Control frame exchange/Pre-HE and HE+ format
  TXOP/PPDU duration constraint to prevent inefficient NPCA
If OBSS’s transmissions that meet the above conditions occupy the MyBSS primary channel and these transmissions are caused by NPCA operations, should NPCA STAs perform channel switching?
  It may be needed to consider whether NPCA operation should be performed for all OBSS frames detected on the primary channel

## Slide 4: Channel switching for NPCA
The NPCA operation may increase spectral utilization of the unused secondary channel when the primary channel is occupied
However, it might be necessary to consider the advantages of NPCA when the BSS primary channel is occupied due to a transmission generated by NPCA operations between OBSS’s NPCA STAs
  When NPCA STAs are allowed to switch to the NPCA primary channel regardless of whether the OBSS frame is generated by NPCA operations, frequent channel switching may occur
    It can reduce power efficiency and degrade overall performance of the BSS
  Moreover, if a PPDU generated by OBSS NPCA STAs occupy the MyBSS primary channel, it can cause MyBSS NPCA STAs to switch to its NPCA primary channel(Ch1); this may also trigger another OBSS NPCA STAs, which use the aforementioned NPCA primary channel(Ch1) as their primary channel, to switch to their designated NPCA primary channel(Ch2)
    It can lead to cascading channel switching behavior, which may impact the entire network throughput

## Slide 5: Cascading channel switching for NPCA
If the NPCA channel switching conditions can be triggered by NPCA operation of an OBSS, we can consider it from two scenarios
  S1) When OBSS NPCA STAs switch to MyBSS primary channel
    The number of backoff contenders on the MyBSS primary channel could be increased
      OBSS NPCA STAs have an advantage, but we could consider the trade-off where this advantaged leads to disadvantage to MyBSS STAs
      If MyBSS STAs cannot access the channel, allowing MyBSS NPCA STAs to perform NPCA might be an efficient way
    However, there may be situations where waiting until the end of the frame exchange between OBSS’s NPCA STAs (i.e., at the time when switching back to their primary channel) on the MyBSS primary channel is more beneficial at some points than performing NPCA
      This is because we cannot ensure the NPCA primary channel for MyBSS NPCA STAs will be IDLE;
      In addition, since congestion due to OBSS NPCA STAs can be merely temporary, having MyBSS NPCA STAs switch channels while consuming power could reduce power effieciency
  S2) When MyBSS NPCA STAs switch channel due to NPCA operation of an OBSS
    In terms of OBSS that using the MyBSS NPCA primary channel as its BSS primary channel, this could increase the number of backoff contenders and potentially trigger NPCA operation in that OBSS
      It can bring P1) recursively

## Slide 6: Example of cascading channel switching
BSS1
BSS2
BSS3
AP1
AP2
AP3
OBSS TXOP
BSS1 NPCA
STAs switch
BSS1 NPCA STAs switch back
BSS1 NPCA
BSS3 NPCA
STAs switch
BSS3 NPCA STAs switch back
BSS2 NPCA
BSS2 NPCA
STAs switch
BSS2 NPCA STAs switch back
BSS3 NPCA
Description :
  The NPCA available channels of BSS1/BSS2 overlap with the primary channels of BSS2/BSS3, respectively
Scenario :
  BSS1 NPCA STAs switch channel to its NPCA primary channel
    BSS1 NPCA STAs contend with BSS2 STAs, and with the channel contention
  BSS2 NPCA STAs switch channel to its NPCA primary channel
    BSS2 NPCA STAs contend with BSS3 STAs, and with the channel contention
  BSS3 NPCA STAs switch channel to its NPCA primary channel
    BSS3 NPCA STAs contend with BSS_X STAs and with the channel contention
  ……
…
Freq.
BSS1 NPCA available channel
(BSS2 primary channel)
BSS2 NPCA available channel
(BSS3 primary channel)

## Slide 7: Prevent cascading channel switching
Since the NPCA primary channel during the NPCA operation can cause cascading channel switching of OBSS NPCA STAs, we consider methods to limit cascading channel switching
Proposal 1: Including an explicit indication in the PPDU to notify that this PPDU is generated from the NPCA operation
  If the NPCA STA initiates frame exchange on the NPCA primary channel with an ICF, it may include an indication within the ICF to prevent NPCA operation of OBSS; and/or
  Indicate the NPCA mark within the UHR SIG field when transmitting UHR PPDU format
When NPCA STAs overhear the NPCA indication on the primary channel, they may optionally choose whether to perform NPCA or not as follows :
  Opt 1) Do not perform NPCA until the OBSS NPCA STAs switch back to their primary channel
  Opt 2) Switching to NPCA primary channel to perform NPCA; After that, do not use untriggered transmission, considering the trade-off between the benefits of NPCA and the increase in backoff contenders due to NPCA
    Allow only the NPCA AP to attempt channel contention

## Slide 8: Summary
In this presentation, we discuss some approaches for NPCA STAs to mitigate the excessive NPCA which can cause cascading channel switching
  Including an explicit indication in the PPDU
    ICF when NPCA STAs initiate frame exchange on the NPCA primary channel; and/or
    Transmission of UHR PPDU format between NPCA STAs on the NPCA available channel
  Create an OBSS AP list that aligns with MyBSS primary channel

## Slide 9: Reference
[1] 24/0495r0, Non-Primary Channel Access (NPCA) - Follow up
[2] 24/0496r1, Secondary Channel Usage Follow Up
[3] 24/1115r1, Channel Switching Rules for NPCA
[4] 24/1259r0, SP-based non-primary channel access follow-up

## Slide 10: SP1
Do you agree to include an explicit indication in the PPDU(TBD) on the NPCA primary channel during NPCA operation?
  The details are TBD