## Slide 1: Management of the Established Multi-AP Coordination
Date: 2024-11-08
Authors:

## Slide 2: Introduction
11bn agreed to define a common framework of a M-AP Coordination [1]
Many contributions have discussed both the initial coordination phase and the operation phase of M-AP coordination [2-9]
  The initial coordination phase includes:
    M-AP Discovery/Advertisement
    Feature-specific negotiation
  The operation phase includes:
    Feature-specific operations
    Management of the enabled M-AP feature(s) (Enabling/Disabling/Adding)
In this contribution, we discuss the following points:
  Suspension of enabled M-AP features
  Termination of M-AP coordination
    Explicit request/announcement-based
    Automatic (timer-based)

## Slide 3: M-AP Coordination Framework
M-AP Discovery/Advertisement
  Each AP advertise its capabilities/ parameters for M-AP features
Feature-specific negotiation
  Two APs negotiate parameters required to enable M-AP feature(s)
  The APs may renegotiate/update the parameters of an enabled M-AP feature or disable it as needed
Termination of the M-AP coordination
  The two APs terminate their M-AP coordination, making it impossible to continue utilizing the M-AP feature
  Each AP may erase all parameters related to an established M-AP coordination when it determines that the coordination has been terminated
Feature-specific operations
  The two APs selectively utilize the enabled M-AP feature(s)
  Each feature may involve a specific/unique frame exchange sequence
Suspension of M-AP features
  The enabled M-AP features between the two APs are suspended when one of them becomes temporarily unavailable
Initial Coordination
Phase
Operation
Phase
Termination Phase

## Slide 4: Suspension of M-AP features
Temporal unavailability of the AP:
  An AP may experience periodic unavailability,
    when it enables SP-based power saving (PS) or when the link it operates on is periodically disabled
  An AP may also experience aperiodic unavailability,
    when it enables dynamic PS mode or when the link it operates on is disabled dynamically
Even if one of the two APs becomes temporarily unavailable, the established M-AP coordination between them should be maintained if both APs agree to do so
If an AP cannot participate in frame exchange sequences initiated by the other APs during its unavailability, it should inform the other APs in advance to prevent interoperability issues
Each AP should avoid attempting to use the M-AP feature with a coordinated AP during periods of that AP’s unavailability

## Slide 5: Suspension of M-AP features (cont’d)
Periodic unavailability of an AP can potentially be managed using mechanisms currently being discussed for addressing periodic IDC-related problems of non-AP STAs
  e.g., An AP may indicate its unavailability information in a management frame(e.g., M-AP beacon)
However, tracking aperiodic unavailability of all coordinated APs in real-time seems to be challenging
  This is because the frequency of frame exchanges between the two APs is expected to be insufficiently high
Therefore, a method should be considered to allow an AP to suspend M-AP operation when it detects that its coordinated AP has transitioned to a state where it cannot participate in the M-AP operation
  An AP expected to be temporally unavailable in the future should inform the other APs of it
  An AP cease further M-AP operations with the coordinated AP that has informed its temporal unavailability upon encountering a single failure
    The other APs would then resume trials of M-AP operations after confirming that the coordinated AP has become available

## Slide 6: Termination of M-AP Coordination
Explicit Request/Announcement-based Termination
  In some cases, an AP may decide to terminate M-AP coordination with another AP
    When this occur, the AP should announce its decision explicitly
    Upon receiving a frame indicating the termination of M-AP coordination, the receiving AP can consider its coordination with the transmitting AP to be terminated
Automatic Termination
  Situations may arise where a coordinated AP becomes unreachable or disappears without an explicit termination announcement,
    such as due to a power outage or an unexpected change in its operating channel
  To account for this, each AP should monitor the reachability of its coordinated APs
    If an AP does not receive any frames from a coordinated AP for a certain period, it may assume that the coordinated AP is unavailable for M-AP coordination

## Slide 7: Termination of M-AP Coordination (cont’d)
Automatic Termination (cont’d)
  To maintain established coordination with other AP(s), each AP should transmit at least one frame on the primary 20 MHz subchannel(s) of its coordinated AP(s)
    If each AP periodically transmits frames for M-AP discovery/advertisement, these frames can serve as keepalive frames for the ongoing M-AP coordination
  An AP will use a specific timeout value (M-AP Max Idle Period) to make termination decision
    Option 1: AP-specific value
      An AP indicates its M-AP Max Idle Period to the other APs, and the other APs respect the value for maintaining established coordination
    Option 2: Pre-defined value (Preferred)
      Each AP should consider a predefined M-AP Max Idle Period when determining the interval for transmitting M-AP discovery/advertisement frames

## Slide 8: Summary
The following elements of the common framework for M-AP coordination were discussed:
  Suspension of M-AP operation
    To handle temporal unavailability of the coordinated AP
  The Termination Stage
    Explicit request/Announcement-based termination
    Automatic termination

## Slide 9: Straw Poll 1
Do you agree to add the following text to the TGbn SFD?
  Established coordination between two APs can be terminated by an explicit request performed by one of the two APs.

## Slide 10: Straw Poll 2
Do you agree to add the following text to the TGbn SFD?
  Established coordination between two APs can be terminated without an explicit request when TBD conditions are met.
    Note: The TBD conditions are used to verify availability of the coordinated AP

## Slide 11: Straw Poll 3
Do you agree to add the following text to the TGbn SFD?
  Define a mechanism(s) for an AP to report its unavailability to coordinated APs, allowing them to suspend the use of enabled M-AP features.
    Details are TBD

## Slide 12: References
[1] 11-24/0209 Specification Framework for TGbn
[2] 11-23/1871 M-AP Coordinated Transmission framework
[3] 11-24/0084 Considerations on Multi-AP Operation – Follow Up
[4] 11-24/0453 Multi-AP Coordination and Roaming
[5] 11-24/0511 Requirements and Functionalities for Multi-AP Framework
[6] 11-24/1075 MAP coordination follow up
[7] 11-24/1217 Multi-AP Coordination Setup Scheme
[8] 11-24/1220 A Framework for Coordinated Access Points
[9] 11-24/1467 Framework of Multi-AP