## Slide 1: Control frames and MAPC for Colocated BSSID Set
Nov 2024
Authors:
Name | Affiliation | Phone | email
Brian Hart | Cisco Systems |  | brianh@cisco.com
Binita Gupta | Cisco Systems |  | 
Malcolm Smith | Cisco Systems |  | 
Juan Carlos Zuniga | Cisco Systems |  | 
Stephen Orr | Cisco Systems |  | 
Javier Contreras | Cisco Systems |  | 

## Slide 2: Situation (1/3) Colocated BSSID Set = Multiple BSSID Set xor Co-hosted BSSID Set
Transmitted BSSID (bold)
Nontransmitted BSSID (normal)
Overheads from 802.11’s xIFS and preamble means that MU+TB PPDUs are the key path to efficiency
Non-AP STAs are split across SSIDs on the same AP radio hardware via virtual APs and BSSs
  Common in the enterprise and now the home too (e.g., core devices + guest devices)
These virtual BSSs make up a Colocated BSSID Set, as one of:
  Multiple BSSID Set
    Beacon + Probe Response frame sharing/compression
    Used predominantly at 6 GHz; harder to use at 2.4/5 GHz due to legacy
  xor Co-hosted BSSID Set
    Separate Beacon + Probe Response frames for each BSSID
    Predominant VBSS mechanism at 2.4+5 GHz due to legacy
Colocated BSSID Set
Multiple BSSID Set
APa
APb
APc
APd
Co-hosted BSSID Set
APa
APb
APc
APd
xor
APa
Key:
APb
[1]

## Slide 3: Situation (2/3) Both kinds of sets are identified via similar signalling
Both kinds of sets are identified via the number of variable LSBs of the BSSID
  E.g., If the virtual BSSs’ BSSIDs can take the form of 0x012345x (x = 0x0...0xf), with a max of 16 BSSIDs in the set, then this is signaled as n = 4
Multiple BSSID Set [1]
Co-Hosted BSSID Set [1]

## Slide 4: Situation (3/3) Enhanced Control frame features are confined to Multiple BSSID Sets
11ax and 11be features are consistently defined for Multiple BSSID Sets but erratically defined for Co-hosted BSSID Sets:
  Both Multiple BSSID Sets and Co-hosted BSSID Sets
    BSS Color (§3.2 [1])
    Intra-BSS and inter-BSS PPDU classification (§26.2.2 [1])
    Dual NAV (§26.2.4 [1])
    Non-SRG & SRG OBSS PD level (§26.2.3, §26.10.2 [1])
    PSR-based SR (§26.10.3 [1])
  Multiple BSSID Sets only
    Rx Control Frame To MultiBSS (§9.4.2.247.2 [1]), which allows set-wide operation of:
      MU-RTS + CTS (§26.2.6.3 [1])
      NDPA + NDP (§26.7.3 [1])
      Trigger + TB PPDU (§26.5.2.2.1, §26.5.2.2.4, §26.5.2.3.1 [1])
      Multi-STA BA (§26.4.1 [1])
      HE dynamic SM power save (§26.14.4 [1])

## Slide 5: Three Problems Co-hosted BSSIDs + Multiple MBSSID Beacons lose out (etc)
Co-hosted BSSIDs cannot partake in the important features enabled by Rx Control Frame To MultiBSS feature
At 6 GHz, due to the Beacon frame length issue, a high number of SSIDs (and thence virtual APs) is enabled via multiple MBSSID Beacons
  Basically, a co-hosted set of a Multiple BSSID Sets
  But 802.11 has no language to account for this
    VBSSs are always one or the other
  Worse, the Rx Control Frame To MultiBSS feature-set is not available across the Multiple BSSID Sets
In C-TDMA, when a portion of the TXOP is granted to a follower AP or returned to the leader AP, that grant and return should apply at the Colocated BSSID Set level for efficiency
Colocated BSSID Set
MBSSID1
AP1a
AP1b
MBSSID2
AP2c
AP2d
Co-hosted BSSID Set
APa
APb
APc
APd
C1a
C1b
C2c
C2d
Ca
Cb
Cc
Cd
Key:
C
C
Non-AP STA that cannot participate in MultiBSS features in this TXOP
Non-AP STA that can participate in MultiBSS features in this TXOP

## Slide 6: Solution (1/5) High Level
Explicitly signal the Colocated BSSID Set
  Via the number of variable LSBs in the BSSID, sent in the UHR Operation element
  (Similar to Multiple BSSID Set / Co-hosted BSSID Set signaling)
Introduce the Rx Control Frame To Colocated BSSID Set field
  Use this to extend the Rx Control Frame To MultiBSS feature-set to all VAPs/VBSSs/VBSSIDs in the Colocated BSSID Set
  Wherever a feature is conditioned on “Rx Control Frame To MultiBSS” today, extend that condition, in the UHR draft, to be “Rx Control Frame To MultiBSS = 1 or Rx Control Frame To Colocated BSSID Set = 1”
    Or similar, since the details are always a little more involved
  Assume all information (PM, DL buffer sizes, BSR, SCS(QC), etc) is shared among APs of a Colocated BSSID Set
Colocated BSSID Set - can mix’n’match anything
Multiple BSSID Set1
AP1a
AP1b
AP2c
AP2d
Co-hosted BSSID Set3
AP3e
AP3f
APg
APh
Multiple BSSID Set2
AP4i
AP4j
Co-hosted BSSID Set5
AP5k
AP5l
APm
Multiple BSSID Set4
or leave anything out (with a sufficiently different BSSID)

## Slide 7: Solution (2/5) Need Colocated BSSID Set BSSID(s) analogous to Transmitted BSSID
Rx Control Frame To MultiBSS feature-set uses the Transmitted BSSID when sending control frames for the entire Multiple BSSID Set. Something similar is needed for a Colocated BSSID Set
Rx Control Frame To Colocated BSSID Set can go two ways:
  Option A: A Colocated BSSID Set has a single Colocated BSSID Set BSSID
    Complete aggregation & efficiency for UHR STAs, but certain legacy STAs can never participate
  Option B: A Colocated BSSID Set uses any (transmitted) BSSID in the set as a Colocated BSSID Set BSSID
    Complete aggregation & efficiency for UHR STAs + all legacy STAs have a way to participate
Key:
Participating Legacy Non-AP STA
Participating UHR Non-AP STA
Colocated BSSID Set
MBSSID1
AP1a
AP1b
MBSSID2
AP2c
X
AP2d
X
Colocated BSSID Set
MBSSID1
AP1a
AP1b
MBSSID2
AP2c
~
AP2d
~
Colocated BSSID Set
MBSSID1
AP1a
~
AP1b
~
MBSSID2
AP2c
AP2d
Option A
All TXOPs
Option B
Transmitted BSSID (bold)
AP2a
Colocated BSSID Set BSSID
Later TXOP
X
Legacy Non-AP STA that can never participate
~
Legacy Non-AP STA not participating in this TXOP
AP1a
Earlier TXOP

## Slide 8: Solution (3/5) Simplest if AIDs are unique across STAs of a Colocated BSSID Set
Simplest if AIDs are unique across STAs of a Colocated BSSID Set
  Since then the STAID is unique too
In a Multiple BSSID Set, the first 2n AIDs are reserved to indicate groupcast traffic in the TIM element in Beacon frames
  This is still only needed for Multiple BSSID Sets
  Aka no need to expand to a Colocated BSSID Set since the co-hosted BSSIDs and “nothing” BSSIDs still have their own Beacon frames

## Slide 9: Solution (4/5) C-TDMA lets All Clients of a Colocated BSSID Set Be Served in one TXOP
As we have seen, a virtual AP in a Colocated BSSID Set could use these “Colocated BSSID Set” control frames to avoid the overheads of C-TDMA for all its UHR STAs
If there are legacy non-AP STAs in a different Co-hosted/Multiple BSSID Set than the TXOP-holding AP, it can either:
  Perform “TXOP-handover-to-self”(!?) (with dashed boxes) via C-TDMA, or
  Perform chained TXOPs (without the dashed boxes)  This should be permitted
AP1a (initial TXOP holder)
Colocated BSSID Set
MBSSID1
AP1a
AP1b
Cohosted2
AP2c
AP2d
C1a
C1 w
C1b
C1x
C2c
C2y
C2d
C2z
C1a/b/w/x
AP2c (chained TXOP)
C2c or C2y
AP2d (chained TXOP)
C2d or C2z
Initial TXOP
TXOP handover
TXOP handover
Chained TXOP
TXOP handover
Chained TXOP
TXOP handover
NAV
(TXOP return)
(TXOP return)
Note: no regulatory impediment to AP2c direct granting the remainder of the TXOP to AP2d instead of a return to AP1a then grant to AP2d

## Slide 10: Solution (5/5) MAPC Should be Between Colocated BSSID Sets not between APs
As an example, MAPC technique, consider a leader virtual AP granting a portion of a TXOP via C-TDMA to a follower virtual AP
  Each virtual AP is part of a Colocated BSSID Set
For maximum efficiency, the scheduler for the follower Colocated BSSID Set should be able to transmit to and/or trigger any non-STA (or multiple STAs) across its Colocated BSSID Set
  Still based on traffic priority, MAPC agreements, etc
Thus, a TXOP grant (via TXS or whatever) should be a grant to a Colocated BSSID Set via its Colocated BSSID Set BSSID(s)
Ditto, for maximum efficiency, when this follower Colocated BSSID Set returns the remainder of the TXOP, then the scheduler for the leader Colocated BSSID Set should be able to transmit to and/or trigger any non-STA (or multiple STAs) across its Colocated BSSID Set
Bottom line: in C-TDMA (and more broadly, MAPC), resource grants and returns (and coordination) should be at the Colocated BSSID Set level (if present), with the Colocated BSSID Set BSSID(s) as addresses
Leader AP(s) of Colocated BSSID Set1 (initial TXOP holder)
Clients of Colocated BSSID Set1
TXOP portion(s) within Colocated BSSID Set1
TXOP handover
TXOP handover
TXOP portion(s) within Colocated BSSID Set2
NAV
TXOP handover
TXOP handover
TXOP portion(s) within Colocated BSSID Set1
Follower AP(s) of Colocated BSSID Set2
Clients of Colocated BSSID Set2

## Slide 11: Summary
Great opportunity for efficiency improvements via combining users across
  The multiple Multiple BSSID Sets at 6 GHz, and
  The Co-hosted BSSID Set at 2.4+5 GHz
… by enlarging the “Rx Control Frame To MultiBSS” feature to “Rx Control Frame To Colocated BSSID Set”
  MU-RTS + CTS, NDPA + NDP, Trigger + TB PPDU, Multi-STA BA and HE Dynamic SM Power Save across all virtual BSSs
The Colocated BSSID Set approach avoids the overheads of C-TDMA to serve the associated non-AP UHR STAs
Still C-TDMA is needed to serve the associated non-AP legacy STAs within the same TXOP
  And there is an opportunity to optimize the C-TDMA-to-self handover via APa  APb  APc
  Rather than APa  APb  APa  APc  APa
Finally, when “APs” grant or return a portion of a TXOP to each other via C-TDMA (or any resource via any MAPC technique), to minimize overheads, the grant or return should be at the Colocated BSSID Set level (if present)

## Slide 12: Strawpoll 1
Do you agree to add the following text to the 11bn SFD:
  The 802.11bn draft shall define how a Colocated BSSID Set can be signaled
  The 802.11bn draft shall define how exchanges that involve control frames (namely MU-RTS + CTS, NDPA + NDP, Trigger + TB PPDU, Multi-STA BA and HE dynamic SM power save) can include multiple STAs associated to multiple APs of the same Colocated BSSID Set
Y / N / A

## Slide 13: Strawpoll 2
Do you agree to add the following text to the 11bn SFD:
  The 802.11bn draft shall define how MAPC-related resource sharing can operate at the Colocated BSSID Set level
Y / N / A

## Slide 14: References
[1] 802.11REVme Draft 7.0

## Slide 15: Backup