## Slide 1: COBF/COSR PPDU Consideration and U-SIG Signaling
Date: 2024-12-09
Authors:
Name | Affiliations | Address | Phone | Email
You-Wei Chen | Mediatek | 2840 Junction Ave. San Jose, CA, 95134 |  | You-Wei.Chen@mediatek.com
Jianhan Liu |  |  |  | 
Shengquan Hu |  |  |  | 
Julia Feng |  |  |  | 
Thomas Pare |  |  |  | 

## Slide 2: Introduction
COBF/COSR motion passed in IEEE [1].
    The Coordinated beamforming (COBF) transmission phase in 802.11bn shall be limited to 2 APs.
    The pre-UHR portion (the portion up-to and including UHR-SIG) of the COBF PPDU shall be transmitted in a non-beamformed (omni) manner.
    The pre-UHR portion of a COBF PPDU shall have identical content across two APs.
    COBF data transmission shall be indicated in the U-SIG for IEEE802.11bn .
    In a COBF transmission, the maximum number of spatial streams given to one user will be 2.
High-level considerations from PHY point of view:
  Minimize the modifications from 11be.
  Have a similar design for COBF and COSR.
  Some proposal [2][3] were presented. In this presentation, we also propose that to have a common U-SIG for COBF and COSR.

## Slide 3: Common U-SIG
It is preferred to have a common U-SIG for COBF and COSR.
For the intended and third-party STA, they can benefit from the common U-SIG for hidden node and preamble collision issues:
    It honors the version independent fields, e.g., TXOP (less collision)
    It checks the BSS colors and can terminates its RX processer. (save power)
AP1
non-AP STA2
AP2
non-AP STA1
non-AP STA3

## Slide 4: COBF/COSR preamble
L-preamble
U-SIG
UHR-SIG
…
If COBF then follow non-OFDMA MU-MIMO
If COSR then follow SU
We propose that COBF and COSR
    Have Common U-SIG
    Limit the transmission phase to 2 AP only. (can carry 2 BSS colors in U-SIG to relax MAC concerns, e.g., BSS color management, AID collision)
    Do not mix with OFDMA.
        Avoid complexity for the first generation of COBF and COSR.
BSS Color 1 and BSS Color 2
COBF/ COSR indication.

## Slide 5: PPDU type and compression mode field
In 11be, there is only one validate entry left, which is used for ELR. (Motion passed [1])
To indicate COBF and COSR, we can combine COBF and COSR with the existing entries.
  COBF and COSR only support DL
  Need an additional bit to distinguish them.
PPDU type and compression mode | UHR PPDU format | Note
0 | UHR MU | DL OFDMA (non-MU MIMO and MU MIMO)
1 | UHR MU | SU/ DL COSR
2 | UHR MU | DL non-OFDMA MU-MIMO/ DL COBF
3 | UHR ELR | DL ELR

## Slide 6: U-SIG in MU PPDU for COBF/COSR
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25
U-SIG1 | PHY version identifier |  |  | Bandwidth |  |  | UL/DL | BSS color |  |  |  |  |  | TXOP |  |  |  |  |  |  | Disregard |  |  |  |  | Validate
U-SIG2 | PPDU Type |  | COBF/ COSR | punctured channel info |  |  |  |  | Validate | UHR-SIG MCS |  | Number Of UHR-SIG Symbols |  |  |  |  | CRC |  |  |  | Tail |  |  |  |  | 
A validate bit (B2) in 11be can be used as the COBF/COSR indicator.
  If PPDU type and compression mode set to 1:
    Set to 1: SU
    Set to 0: DL COSR SU
  If PPDU type and compression mode set to 2:
    Set to 1: non-OFDMA MU-MIMO
    Set to 0: DL COBF non-OFDMA MU-MIMO

## Slide 7: Straw Poll #1
Do you support that 802.11bn defines:
  COBF only applied in DL non-OFDMA MU MIMO transmission
  COSR only applied in UHR SU transmission

## Slide 8: Straw Poll #2
Do you support that 802.11bn combining ‘PPDU type and compression mode’ and ‘B2’ in U-SIG2 to indicate DL COSR SU and DL COBF non-OFDMA MU-MIMO?
  If PPDU type and compression mode set to 1:
    B2 set to 1: SU
    B2 set to 0: DL COSR SU
  If PPDU type and compression mode set to 2:
    B2 set to 1: non-OFDMA MU-MIMO
    B2 set to 0: DL COBF non-OFDMA MU-MIMO

## Slide 9: Straw Poll #3
Do you agree to include the following to the 11bn SFD?
  CoBF is only applied in DL non-OFDMA MU MIMO transmission
  C-SR is only applied in UHR DL SU transmission in each BSS
  The entire U-SIG format in a UHR MU PPDU is as in the following figure
Supporting doc: 11-24/1834r4, 11-24/1831r3, 11-24/1864r1

## Slide 10: References
[1] TGbn Motions List - Part 1, 24/171r21
[2] UHR U-SIG and UHR-SIG common field general design, 24/1831r2
[3] 11bn Non-ELR Signaling Design for New Features, 24/1834r3