## Slide 1: Universal Sounding and NDPA Signaling
Date: 2024-11-11
Authors:
Name | Affiliations | Address | Phone | Email
You-Wei Chen | Mediatek | 2840 Junction Ave. San Jose, CA, 95134 |  | You-Wei.Chen@mediatek.com
Jianhan Liu |  |  |  | 
Kaiying Lu |  |  |  | 
Julia Feng |  |  |  | 
Huai-Yan Feng |  |  |  | 
Thomas Pare |  |  |  | 

## Slide 2: Introduction
Sounding sequence was discussed in the previous IEEE meeting [1-3].
In this time, we would like to follow up our previous contribution [1] and present the universal sounding concept. We will also discuss maximum number of spatial stream supported and NDPA signaling.

## Slide 3: Universal sounding sequence
A universal sounding can be applied for MU TB sounding and coordinated sounding [1].
  From non-AP STA point of view, the sounding sequences are transparent.
  All the sounding sequence is ‘per-BSS’ based.
  Responding AP follows the instructions in NDPA to perform NDP transmission.
NDPA
BFRP
BFR
NDP
If containing information to shared AP:
No: TB sounding sequence in 11ax/be/bn.
Yes: Sounding sequence for COBF

## Slide 4: Sounding sequence for COBF
AP1 uses NDPA to inform AP2 how to perform the NDP transmission.
  For exmaple, in the NDPA to AP2, we can use a starting spatial stream (SS) index to indicate:
      Starting from the first stream: NDP comes solely from AP2
      Starting from the fifth stream: a joint NDP
AP1
AP2
NDPA
NDP
NDP
Shared AP starting SS index is 0 or 1.

## Slide 5: Maximum number of SS consideration
In 11ax/be, the mandatory support for Non-AP STA is 4 SS. For 11bn, we propose to have the below mandatory number of SS support:
      4 is mandatory except for Non-AP STA with 20 MHz-Only Limited Capabilities Support subfield equal to 1.
      8 is optional for DL MU-MIMO and sounding NDP
    On the other hand, the main use case discussed in COBF [2], the maximum required NSS is 4. To avoid complexity for the first generation of COBF, it is desired to limit the total maximum NSS=4 (across all users) for COBF data transmission.
    If NSS=4 is mandatory in 11bn, then COBF sequential sounding (NDP solely from the responding AP) is conditional mandatory.

## Slide 6: NDPA variant
In 11be, currently there is no reserved bit to indicate more NDPA variant.
A straightforward extension is indicating EHT and beyond NDPA variant together and use a special STA info field to indicate NDPA variant.
      It should be placed right after Sounding Dialog Token field.
EHT and beyond NDPA

## Slide 7: NDPA signaling for Universal Sounding
NDPA version can be indicated in a special STA info field with a special AID.
It is desirable that the NDPA can carry all the information, e.g., common information (bandwidth, TXOP, punctured channel info…) and SS configuration (number of LTF, starting SS, NSS, GI) to the responding AP. Similar discussion in [4].
In this case, the responding AP can simply copy the information in NDPA to perform NDP.
Disambiguation subfield (B27) should set to 1 to prevent a VHT STA from wrongly identifying its AID.
 | 0 | 1 |  |  | 10 | 11 |  | 13 | 14 |  | 17 |  | 26 | 27 | 28 | 29 | 30 | 31
Special STA info field | Special AID11 (e.g., 2047) |  |  |  |  | NDPA version |  |  | Common Info | Punctured channel info | Punctured channel info | Punctured channel info | Sounding type | Disambiguation | Common Info | Sounding type |  | Reserved
2nd STA info field | AID11 (Responding AP identifier) |  |  |  |  | Common Info/ SS configuration |  |  | Shared AP starting SS index | Number of LTF | Shared AP Starting SS |  |  | Disambiguation | Common Info/ SS configuration |  | GI+LTF Size | Reserved
One bit in the AP STA info field, e.g., B17, can be used for starting SS indication

## Slide 8: Summary
We propose that:
802.11bn defines a universal sounding for MU TB sounding and COBF sounding.
Maximum NSS for sounding NDP and the maximum total NSS (across all users) for UHR DL MU-MIMO and COBF PPDUs
    4 is mandatory
NDPA signaling for Universal sounding sequences.

## Slide 9: Straw Poll #1
Do you support that 802.11bn uses the same sounding sequence for MU TB sounding and COBF sounding?

## Slide 10: Straw Poll #2
Do you support for COBF that “Starting SS” in NDPA indicates that:
      Value 0: Starting from the first stream (NDP comes solely from the responding AP)
      Value 1: Starting from the fifth stream (Joint NDP)

## Slide 11: Straw Poll #3
Do you support the following on the maximum number of spatial streams supported for reception of sounding NDP in UHR and the maximum total number of streams (across all users) supported for reception in UHR DL MU-MIMO and CoBF PPDUs?
      4 is mandatory except for Non-AP STA with 20 MHz-Only Limited Capabilities Support subfield equal to 1.
      8 is optional for DL MU-MIMO and sounding NDP (Note: More than 4 is not allowed for COBF PPDUs)

## Slide 12: Straw Poll #4
Do you support making the COBF sequential sounding support to be conditional mandatory if the device supports COBF ?

## Slide 13: Straw Poll #5
Do you support to include the following signaling design for NDPA to the 11bn SFD?
  NDPA Version Identifier set to 0 for COBF sounding in UHR
  Number of LTF symbols set to 0 and 1 for 4 and 8 symbols, respectively
  Starting Spatial Stream set to 0 and 1 for the 1st and 5th streams, respectively
  Number of spatial streams set to 0 and 1 for the 4 and 8 streams, respectively
  LTF+GI set to 0 and 1 for 2x LTF+0.8us GI and 2x LTF+1.6us GI, respectively
 | 0 |  |  | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 |  | 26 | 27 | 28 |  | 30 | 31
1st STA Info field | AID11: 2047 |  |  |  | NDPA version |  |  | BSS Color |  |  | Shared AP starting SS index |  |  | TXOP | Sounding type |  | Disambiguation | Bandwidth | Sounding type |  | Reserved
2nd STA Info field | AID11 (Responding AP AID) |  |  |  | Punctured Channel Info. |  |  | Shared AP number of SS |  | Number of LTF Symbols | Starting Spatial Stream | Number of Spatial Streams | LTF+GI | Reserved |  |  | Disambiguation | Reserved |  | GI+LTF Size | Reserved

## Slide 14: References
[1] Coordinated Sounding for CoBF, 24/1582r0
[2] Sounding Schemes for Coordinated Beamforming, 24/1542r0
[3] Sounding Design for C-BF, 24/1568r0
[4] Backward Compatible Sounding for CoBF, 24/1835r0