## Slide 1: Further Consideration for NPCA Operation
Date: 2024-11-05
Authors:

## Slide 2: Introduction
NPCA in TGbn SFD [1]
  [Motion #11]: TGbn defines a mode of operation that enables a STA to access the secondary channel while the primary channel is known to be busy due to OBSS traffic or other TBD conditions.
NPCA operation can increase the transmission opportunities when the primary channel is busy [1, 2]
  It can reduce the latency of data delivery, especially for the low latency(/urgent) traffic
Therefore, it would be better for STA to have more NPCA chances especially when STA has low latency (higher priority) traffic
Current NPCA switching condition is based on the OBSS traffic but we can consider other conditions for more NPCA opportunities

## Slide 3: NPCA considering P2P transmission
P2P transmission in Intra-BSS looks very similar to OBSS transmission in terms of resource utilization
While P2P STA (STA3) communicates with the peer STA (STA4) on primary channel, the AP and non-AP STAs (STA1, 2) that detect the P2P transmission can not use the primary channel
We can consider Intra-BSS P2P transmission as a condition for NPCA operation

## Slide 4: NPCA considering P2P transmission
NPCA STA may switch to NPCA PCH when the NPCA STA detects Intra-BSS DL PPDU (e.g., DL/UL flag = DL)
  NPCA AP regards the Intra-BSS DL PPDU as P2P PPDU
  NPCA non-AP STA, for the Intra-BSS DL PPDU that is not addressed to the non-AP STA
They can perform NPCA operation during the duration indicated in the P2P PPDU
Non-AP STA can enable this mode when it has low latency(/urgent) traffic stream with AP
Non-AP STA may disable this operation if the STA wants to save more power

## Slide 5: NPCA considering P2P transmission
If the AP does not communicate with any non-AP STA during the Intra-BSS PPDU length, the AP returns to primary channel before the end of the PPDU

## Slide 6: NPCA considering P2P transmission
After switching to NPCA PCH, if the non-AP STA does not receive a frame from AP during the Intra-BSS PPDU length, the non-AP STA returns to primary channel before the end of the duration of the PPDU

## Slide 7: Conclusion
Currently, NPCA STA can switch to NPCA channel on the condition of OBSS traffic on primary channel
We proposed NPCA operation considering P2P transmission
  STA switches to NPCA channel when the STA detects Intra-BSS DL PPDU
  If the STA does not communicate with AP/non-AP STA during the PPDU length, the STA returns to primary channel before the end of the PPDU
This will increase TX opportunities by more NPCA usages and it will be very useful especially when non-AP STA has low latency traffic or urgent traffic
Non-AP STA can also decide to disable this mode if it wants to reduce power consumption using the Intra-BSS PPDU PS

## Slide 8: References
[1] 24/0209r7, Specification Framework for TGbn
[2] 24/1762, PDT-MAC-NPCA

## Slide 9: Straw Poll
Do you agree the following text?
  NPCA capable STA may switch to NPCA primary channel when it receives an intra-BSS DL PPDU on primary channel
    Detailed conditions and procedures are TBD.