## Slide 1: A Technical Proposal for TGbi
Date: 2024-11-13
Authors:

## Slide 2: Abstract
The reason for a personal motion in the mid-week plenary

## Slide 3: Background on Password Identifiers
Back in 2001, PSK authentication was designed under an assumption: one secret for the whole network.
  SAE inherited this unfortunate architectural design
  There is significant demand for supporting multiple secrets on a single SSID though.
  The technique used for supporting multiple credentials on a PSK network does not work on an SAE network (by design).
Password identifiers were added to SAE nearly a decade ago
  Password identifiers allow for a password to be either unique to a device or shared among devices and multiple passwords can be supported on a single SSID
  Password identifiers are passed in the clear during the SAE exchange

## Slide 4: What’s The Problem?
“Password Identifiers” have a privacy issue
  Since SAE Password Identifiers are passed in the clear, they potentially expose Personally Identifiable Information (PII), especially in the degenerate case where they are used like usernames– each device gets its own password/identifier pair
TGbi has an approved document describing requirements for the project: 11-21/1848r16 which includes:
  “11bi shall define a mechanism to prevent an evesdropper distinguishing whether authentication exchanges between CPE Clients and CPE AP use identical SAE credentials or distinct SAE credentials (where a CPE AP supports multiple SAE credentials).”
To satisfy the requirement, the group needs to come up with a solution that protects SAE password identifiers over the air

## Slide 5: OK, So What’s The Solution?
There is a proposal to address this problem and protect SAE password identifiers: 11-24/0046r3
  Unfortunately, a static group of members has consistently voted no on any attempt to address this requirement, including 11-24/0046
  Members of this group have refused repeated questions to explain their opposition or to suggest changes that could change their no votes to yes
  The members of this group were asked to provide an alternative mechanism that would address the requirements, but no alternative proposal was presented
The TG needs to address this issue and it has not been able to because of this voting group
Given the importance of preserving privacy and that ultimately the approval of P802.11bi rests with the WG, we believe the WG should consider this specific issue.
  This would allow TGbi to progress and meet its objectives.

## Slide 6: Proposed Motion
Instruct the TGbi editor to incorporate the changes indicated in 11-24/0046r3 into the TGbi draft
Motioned:
Seconded:
Y:
N:
A:

## Slide 7: References
https://mentor.ieee.org/802.11/dcn/21/11-21-1848-16-00bi-requirements-document.docx