## Slide 1: SMD Architecture
Date: 2024-11-04
Authors:

## Slide 2: Introduction
Several UHR presentations have covered seamless roaming improvements [1-8]
Two different variants of SMD (seamless mobility domain) roaming architecture have been proposed:
  SMD roaming with different MAC-SAP for each AP MLD of the SMD – roaming within AP MLDs of an SMD covering multiple non-collocated AP MLDs, where each AP MLD exposes its own MAC-SAP to the DS for SMD roaming.
  SMD roaming with a single MAC-SAP for the SMD – roaming within AP MLDs of an SMD covering multiple non-collocated AP MLDs, where a single MAC-SAP is exposed to the DS across all AP MLDs for SMD roaming.
In this presentation we propose a common SMD roaming framework that would support both variants of SMD roaming architecture

## Slide 3: SMD Architecture (1)
SMD defines a set of AP MLDs across which a non-AP MLD can perform seamless roaming
A logical SMD management entity (SMD-ME) provides single anchor point for management functions that include IEEE 802.1X authenticator, RSNA Key Mgmt and Association, across all AP MLDs of the SMD.
  SMD-ME is identified by an SMD MAC Address, which is also the 802.1X authenticator address (AA)
  PTKSA is generated between 802.1X Authenticator address (AA) and non-AP MLD MAC address (SPA)
Upper MAC functions at SMD-ME include authentication, association and management of security associations
  Split of other upper MAC functions between SMD-ME and AP MLDs is based on the SMD roaming variant/mode deployed
  AP MLDs interface with each other for context transfer (when needed)

## Slide 4: SMD Architecture (2)
Logical SMD-ME can be hosted on a centralized controller/WLC or on individual AP MLDs of the SMD
SMD-ME hosted on a WLC:
WLC provides the SMD level 802.1X authenticator and association functions for non-AP MLDs
Context related to a non-AP MLD is transferred between AP MLDs when SMD-ME is not exposing a single MAC-SAP
SMD-ME hosted on AP MLDs:
SMD level 802.1X authenticator and association functions for non-AP MLDs are hosted in a distributed manner on AP MLDs
Context related to a non-AP MLD is transferred between AP MLDs during seamless roaming

## Slide 5: SMD Architecture (3)
When a non-AP MLD authenticates and associates with an SMD-ME, a pair of 802.1X ports (U and C ports) are created by the 802.1X Authenticator for the non-AP MLD, through which authentication is done and connectivity to DS is controlled
SMD-ME can expose different MAC-SAPs (for each AP MLD of the SMD) or a single MAC-SAP (across all AP MLDs of SMD) to the DS for MSDUs exchange
  SMD-ME advertises the deployed mode (different MAC-SAPs vs same MAC-SAP). Non-AP MLD behavior depends on the mode - context transfer or context renegotiation can be initiated by non-AP MLD for the first case.
Case 1: SMD-ME exposes different MAC-SAPs to the DS for each AP MLD
  Access to DS via C-port is enabled only through MAC-SAP of one of the AP MLDs at a time
  During seamless roaming execution, 802.1X authenticator blocks UL to DS at the C-port until DS mapping change is initiated by target AP MLD, at which point UL to DS is reopened (at the C-port) through MAC-SAP of the target AP MLD
SMD-ME exposing different MAC-SAPs (logical view)

## Slide 6: SMD Architecture (4)
Case 1: SMD-ME hosted at each AP MLD when exposing different MAC-SAP to the DS
  During SR, after receiving roaming execution request, 802.1X authenticator of SMD-ME at current AP MLD blocks UL to DS at C-port
  After DS mapping change is initiated by the target AP MLD, 802.1X authenticator of SMD-ME at target AP MLD opens UL access to DS (at C-port) through MAC-SAP of the target AP MLD
  802.1X authenticator at current and target AP MLD is identified by same SMD MAC address
  The MAC-SAP of each AP MLD is identified by the AP MLD MAC address
  Such an architecture provides desired scalability for large deployments
SMD-ME exposing different MAC-SAPs (physical deployment)

## Slide 7: DS Mapping change for SMD roaming
Case 1: For SMD roaming, the SMD-ME entity on the target AP MLD should initiate DS mapping change, since non-AP MLD associates with SMD-ME. The DS SAP primitive can be enhanced to support this:
  Add a new APMLDMACAddress parameter that specifies the MLD MAC address of the AP MLD trough which the non-AP MLD specified by the STAAddress is now connected with in the SMD.
  DS-STA-NOTIFY.request(
STAAddress,
APMLDMACAddress,
UpdateType
)

## Slide 8: SMD Architecture (5)
Case 2: SMD-ME exposes a single MAC-SAP to the DS across all AP MLDs of the SMD
  SMD-ME is hosted at a centralized entity that exposes the single MAC-SAP
  The single MAC-SAP is identified by the SMD MAC Address
  The 802.1X authenticator (identified by SMD MAC Address) creates a pair of 802.1X ports for a non-AP MLD
  During SR between AP MLDs, no DS mapping change need to be initiated, since same MAC-SAP is used even after roaming
Note: When SMD-ME is exposing a single MAC-SAP to the DS, it can’t be hosted on individual AP MLDs – because multiple AP MLDs can’t expose same MAC address to DS

## Slide 9
SMD-ME
AP MLD1
MLD Lower MAC
AP11
PHY
MLD Lower MAC
AP12
PHY
MLD Upper MAC
AP MLD2
MLD Lower MAC
AP21
PHY
MLD Lower MAC
AP22
PHY
MLD Upper MAC
AP MLD3
MLD Lower MAC
AP31
PHY
MLD Lower MAC
AP32
PHY
MLD Upper MAC
SMD
SMD Upper MAC Part 1
SMD-ME
SMD Upper MAC Part 1
SMD-ME
SMD Upper MAC Part 1
MAC SAP
MAC SAP
MAC SAP
DS (Distribution System)
STA 1
Non-AP MLD
STA 2
1. Non-AP MLD is connected to DS through the links of AP MLD1.
Case 1: Example roaming with SMD-ME exposing different MAC-SAPs (1)

## Slide 10
SMD-ME
AP MLD1
MLD Lower MAC
AP11
PHY
MLD Lower MAC
AP12
PHY
MLD Upper MAC
AP MLD2
MLD Lower MAC
AP21
PHY
MLD Lower MAC
AP22
PHY
MLD Upper MAC
AP MLD3
MLD Lower MAC
AP31
PHY
MLD Lower MAC
AP32
PHY
MLD Upper MAC
SMD
SMD Upper MAC Part 1
SMD-ME
SMD Upper MAC Part 1
SMD-ME
SMD Upper MAC Part 1
MAC SAP
MAC SAP
MAC SAP
DS (Distribution System)
STA 1
Non-AP MLD
STA 2
2. Non-AP MLD is in roaming transition to AP MLD2. UL data to DS is paused from AP MLD1 during roaming transition. After DS mapping change is initiated by AP MLD 2, UL and DL data are enabled with AP MLD2
Case 1: Example roaming with SMD-ME exposing different MAC-SAPs (2)
Context transfer

## Slide 11
SMD-ME
AP MLD1
MLD Lower MAC
AP11
PHY
MLD Lower MAC
AP12
PHY
MLD Upper MAC
AP MLD2
MLD Lower MAC
AP21
PHY
MLD Lower MAC
AP22
PHY
MLD Upper MAC
AP MLD3
MLD Lower MAC
AP31
PHY
MLD Lower MAC
AP32
PHY
MLD Upper MAC
SMD
SMD Upper MAC Part 1
SMD-ME
SMD Upper MAC Part 1
SMD-ME
SMD Upper MAC Part 1
MAC SAP
MAC SAP
MAC SAP
DS (Distribution System)
STA 1
Non-AP MLD
STA 2
3. Non-AP MLD has completed roaming transition and is now connected to DS through the links of AP MLD2.
Case 1: Example roaming with SMD-ME exposing different MAC-SAPs (3)

## Slide 12: Case 2: Example roaming with SMD-ME exposing single MAC-SAP (1)
AP MLD1
MLD Lower MAC
AP11
PHY
MLD Lower MAC
AP12
PHY
AP MLD2
MLD Lower MAC
AP21
PHY
MLD Lower MAC
AP22
PHY
MLD Upper MAC
MLD Upper MAC
SMD
SMD Upper MAC Part 1
AP MLD3
MLD Lower MAC
AP31
PHY
MLD Lower MAC
AP32
PHY
MLD Upper MAC
SMD Upper MAC Part 1
SMD Upper MAC Part 1
SMD Upper MAC Part 2
SMD-ME
MAC SAP
MAC SAP
MAC SAP
MAC SAP
DS (Distribution System)
STA 1
Non-AP MLD
STA 2
1. Non-AP MLD is connected to DS through the links of AP MLD1.

## Slide 13: Case 2: Example roaming with SMD-ME exposing single MAC-SAP (2)
AP MLD1
MLD Lower MAC
AP11
PHY
MLD Lower MAC
AP12
PHY
AP MLD2
MLD Lower MAC
AP21
PHY
MLD Lower MAC
AP22
PHY
MLD Upper MAC
MLD Upper MAC
SMD
SMD Upper MAC Part 1
AP MLD3
MLD Lower MAC
AP31
PHY
MLD Lower MAC
AP32
PHY
MLD Upper MAC
SMD Upper MAC Part 1
SMD Upper MAC Part 1
SMD Upper MAC Part 2
SMD-ME
MAC SAP
MAC SAP
MAC SAP
MAC SAP
DS (Distribution System)
STA 1
Non-AP MLD
STA 2
2. Non-AP MLD is in roaming transition to AP MLD2. UL and DL are enabled through AP MLD1 and AP MLD2 during roaming transition.

## Slide 14: Case 2: Example roaming with SMD-ME exposing single MAC-SAP (3)
AP MLD1
MLD Lower MAC
AP11
PHY
MLD Lower MAC
AP12
PHY
AP MLD2
MLD Lower MAC
AP21
PHY
MLD Lower MAC
AP22
PHY
MLD Upper MAC
MLD Upper MAC
SMD
SMD Upper MAC Part 1
AP MLD3
MLD Lower MAC
AP31
PHY
MLD Lower MAC
AP32
PHY
MLD Upper MAC
SMD Upper MAC Part 1
SMD Upper MAC Part 1
SMD Upper MAC Part 2
SMD-ME
MAC SAP
MAC SAP
MAC SAP
MAC SAP
DS (Distribution System)
STA 1
Non-AP MLD
STA 2
3. Non-AP MLD has completed roaming and is connected to DS through the links of AP MLD2.

## Slide 15: Hierarchical SMD Architecture
In some deployments, there can be SMD with single MAC SAP deployed for smaller/targeted areas to provide improved reliability of connecting over links of multiple AP MLDs (e.g. in IIoT). Other areas may have AP MLDs deployed.
For such deployments, a higher level SMD (SMD-H) can provide seamless roaming across a lower level SMD with single MAC SAP (SMD-L) and other AP MLDs, leading to a hierarchical SMD deployment with SMD of (AP MLDs + lower level SMD(s) with single MAC SAP)
Here, PMKSA and PTKSA can be established at SMD-H level and used for SMD-L and other AP MLDs
Client would roam from an AP MLD in SMD-L to another AP MLD within SMD-H when moving out of the SMD-L area

## Slide 16: Conclusion
We covered a common SMD roaming framework that can support both variants of SMD roaming
  SMD roaming with different MAC-SAP exposed for each AP MLD of the SMD
  SMD roaming with a single MAC-SAP exposed across all AP MLDs of the SMD
SMD roaming with different MAC-SAPs for each AP MLD provides a scalable solution for seamless roaming for large-scale enterprise deployments
SMD roaming with a single MAC-SAP can be useful for seamless roaming in small-scale deployments to provide improved reliability by eliminating UL data pause
A hierarchical SMD architecture can enable SR in hybrid deployments of these two variants
To support seamless roaming for large scale enterprise deployments, 11bn must define an SMD roaming framework that supports different MAC-SAP for each AP MLD of the SMD

## Slide 17: SP1
Do you support to add following to 11bn SFD?
11bn defines a Seamless Mobility Domain (SMD, exact name TBD) that consists of multiple AP MLDs, where a non-AP MLD can use the UHR seamless roaming procedure to roam between the AP MLDs of the SMD?
A logical SMD Management Entity (SMD-ME, exact name TBD) provides association, IEEE 802.1X Authenticator and RSNA Key management for non-AP MLDs across all AP MLDs of the SMD.
A non-AP MLD transitions between AP MLDs within the SMD while maintaining its security association with the SMD-ME.
SMD-ME either exposes a single MAC-SAP to the DS across all AP MLDs of the SMD or exposes different MAC-SAP to the DS for each AP MLD of the SMD

## Slide 18: References
[1] 11-23-2157 “Seamless roaming within a mobility domain”
[2] 11-22/1910 “Seamless Roaming for UHR”
[3] 11-23/0170 “Smooth Roaming”
[4] 11-23/1131 “Thoughts on seamless roaming”
[5] 11-23-1416 “Seamless roaming follow up”
[6] 11-23-1996 “Improve roaming between MLDs”
[7] 11-23-0632 “smooth-roaming-follow-up”
[8] 11-24-0396 “Seamless roaming within a mobility domain – follow up”