## Slide 1: VLAN Segregated Data Services
Slide 1
Date: 2024-11-11
Authors:
Notes: doc.: IEEE 802.11-07/xxx2r0
July 2007
        Donald Eastlake 3rd, Motorola

## Slide 2: Abstract
Slide 2
802.11 networks frequently handle different communities that need to provide separate services. This is typically done by VLANs (802.1Q) in wired networks. The need varies from distinguishing between “visitors” and “residents” in a home network to much stronger and more complex requirements in enterprise, governmental, and other systems. This presentation provides scenarios and requirement areas for VLAN segregated data services in IEEE 802.11.
Notes: doc.: IEEE 802.11-07/xxx2r0
July 2007
        Donald Eastlake 3rd, Motorola

## Slide 3: Example Scenario Ia (unified infrastructure, single interface end stations)
MAP 1
Guest Station
MAP 2
AP 2
Guest Station
Local Station
Local Station
Internet
Local Station
Protected Services
Local Station
Local VLAN
Guest VLAN
Wired Connection
Firewall

## Slide 4: Example Scenario Ib (unified infrastructure, single interface end stations)
MAP 1
Infected Station
MAP 2
AP 2
New Station
Healthy Station
Healthy Station
Healthy Station
Healthy Station
Normal VLAN
Assessment and Remediation VLAN
Wired Connection
Other Services
End Point Assesment and Remediation

## Slide 5: Example Scenario II (diverse mesh, multi-interface mesh points)
Org 1 MP
Internet
Org 1 MP
Org 2 MP
Org 2 MP
Org 2 MP
Org 3 MP
Org 1 MP
Organization 1 Infrastructure
Org 1 MPP
Local Mesh Service
Organization 1 Service
Organization 2 Service
Organization 2 Infrastructure
Org 2 MPP

## Slide 6: Scenario II without segregated data services
Org 1 MP
Internet
Org 1 MP
Org 2 MP
Org 2 MP
Org 2 MP
Org 3 MP
Org 1 MP
Organization 1 Infrastructure
Org 1 MPP
Organization 1 Service
Organization 2 Service
Organization 2 Infrastructure
Org 2 MPP

## Slide 7: Areas
Slide 7
Work Done?
  Availability of Services
    In 802.11, “service” can be indicated by an SSID and multiple SSIDs can be advertised. See also GAS & PAD.
  Transit Frame Labelling (including GLK/Mesh)
    Just use VLAN ID in an 802.1 C-tag (formerly Q-tag).
New Work?
  Portal/Link/SSID Mapping to Services/VLAN/Priority
    Needs to be configurable
  Service Location & Multi-Service Connections
    Subscription service provider network (SSPN) interface relevance? Tunnelling a frame through nodes not fully trusted by the endpoints.
    Service location and mutli-service connections in mesh?
Notes: doc.: IEEE 802.11-07/xxx2r0
July 2007
        Donald Eastlake 3rd, Motorola

## Slide 8: Availability of Services
Slide 8
Some Things Already Standardized:
  Multiple SSIDs can be advertised by an AP.
  Generic Advertisement Service (GAS) mechanisms and Pre-Association Discovery (PAD) are relevant. See Annex R of 802.11-2020.
Notes: doc.: IEEE 802.11-07/xxx2r0
July 2007
        Donald Eastlake 3rd, Motorola

## Slide 9: Transit Frame Labelling
Slide 9
Current Practice:
  Base 802.11 standard permits 802.1 C-Tag (VLAN, formerly Q-Tag) in payloads. See Annex M of 802.11-2020.
Notes: doc.: IEEE 802.11-07/xxx2r0
July 2007
        Donald Eastlake 3rd, Motorola

## Slide 10: Portal/Link/SSID Mapping to Services/VLAN/Priority
Slide 10
Possible work:
  VLAN IDs should be coordinated across ESSes so that an SSID or set of SSIDs map to a VLAN and might map priority.
  Should portals (or mesh gates) have a configurable mapping between external VLAN/priority and 802.11 TID?
Notes: doc.: IEEE 802.11-07/xxx2r0
July 2007
        Donald Eastlake 3rd, Motorola

## Slide 11: Service Location & Multi-Service Connections
Slide 11
Possible new work:
  Could a STA associated with an AP use multiple VLANs for different services?
    Existing provisions in the standard mostly have to do with VLANs between an AP and other interworked networks rather than between a AP and a STA.
  How does a mesh station (which might have just joined the mesh) find a new service that was not previously transiting the mesh but is offered by some other station/portal?
Notes: doc.: IEEE 802.11-07/xxx2r0
July 2007
        Donald Eastlake 3rd, Motorola
Page 11

## Slide 12: Results in At January 2008 Interim
Slide 12
11-07/2941r2 Presented In WNG Standing Committee
Results As reported in 11-08/114r0:
Vote in WNG
  Moved, To request the IEEE 802.11 Working Group to approve and forward to the IEEE 802 Executive Committee the creation of a “WLAN Segregated Data Services” Study Group to consider how best to meet requirements as follows and how best to coordinate such activities with 802.1:
    labeling frames per service; security of data within a service; and the configuration and management of such services.
  Moved: Donald Eastlake 3rd Seconded: Guido Hiertz
  Yes: 22 No: 0 Abstain: 4 (100% approval)
Vote In 802.11 Working Group at Closing Plenary
  Yes: 19 No: 9 Abstain: 24 (67.85% approval)
Notes: doc.: IEEE 802.11-07/xxx2r0
July 2007
        Donald Eastlake 3rd, Motorola
Page 12

## Slide 13: Possible Motion
Slide 13
Moved, To request the IEEE 802.11 Working Group to approve and forward to the IEEE 802 Executive Committee the creation of a “VLAN Segregated Data Services for WLAN” Study Group to consider how best to meet requirements as follows and how best to coordinate such activities with 802.1:
    VLAN labeling frames per service within a WLAN; security of data within a service; and the configuration and management of such services.
  Moved: Seconded:
  Yes: No: Abstain:
Notes: doc.: IEEE 802.11-07/xxx2r0
July 2007
        Donald Eastlake 3rd, Motorola
Page 13

## Slide 14: Straw Poll
Slide 14
Do you favor the formation of a Study Group to explore additional uses of and management of VLANs inside WLANs?
  Yes
  No
  Abstain
Notes: doc.: IEEE 802.11-07/xxx2r0
July 2007
        Donald Eastlake 3rd, Motorola
Page 14

## Slide 15: References
Slide 15
IEEE Standard 802.11-2020 – WLANs
IEEE Standard 802.1Q-2018 – VLANs
Notes: doc.: IEEE 802.11-07/xxx2r0
July 2007
        Donald Eastlake 3rd, Motorola